## Slide 1: CIS101B
Computer Operating Systems

## Slide 2: Professionalism
Professional Tech:
Appearance: dressing down professionalism
Dressing casual gives the false impression of being casual; not being taken too seriously
Perception of laziness or not caring about self worth
Dressing more professional gives the impression that you are serious at what you do
That you care about yourself enough to project

## Slide 3: Professionalism
Traits of a Tech:
Honesty / Integrity
Honesty means to tell the truth
Integrity means to do the right thing
Dependability / Responsibility
Dependable people perform agreed-upon actions
Responsible people is answerable to their own actions
Sensitivity
Ability to appreciate another’s feelings and emotions
Acting in a way to make others comfortable

## Slide 4: Professionalism
Effective Communication:
Assertive Communication
Two parts to assertive communication
  Understanding and appreciation of the importance of their feelings
  Ability to state the issues clearly without accusing the user directly
Respectful Communication
Ask if you may start working on the issue; do not assume you can just start
Actively listen do not interrupt a client when they are explaining the issue
Maintain a positive attitude; do not get defensive
Avoid Distractions that take your focus away from the client

## Slide 5: Professionalism
Getting Answers:
Avoid accusations: What did you do this time!?
Keep questions friendly and factual
Avoid jargon, acronyms and slang; even if they use it
Expectations and Follow up:
Always give customers realistic expectations concerning time and outcomes
Try and follow up later to ensure that the work completed is still functioning

## Slide 6: Safety
Be Prepared!
Electrostatic Discharge (ESD):
Passage of a static field electrical charge from one item to another
Will destroy the sensitive parts of any computing device
Antistatic Tools:
ESD Strap: Wrist or Heel
ESD Mat: Desk or Floor
ESD Carpet
ESD Clothing
ESD Bag

## Slide 7: Safety
Interference:
Electromagnetic: Magnetic fields interfere with electronics
Radio Frequency: Will not damage, but it is annoying
Physical Tools:
Phillips screwdriver
Torx Wrench
Parts retriever
Multimeter
Power supply tester

## Slide 8: Safety
Personal Safety:
Avoid tripping hazards
Lifting heavy boxes; lifting belt, lift with legs
Careful around hot components
Remove jewelry, tie up loose fiting shirts and long hair
Troubleshooting:
Identify the problem
Establish a theory of probable cause
Test the theory to determine cause
Establish a plan of action to resolve the problem and implement the solution
Verify full system functionality and implement preventive measures
Document findings, actions and outcomes

## Slide 9: Computing Software
OS Functions and Computer Interfaces
Communicates with the hardware of the PC or device
Creates a user interface: visual representation of the computer
Enables users to determine what functions on the computer to perform and when to stop using them
Enables the user to add, move or delete tools and applications
Provides methods to secure the system from threats

## Slide 10: Computing Software
User Interfaces:
Graphical User Interface: GUI
Command Line Interface: CLI
macOS:
Dock: Similar to taskbar in Windows; pin commonly used apps
Spaces: multiple desktops; different customizable screens on one Desktop
Linux:
Distributions (distros): different versions of Linux; all with their own features
Desktop environments (DEs): similar in function to Windows and macOS

## Slide 11: Computing Software
File Structure and Paths:
Root Directory: where the OS is installed
Windows Explorer (Win 7) / File Explorer (8.1/10): access files and folders
Finder (macOS): access files and folders
File extension: tells OS which app to use with this file
Folders:
C:\Program Files (All Versions): default location for OS apps
C:\Program Files (x86): location of 32-bit apps in a 64-bit OS
Personal documents:
C:\Users\username\Desktop C:\Users\username\Documents
C:\Users\username\Downloads C:\Users\username\Music
C:\Users\username\Pictures C:\Users\username\Videos

## Slide 12: Computing Software
Control Panel: Handles most of the maintenance, upgrade, and configuration aspects of Windows; populated by applets
System Tools: access to commonly used tools like System Information and Disk Defragmenter
Administrative Tools: enables you to set up hard drives, manage devices, test system performance, ect
macOS:
System Preference: access to all settings you will need to administer a macOS system
Utilities folder: (in Applications folder): provides services beyond system preference like activity monitor and terminal
Linux:
GNOME 3: “All Settings” application
KDE Plasma Desktop: kickoff menu (start menu)

## Slide 13: Power Supplies
Equipment Grounding and Surge Suppression
Do not assume that a convient three-prong outlet has proper grounding
Handling spikes and sags to limit or prevent damage to devices
Surge Suppressor: Surge is an increase in voltage that lasts seconds; can eventually destroy parts. Suppressor aborbs extra voltage from reaching the PC
Surge suppressors are rated in joules: the higher the joule rating, the more it can absorb (minimum 2000 joules)
Uninterruptable Power Supply (UPS): protects your PC and data in the event of a power sag, power outage or power spike
Measure in Watts (true amt of power they supply) and volt-amps (VA); power the UPS could supply if the device took power in a perfect way
Every UPS has surge and spike protection and power line conditioning

## Slide 14: Implementing Mass Storage
Hard Drive Partitions / Formatting
First sector of an MBR HDD contains the Master Boot Record; informs the system about the installed OS. Where the BIOS looks to see if the drive is bootable
MBR contains the partition table; describes the number and sizes of each partition. MBR can only hold 4 paritions
  Primary Partition: loads the OS on that partition
  Extended Partition: not bootable, but can hold data
  Active Partition: code built into Primary partitions; decides which Primary Partition to boot to if more than one OS is installed (Dual/Multi – Boot)

## Slide 15: Implementing Mass Storage
Dynamic Disks:
Create up to 128 volumes; not limited to four partitions
Implement RAID, span volumes over multiple drives, extend volumes on one or more drives
  Simple volume: works like primary partitions
  Spanned volume: use unallocated space on multiple drives to create a single volume
  Striped volume: RAID 0
  Mirrored volume: RAID 1
  RAID 5 volume

## Slide 16: Implementing Mass Storage
GUID Partition Table (GPT)
GPT removes the limits of MBR partitioning
128 Partitions (Microsoft limit)
Hold 9.6ZB (ZettaBytes – 1 Billion TerraBytes)
GPT partitions are stored in a secure database hidden instead of a MBR
Only be implemented on a UEFI system
When to Partition?
Typically when an OS is being installed; FDISK or Disk Management are common tools to partition a drive

## Slide 17: Implementing Mass Storage
Hard Drive Formatting:
Once a drive is partitioned, it needs to be formatted to make the partitioned space usable by the OS
Formatting process implements OS file system (NTFS, EXT4, AFS) and assigns a volume letter (C: is default for Windows) – FAT32 is common to all platforms but lacks security and has file and capacity limits
FAT32: 32-bit OS; limited to 2TB partitions; 4GB single file size; 268M files
NTFS: 64-bit OS; limited to 16EB partitions; 16TB single file size; 4B files; security; compatible to FAT32
HFS/AFS: 64-Bit OS; compatible to FAT32 and exFAT; only read NTFS
EXT4: 64-bit OS; limited to 16EB partitions; 16TG single file size; 4B files; security; journaling; compatible to FAT32

## Slide 18: Implementing Mass Storage
Disk Initialization:
Foreign drive: move a dynamic disk from one PC to another
Formatting: you are formatting a drive
Failed: Disk is damaged or corrupt; data most likely has been lost
Online: Healthy and communicating properly with the PC
Offline: Drive is either corrupt or having communication issues
Mount Point:
Drive volumes can be assigned to folders; allows you to use existing folders to store more data than you can fit on a single drive or partition

## Slide 19: Implementing Mass Storage
Maintaining and Troubleshooting Hard Drives
Maintenance:
Error Checking: chkdsk (windows), fsck (linux): will check and potentially fix errors and bad sectors found on drives
Errors: lost sectors, missing files, cross-linked files ect
Apple: Reboot and press Apple Key + R until recovery partition loads
Defragmentation (HDD only!):
Reorganizes data stored on platter HDD; optimizes read times by storing files linear instead of scattershot
Disk Cleanup:
Scans drives for unneeded files and deletes them permanently.
Recycle Bin, Temp files, Temp Internet files, Download programs

## Slide 20: Building A PC
Installing and Upgrading Windows
Media sources: Optical (phasing out); USB storage; Network connection
Types of Installation:
Clean Install: Old data is erased and replaced with fresh new OS
Upgrade install: Requires qualifying version of OS preinstalled, then new OS replaces old OS files; user data left alone
Multi-Boot Install: Create a separate Partition for up to 4 Oss on a standard MBR drive; with each OS being installed on its own partition. Boot menu will then prompt user to choose which Primary partition to make primary
Network Install: Using a WDS (windows distribution server) and PXE (Pre-Execution Environment) on the clients, the clients will boot into the WDS and have Windows installed

## Slide 21: Building A PC
Installing macOS over a network: NetBoot is Apple’s tools for network install and imaging
Troubleshooting Install Problems:
Media errors: corrupt USB, no network, scratched DVD
RAID Array not Detected: Driver not installed prior to Windows installation
No Boot Device present: Non-bootable USB installed, No Disk present, No network or WDS found

## Slide 22: Building A PC
Post Installation Tasks
Patches, Service packs, and Updates
Upgrading drivers
Restoring User data (if applicable)
Install Essential Software: Client approved applications
Migrating and retiring Systems
  User State Migration Tool (USMT): backup and restore Active Directory
  Windows Easy Transfer: User data and personalization quickly
Data Destruction: Destroy or Sanitize
Drill Holes or crush the drive to destroy; Low level format to sanitize

## Slide 23: CIS101B Week One
END of Week One