## Slide 1: CIS101A Week Two
Computer Hardware fundamentals
Comptia 1001

## Slide 2: DRAM STICKS
Bus Width started with 4 to 16 bits wide; now it is 64 bits wide
Optimize the flow of data in and out of the CPU utilizing an MCC (Memory Controller Chip)
Requests for certain data from memory are done on the address bus

## Slide 3: Types Of RAM: SDRAM | RDRAM
Synchronous DRAM (SDRAM): standard memory tied to system clock
1996: dual inline memory module were released (DIMM)
micro-DIMM |SO-DIMM |Uni-DIMM
68- 144- 172- 72- 144- 200- 200- pins
Rambus DRAM (RDRAM): up to 800Mhz ; stopped due to production and cost
Serial inline memory: needed to be terminated
RIMM: Stick of RDRAM

## Slide 4: DDR SDRAM
Double Data Rate SDRAM [DDR]: replaced RDRAM
Two 64 bit processes for every clock cycle with 1 command [read | write]
100-200Mz front side bus
184 pin module | 2.5V
DDR rating: Bus speed * 2  Clock speed 100Mhz = DDR200 stick
PC rating (Bandwidth): DDR rating * 8 (in MB/sec)  DDR200 = PC1600
Double Data Rate 2 [DDR2]
Four 64 bit processes for every clock cycle with 1 command [read | write]
200-533Mhz front side bus
240 pin module | 1.8V

## Slide 5: DDR SDRAM
Double Data Rate 3 [DDR3]
Eight 64 bit processes for every clock cycle with 1 command [read | write]
400-1000Mhz front side bus | 128GB / stick limit
240 pin (re-notched) | 1.5V (1.3V DDR3L)
Extreme Memory Profile (XMP): Allows overclocking
Supports Triple | Quad channel architecture
Double Data Rate 4 [DDR4]
Eight 64 bit processes for every clock cycle with 1 command [read | write]
1066-2133MHz front side bus | 512GB / stick limit
288 pin (260 pin Uni-DiMM) | 1.2V (1.05V DDR4L)
Measured in MegaTransfers (MT) per sec
Supports Triple | Quad channel architecture

## Slide 6: Variations Latency | Parity * ECC
Classes of RAM will come with different packaging, speed, quality
Latency: Delay when memory controller fetches
CAS Latency: column address strobe
CL: clock cycle delay
Parity RAM: stores extra bit of data that MCC uses to verify the data
Find an error, but not correct it
Error Correcting Code RAM [ECC]: Detect and correct errors. Slower than non-ECC and used for servers

## Slide 7: Working with RAM: Virtual Memory
Portion of the hard drive can be used as virtual storage for RAM
Saved as a “page file” or “swap file”
Apps can be stored on HDD when RAM is filled
Best results, make the min and max page file size equal
Disk Thrashing: programs are rushed by the OS between RAM the HDD and RAM again
32-bit Windows: 2GB to get by; 4GB recommended
64-bit Windows: 4GB to get by; 8GB for good performance; 16+GB Gaming

## Slide 8: Getting the Right RAM / Mix Speeds
Motherboard documentation must be consulted to determine what RAM to get and how many
Tell you the max allowed per stick limit and whether memory can be channeled
Mix Speeds is NOT recommended
Best case, your memory all runs slower
Worst case, your system locks up and crashes
Mixing capacities at the same speed is perfectly fine

## Slide 9: Installing DIMM | SO-DIMM
Follow ESD Pre-cautions
Side connectors on both sides of the slot should be pushed down
Do not touch gold conductors or chips on RAM
[DIMM] Line up notch on slot with groove on RAM stick and push down on both ends with equal force. End connectors should push up to lock in place
[SO-DIMM] Insert at 45° angle with the connector and push down to lock in place
Serial Presence Detect (SPD) chip stores all data involving the memory and is queried by the BIOS

## Slide 10: Troubleshooting RAM
Memory Errors: Page Fault
Mild error that can be caused by non memory devices.
Typically get address of the error (write it down)
Memory Errors: Non Maskable Interrupt
Error severe enough to interrupt the CPU enough that it cannot ignore it
Proprietary crash screen (BSoD or SPoD)
While it may be caused by faulty RAM, mostly caused by bad code
Memory Errors: Intermittent Errors:
Power Supply issues | ESD Damage |
Attempt the “replace and pray” method to recover

## Slide 11: BIOS | ROM
Basic Input Output System: Enables CPU to talk to hardware
Stored on Motherboard on EEPROM or FLASH Memory chips
ROM: Read Only Memory
Non-Volatile (Keeps data with power removed)
EEPROM: Electrically Erasable – Flash ROM
System BIOS collectively stores code for each piece of supported hardware
Up to 1MB of Storage and support for 2TB or less HDD

## Slide 12: UEFI
Unified Extensible Firmware Interface 64-bit Firmware
Supports Drives 2.2TB or larger
Handles all boot loading devices
Legacy support for BIOS
Secure Boot for Windows platform
GUI driven
Flash Memory storage

## Slide 13: CMOS and RTC
Complementary Metal Oxide Semiconductor
Stores BIOS Settings | Requires 3V CMOS battery
Utilizes a System Setup Utility to modify data | EZ mode and Advanced Mode
Real Time Clock
Manages Date and Time of the system
IRQ0: highest Interrupt
CMOS battery failure will cause RTC to fail

## Slide 14: BIOS Security Settings
Admin Password: Blocks changes to BIOS settings
User Password: Blocks access to OS
HDD Password: Blocks access to HDD
Chassis Intrusion: requires a compatible case. If enabled, BIOS alert that the case was compromised (Time and Date stamped)
LoJack: Track stolen equipment
TPM: Trusted Platform Module: Chip that allows encryption of files and drives through random number generation

## Slide 15: Power On Self Test: POST
Program stored in ROM that checks all the whole system every time it boots or reboots
2 – 4 digit Hexadecimal Code that each device is programmed with. Motherboard manual can correlate the Hex codes with a particular device
Built into Motherboard or added as Expansion card
Errors have three categories:
Audible: from speaker: Beep codes – Translated using Motherboard book
Numerical: From POST Card itself – translate codes from Motherboard book
Visual: Text errors (No OS Detected; Keyboard error, Push F1 to continue)

## Slide 16: Default | Optimized Settings
Reset Options: Load Default and OS Optimized Defaults
Default is factory set to simple settings mostly likely not to cause conflict
OS Optimized is best possible speed/stability

## Slide 17: Clearing CMOS RTC RAM
Almost every motherboard has a set of wires or connectors that will clear RTC (CLRTC)
Turn off PC, Remove case
Find CMOS RTC Clear wires or connectors (consult motherboard book)
Move wires to the CLR setting for 10 seconds, then replace back to original setting
If your board does not have the CLRTC feature, try removing the 3V battery for 10 seconds and place it back

## Slide 18: Losing CMOS RTC Settings
CMOS settings require a 3V power source (Lithium battery or 2 AAA)
If the battery dies, your RTC settings can clear including date and system time
Some of the error messages you may get are:
CMOS config mismatch
CMOS date/time not set
BIOS time and settings reset
No boot device available
CMOS battery state is low
Replace the battery if you see these error messages

## Slide 19: Flashing the ROM
Firmware Update:
Requires a bootloader software that will take the update file and copy it to the Flash BIOS
Designed to allow functionality and feature updates to the motherboard
Backup your current BIOS prior to any updating
Only update IF you have the need to do so. If it is not broke, so not fix it

## Slide 20: End of Part 1

## Slide 21: Magnetic HDD | Spindle Speed
Traditional hard disk drive is composed of platters with r/w heads on an actuator arm
Aluminum platters coated in ferrite to store data magnetically
HDD run at a spindle speed of 5400, 7200, 10,000 and 15,000 RPM
Faster drives give better performance but at the cost of noise and heat
Drive bay fans can help with heating issues
Form Factor: 2.5” or 3.5” are common for HDD

## Slide 22: Solid State Drives [SSD]
Use Flash memory chips for storage; no moving parts
Low power and cool
2.5” form factor for drives; mSATA and M.2 for motherboards that can support PCIe NVMe memory
SSD controller dictates the writing of data based on scattershot
Low latency built in; no motor to spin up
NVMe can do 2500MBps sequential read and write

## Slide 23: Connecting Mass Storage
Standardized physical interfaces: ISA | PATA | SATA | SAS | M.2
CPU needs standard protocols (ATA) / (ATAPI)
PATA (Parallel Advanced Technology Attachment)
40 pin ribbon cable (Master/slave) / 4 pin Molex power (+12, gnd gnd, +5)
(also called an IDE cable)
Implemented S.M.A.R.T with V3 of ATA for HDD
SATA (Serial Advanced Technology Attachment)
Utilizes a host bus adapter (HBA)
Uses a 7 pin serial data cable and a 15 pin power cable
SATA Cable (1m Internal , 2m External)
SATA is 1.5Gbps | SATA2 is 3Gbps | SATA3 is 6Gbps
SATA Express is 2000MBps | eSATA is just external SATA

## Slide 24: Refining Mass Storage Communication
AHCI: Advanced Host Controller Interface
Allows for HBA control of SATA
Native Command Queuing (NCQ): disk optimization for SATA drives
When AHCI is enabled, SATA drives are hot swappable
NVMe: Non-Volatile Memory Express
Supports communication between the OS and SSD directly through a PCIe lane
Offered as an expansion card or M.2 connector

## Slide 25: R.A.I.D
Redundant Array of Independent Discs
Through multiple drives: Adds Performance, Fault Tolerance, or Both
Industry tends to focus on RAID Level 5
Can be implemented as Hardware or Software RAID
Hardware would be a dedicated RAID controller on the MB or expansion card | Software would be the OS (Win10) managing your drives with CPU as RAID Controller

## Slide 26: RAID Levels
RAID 0 – Disk Striping: Requires 2 drives; no redundancy. Provides performance through parallel reading. No overhead.
RAID 1 – Mirroring: Requires 2 drives; redundant. No performance increase. 50% overhead since the same data is written to both drives at once
RAID 5 – Disk Striping with Extra Parity: Distributes data and parity information across all drives evenly. Requires at least 3 drives, but more is preferred. Overhead changes based on drives utilized (1/n)*100%; n = # of drives.
RAID 10 – Nested, Striped Mirrors: Requires a minimum of 4 drives. Provides performance and fault tolerance since it is a stripe and mirror. 50% overhead.

## Slide 27: Installing Drives
Choosing your drive:
M.2, SSD or HDD
M.2 plugs into Motherboard directly
SSD / HDD SATA connector via 7 pin and 15 pin cables
(If PATA, set drive to master / slave via jumper or CS, connect by ribbon cable and molex connector)

## Slide 28: BIOS Support
BIOS or UEFI; either controls how hardware will be configured
Make sure all the controllers you need are enabled in the BIOS / UEFI
If you have RAID support, either enable or disable if planning to use RAID or not
Most settings in BIOS / UEFI will be set to autodetection; versus manually setting all the variables yourself (even overclocking can be auto)
Drive Boot Order will give the option of what device to scan first in the SATA chain or USB.
AHCI: IDE/SATA; AHCI or RAID – IDE mode is for old OS like 98/XP

## Slide 29: Troubleshooting HDD
Auto detection is your best friend when it comes to troubleshooting HDD install issues; it is there or it is not
Most issues relate to the cables (data and power) or lack there of
Other issues stem from settings being disabled in the BIOS/UEFI

## Slide 30: Troubleshooting HDD Implementation
Install Errors, Data Corruption, Dying Hard Drives and RAID issues
Install errors: Connectivity, system setup, partitioning, and formatting
Partition errors: Fail to partition, or wrong partition size or type
(fixed in Disk Management)
Formatting errors: Drive not formatted or formatted with incorrect file system. Drive could also have bed sectors
Data corruption errors: power surges, incorrect shutdowns, viruses
(CheckDisk can fix most of these errors)
Dying HDD: Physical damage or wear and tear (starts with clicking sounds)

## Slide 31: Common Ports
Serial Ports: DB-9 (RS232/RS485) – Communication ports: 115kBps
USB Ports: Host Controller and Hub: dictate USB type and speed
USB Standards:
Hubs can be Passive or Active (powered by host or wall outlet)
Low power is 100mA, 2.0 is 500mA, 3.0 is 900mA of current
Name | Standard / Port Color | Max Speed / Cable Length | Common Usage
Low Speed | 1.1 -- White | 1.5Mbps -- 3m | Keyboard/Mouse
Full Speed | 1.1 -- White | 12Mbps -- 5m | Headphones/Blue-tooth devices
Hi-Speed | 2.0 -- Black | 480Mbps -- 5m | Webcams/Card Scanners
SuperSpeed | 3.0 -- Blue | Up to 5Gbps - 3m | Flash drives/ External Storage
SuperSpeed+ | 3.1 -- Teal | Up to 10Gbps 5m | Flash Drives/ External Storage/Networking

## Slide 32: FireWire | Thunderbolt Ports
IEEE1394: Apple – Firewire / Sony – iLink / Texas Instruments – Lynx
IEEE1394a standard: Up to 400Mbps, 4.5m cable, 4 pin passive / 6 pin active
IEEE1394b standard: Up to 3200Mbps, 100m cable, 4 pin passive / 9 pin active, uses 1394.3 standard for peer to peer connecting
Thunderbolt: PCIe technology. Thunderport 1 and 2 utilize mini Display Port (mDP) / Thunderbolt 3 uses USB C connector
Copper Thunderbolt goes to 3m / Fiber Thunderbolt goes 60m
Thunderbolt 1 = 10Gbps / 2 = 20Gbps / 3 = 40Gbps

## Slide 33: Common Peripherals
Keyboard / Pointing Devices / Biometric / KVM ect
Keyboards: IRQ1 Device, mostly USB [legacy PS/2 – Din6]
Need cleaning maintenance somewhat regularly
Pointing Devices: Mouse is the most common, mostly USB [legacy PS/2 – Din6]
Touchpad, Trackball, nub, styllus are all variants
BioMetric: Scans and holds physical data and characteristics
KVM (Keyboard, Video, Mouse): Share 1 monitor, keyboard and mouse with multiple machines

## Slide 34: Storage Devices
Removeable Media: Ability to replace full media with blank and continue to save
USB Storage
Tape Drive
Optical Media

## Slide 35: Flash Memory
USB Storage: Thumb drives , Compact Flash , Secure Digital
Card Readers: 4 in 1 / 6 in 1 format readers

## Slide 36: Optical Media
CD/DVD/BD: Laser Medium (Red / Blue)
ROM: Store bought: Pressed disk
-R: Writable Media (once)
-RW (CD/DVD): Rewriteable
-RE (BD): Erasable
Transfer Rate:
CD: 150kBps at 1X | DVD: 1.35MBps | BD: 4.5MBps
Capacity:
CD: 700MB | DVD-5 (4.37GB) | DVD-9 (7.95GB) | DVD-10 (8.74GB) | DVD-18 (15.9GB) |
BD-SL (25GB) | BD-DL (50GB) | BD-TL (100GB) | BD-QL (133GB)