## Slide 1: Week Four CIS101A
COMPUTER HARDWARE FUNDAMENTALS

## Slide 2: BENEFITS OF VIRTUALIZATION
POWER SAVING, HARDWARE CONSOLIDATION, SYSTEM MANAGEMENT AND RESEARCH
POWER SAVINGS COMES FROM HAVING MULTIPLE OS's STORED ON ONE PHYSICAL MACHINE VS HAVING A SEPARATE MACHINE FOR EACH OS
HARDWARE CONSOLIDATION: PLACE MULTIPLE SERVERS AND CLIENTS INTO A SINGLE MACHINE; JUST BUILD A ROBUST MAIN SYSTEM
SYSTEM MANAGEMENT & SECURITY: VM's CAN BE COPIED; IF A SYSTEM FAILS, JUST COPY THE VM BACK TO THE SYSTEM AND EVERYTHING IS RESTORED QUICKLY; CAN ALSO BE SNAPSHOT OR CHECKPOINT
RESEARCH: COMDUCT TESTS ON MULTIPLE PLATFORMS FROM ONE DEVICE

## Slide 3: IMPLEMENTING VIRTUALIZATION
WHETHER VMWARE, HYPER-V OR XEN; EACH HAS ITS OWN METHODS OF SETTING UP AND MANAGEING HARDWARE
HYPERVISOR: MANAGES ALL VIRTUAL ENVIRONMENTS FROM A SINGLE HOST PLATFORM. RESPONSIBLE FOR RAM, CPU AND HDD ALLOCATION
EMULATION VERSUS VIRTUALIZATION: EMULATOR WILL CONVERT COMMANDS FROM A HOST PLATOFRM INTO ANOTHER PLATFORM; VIRTUALIZATION WOULD PUT BOTH PLATFORMS ON ONE MACHINE AS NATIVE

## Slide 4: CLIENT-SIDE VIRTUALIZATION
SET-UP SYSTEM HARDWARE TO SUPPORT VIRTUAL MACHINE(S) AND VERIFY IT MEETS RESOURCE REQUIREMENTS
INSTALL A HYPERVISOR ON THE SYSTEM
CREATE A VIRTUAL MACHINE THAT MEETS ALL NECESSARY HARDWARE REQUIREMENTS
START THE NEW VIRTUAL MACHINE AND INSTALL THE GUEST OS ON THE PLATOFRM
REQUIREMENTS: RAM IS THE MOST NEEDED! NEED RAM NOT ONLY FOR THE HOST MACHINE, BUT ENOUGH MEMORY TO SECURELY RUN EACH OTHER PLANNED OS
HDD SPACE: VM FILES CAN BE HUGE. ENOUGH DRIVE SPACE FOR YOUR HOST OS TO RUN PLUS ENOUGH DRIVE SPACE FOR EACH OTHER OS INSTALELD

## Slide 5: CLIENT-SIDE VIRTUALIZATION
NETWORK: INTERNAL, BRIDGED, VIRTUAL SWITCHES, OR NO NETWORK AT ALL
INTERNAL NETWORK: NO CONNECTION TO AN EXTERNAL PHYSICAL NETWORK. ONLY VM's CONNECTED TO THE SAME VM HOST SERVER WILL BE NETWORKED. PRIVATE INTERNAL NETWORK IS FURTHER ISOLATED FROM INTERNAL NETWORK VM DEVICES
BRIDGED NETWORKING: ALLOWS A VM INTERNAL NETWORK TO CONNECT TO A PHYSICAL NETWORK FOR USE OF THE INTERNET. THE BRIDGE ROUTES VM NETWORKED TRAFFIC THROUGH A DEFAULT GATEWAY
VIRTUAL SWITCH: HYPERVISOR ALLOWS FOR THE CREATION OF ALL NETWORK EQUIPMENT IN A VM. A VIRTUAL ROUTER, SWITCH, BRIDGE WILL PERFORM THE JOBS SIMILAR TO THEIR PHYSICAL COUNTERPARTS
NO NETWORK: SELF EXPLANITORY. THERE IS NO NETWORK; JUST VMs

## Slide 6: SERVER-SIDE VIRTUALIZATION
INSTALL JUST THE HYPERVISOR WITH NO GUEST OS "BARE-METAL" HYPERVISOR
  CONSIDERED A TYPE-1 HYPERVISOR
  TYPE-2 HYPERVISOR WOULD BE VMware OR HYPER-V
ALSO RUN ON THE CLOUD; SINCE VM's ARE JUST FILES. IaaS CAN RUN VM's FROM THE CLOUD SO YOU DO NOT HAVE TO OWN THE HARDWARE

## Slide 7: THE SERVICE-LAYER CAKE
Cloud services can be offered as Infrastructure, Platform and Software as a Service: IaaS, PaaS and SaaS
IaaS: hardware requirements: Servers, storage, datacenters, network, computers, mainframes. Physical devices can be leased
PaaS: Tools developers (web) need to deploy, administer, and maintain a Web application. Acts as a service for developers to run their tasks without hardware concerns
SaaS: Web applications offered as a try before you buy service. Always up to date so the end user would not need to worry about having the latest software

## Slide 8: OWNERSHIP AND ACCESS
There are four cloud service types: Public, Private, Community and Hybrid
Public Cloud: for the general public. Public offerings of IaaS, PaaS or SaaS; users typically associate their storage as public
Private Cloud: Meant for single organizations. Cloud a business would own outright. Managed by 3rd party, the business focuses on their data and its security while enjoying the flexibility of the cloud. Doctor office would be an example
Community Cloud: Multiple similar organizations consolidate to pay for cloud services. Like a private cloud, community clouds are managed by 3rd parties, are encrypted, and the companies own their data. Hospitals and college campuses are examples.
Hybrid Cloud: combination of public, private and community clouds under one umbrella.

## Slide 9: WHY CLOUD?
VIRTUALIZATION, SHARED RESOURCES, RAPID ELASTICITY, ON-DEMAND, RESOURCE POOLING. MEASURED AND METERED SERVICE, CLOUD-BASED APPLICATIONS, CLOUD-BASED VIRTUAL DESKTOPS, CLOUD FILE STORAGE SERVICES
RAPID ELASTICITY: ALLOWS FOR SCALABLILITY OF YOUR SERVICE(S). NEED GROWTH? DONE! DOWNSIZING? DONE!
ON-DEMAND: ALLOCATION OF RESOURCES LIKE BANDWIDTH WHEN THE NEED(S) ARISE
MEASURED SERVICE: PAY AS USED
METERED SERVICE: PAY FOR TIME OR RESOURCE BANDWIDTH
CLOUD-BASED APPS: OFFICE365 AS AN EXAMPLE
CLOUD-FILE STORAGE SERVICES: DROPBOX, ONEDRIVE, ICLOUD

## Slide 10: PORTABLE DEVICES
TYPICALLY VIEWED AS A NOTEBOOK OR A LAPTOP; EITHER IS MEANT AS A REPLACEMENT FOR A DESKTOP PC
GAMING, NETBOOKS (CHROMEBOOK), 2-IN-1s, CONVERTIBLES (ROTATING SCREENS)

## Slide 11: PORTABLE INPUT DEVICES
Smaller form factor QWERTY keyboard (88 keys instead of 105)
  Uses a Fn key to add functionality to sets of keys (F1 – F12)
  No separate numpad to conserve space
Pointing devices: track-point (pointing stick), touchpad, stylus
  Pointing stick is like an eraser in the middle of the keyboard
  Touchpad has a capacitive contact area with mouse buttons built in or below
  Stylus is like a pen used for digitized screens
Webcams / microphones: two-way camera that allows voice and audio data to be sent over IP

## Slide 12: Portable Device Display Types
Majority of laptop screens are LCD (Liquid Crystal Display)
10 to 17" diagonal with a 4:3, 16:9, 16:10, or 21:9 aspect ration
Screens are either high gloss or matte
LED backlighting has helped matte screens keep their brightness with antiglare screens
Most laptop LCD screens are TN or IPS

## Slide 13: Single-Function Ports
Audio port: 3.5mm TRS jack is typical on portable devices
Display ports: HDMI, DP, VGA, DVI are typical; use Fn + dual monitor to allow for two screens
Smart-Card reader: Log in device along with a PIN number for secure log in

## Slide 14: Networking Options
802.11 Wireless:
Bluetooth:
Hardware switches: manually control device to be enabled or disabled
Wired Ethernet (RJ45)

## Slide 15: General-Purpose Ports
Universal Serial Bus
Thunderbolt
IEEE1394
Docking station: allows for external devices to be plugged into your portable device while the device is charging
Port replicator: support connectors laptop devices lack
USB adapters: convert USB to RJ45, 802.11, RJ11

## Slide 16: Managing / Maintaining Portable Computers
Batteries: NiCad, NiMH, Li-Ion are common battery types for portable; Li-Ion only one used today
Li-Ion: keep 70-80% charged, never drain to 0% unless calibrating, store in a cool place (do not freeze); do not handle a ruptured battery
Li-Ion have built in circuitry to prevent overcharging

## Slide 17: Power Management
Designed to work with all hardware, the BIOS, and the OS to keep battery usage to a minimum for conservation
Power Modes: Mechanical and soft-power off mode
Also Sleep, Standby or Suspend modes
Hibernate mode is the slowest to recover from but saves the most battery
Configure Power Options:
Starts with the BIOS, enable ACPI
OS configure: Advanced Configuration and Power Interface; found in control panel or power | sleep in Windows
Use a pre-built plan or customize your own power plan

## Slide 18: Device Maintenance:
Cleaning: clean regularly, screen cleaner to remove dust from screen
Heat: Use power management (even with desktop) to turn off idle devices; listen and watch for fans (spinning too fast or being too silent are bad); keep ventilation space between back of PC and walls/obstructions
Cord/Cable management: avoid tripping hazards; keep cables out of walk ways
Security: Device/Cable lock; LoJack
Shipping: label as generic electronics versus 17" laptop

## Slide 19: Upgrading and Repairing Laptop
Review laptop documentation first and foremost!
Follow all ESD precautions!
Upgrading is limited to HDD, Optical, and RAM internally; externally ethernet and sound can be updated but at a cost of battery life
Disassembly of a laptop is a detailed orientated job. Manuals or guides should be followed to the letter to correctly disassemble a laptop; if no documentation is available, consult the Internet
  Organize all parts (screws especially) in labeled bags so as not to lose or miss any parts when reassembling
  If a part seems damaged or you fear breaking a component (ribbon cable), you may need to consult experts for advice

## Slide 20: Upgrading RAM in Laptop
Remove back RAM panel
Lift Ram at 45° angle and slide out of connector or place at 45° angle and slide in
Restore back RAM panel
If no panel exists in the back, RAM may still be upgradeable internally or not upgradeable as it is soldered to motherboard

## Slide 21: Upgrading HDD/SSD Storage
Remove back HDD panel
Use pull tab to remove HDD/SSD from SATA port or Insert HDD/SSD into cradle and slide into HDD SATA port
Return back HDD panel
If no panel on back, may be removed internally by removing bottom of laptop and keyboard

## Slide 22: Troubleshooting Laptops
Wont Power On:
Verify AC power, check wall outlet, check brick for laptop
If outlet is bad, call electrician. If adapter (brick) is bad; replace brick with exact replacement
Poor Performance:
One main cause of poor performance is too many application, too few resources (RAM is a culprit to poor performance)
Battery Issues:
Swollen Battery – overcharging, bad inverter; check battery often
Battery wont charge at all; battery may be exhausted, or AC is not doing its job (current too low)
Overheating:
Constant reboots; fans constantly on high speed, try to remove from hot environments

## Slide 23: Troubleshooting Laptops
Display Issues:
No display; check power, check screen dim settings. Check dual monitor settings
Try external screen to see if GPU adapter in laptop is working
Screen won't re-orientate; see if setting is disabled
Wireless issues:
Make sure not in airplane mode!
Make sure you are logged in to wireless
Make sure wireless in enabled or on

## Slide 24: Mobile Computing Devices
Smartphones:
Tablets:
E-Readers:
Wearable Technology:
Hardware Features:
Screens are OLED technology (organic light emitting diodes)
Cameras (HDR):
Digitizers:
GPS:

## Slide 25: Troubleshooting Mobile Devices
Check settings and configurations: something may be set incorrectly
Close all running app: check all running apps and close those you do not recognize or need running
Soft Reset: go to manufacturers resources and soft reset your device to try to get it back to a functioning state; typically after it locks up or freezes
Uninstall/Reinstall Apps: some apps (especially Android) are susceptible to crashing. Remove the app and leave feedback with the app developer
Factory default: hard crashes or phone turn in may need you to restore the phone back to its original state. Everything personalized will be lost if not backed up elsewhere
Dim display: increase your contrast or backlight; turn off auto-adjustments; make sure power management is not the cause of the screen being dimmed

## Slide 26: Troubleshooting Mobile Devices
Apps not loading: compatibility issue; problem with RAM or storage; run 3rd party tool to track app errors
Overheating: charging a defective battery, long downloads, frozen apps, or any intensive task can cause overheating
Slow Performance: virus; memory full or storage is full; too many apps or tasks running simultaneously; current hardware forced to run current platform (OS update)
System lockout: too many consecutive failed log in attempts (either by pin, pattern, biometric, or password; may wipe phone to factory default after too many wrong attempts
BYOD vs Corporate owned: Many corporations will not permit personal mobile devices on the premises for security concerns and may opt to hand own corporate phones to handle secure business (phone is controlled by IT)

## Slide 27: Troubleshooting Mobile Devices
Securing your data: multifactor authentication (password, biometric, pattern)
Biometric: face recognition, finger print, voice
Poor wireless: use wireless analyzer, turn off airplane mode
Poor cellular: use cell tower analyzer, turn off airplane mode
Weak signal: check SSID; see what wireless traffic or interference is around you
Unauthorized root access: jail Breaking

## Slide 28: Printer and Multifunction Devices
Printers: Impact, Inkjet, Dye-Sublimation, Thermal, Laser, 3-D Printers and virtual printers!
Impact: Dot Matrix; resolution is in pin-head count (9,12,18 and 24); Speed is in cps (characters per sec) 32-72 cps; loud and very hot due to friction; have a tractor feed paper (due to sprockets on sides that grab the apaper)
Inkjet: Printhead conencted to an ink cartridge; roller grabs paper a sheet at a time from tray; resolution is in dpi (dots per inch) 150 to 1400 dpi; speed is in ppm (pages per minute); 16 drops of ink to make a single color; colors include: cyan, magenta, yellow and black
Dye-Sublimation: print head heats up ink to turn it into vapor; photo quality printing; high-end graphics; special coated paper that will aborb all the different vapored ink into a continuous stream of color (no pixelation)

## Slide 29: Printer and Multifunction Devices
Thermal Printers: heated printhead to create high quality text on special paper; direct thermal or thermal wax transer paper; roll feed assembly
Laser Printers: electro-photographic imaging; high quality and high speed; parts of the Laser Printer:
  Toner Cartridge: supplies dry fine toner to the printer
  Imaging drum: aluminum cylinder coated with particles
  Erase lamp: exposes the entire surface of the imaging drum to light, making the whole drum conductive again
  Primary Corona/Charger roller: charge with high voltage forming a corona, enabling voltage to pass to the drum to charge the particles (600-1000V)
  Laser: acts as writing mechanism. Any particle struck by the laser becomes conductive; cause an image to be writen on the drum to be transferred to paper
  Toner: fine powder made up of plastic particles; charged to 200 to 500 Volts, causing the toner to be atracted to the charged particles of the drum

## Slide 30: Printer and Multifunction Devices
Laser Printers: electro-photographic imaging; high quality and high speed; parts of the Laser Printer:
  Transfer Corona: transfers the image from the drum to the paper by charging the paper positive to attract the image from the drum
  Fuser assembly: two rollers: pressure and heated, force the toner to stay in place and melt to the paper
3-D Printers: use melted materials to create images in three dimensions (x,y,z); printer will take a scanned image and build it from the bottom one layer at a time
Virtual Printers: Print to File
Print to PDF: requires adboe reader minimum to work. Saves document as a pdf ready file
Print to XPS: Default option for all Windows platforms
Print to Image: picture format (Jpeg, Bitmap, Gif, PNG)
Cloud Printing: Google Cloud Print, iCloud Printing

## Slide 31: Printer Languages
ASCII: developed by IBM; machine or binary code
Postscript; developed by adobe for font and graphics
Printer Command Language; Developed by HP
XPS; Developed by Windows

## Slide 32: Laser Printing Process
Processing: OS process your request to print through print spooler; creates a raster image on the page representing what the image should look like; goes to RIP to process image to the laser; requires enough RAM to do the whole job at once
Charging: Charge Drum with a uniform negative charge (600 to 1000V)
Exposing: Laser creates positive image on the drum based on raster image
Developing: Toner transfer to positive charge part of the drum
Transferring: Charges paper positive to attract toner on drum to the paper
Fusing: go to press and heated rollers to fuse toner to paper
Cleaning: rubber scrapper and erase lamp remove toner and charge from drum for next print job

## Slide 33: Configuring Print Settings
Layout: duples, orientation, multiple page, scaling, invert
Paper: paper size, paper type, paper source
Quality: resolution, optimize text or graphics, reduce ink usage
Common settings: apply watermark, header/footer, collate

## Slide 34: Troubleshooting Printers
Tools of the trade: multimeter, cleaning solutions, extension magnet, screwdrivers, anti-static vaccum
Print Job never prints: Is it on? Is it connected? Does it have paper? Is it conencted to the network? Correct IP address?
Strange size: check page setup; correct settings for paper type and size?
Misaligned or garbled print: driver issue mostly; check cables and software
Color prints in wrong color: wrong ink placed in wrong slot; ran out of a color; set print to grayscale