## Slide 1: CIS101A Week One
Computer Hardware Fundamentals
Comptia 1001

## Slide 2: Computing Process:
What is a computer?
What is an example of a computer?
What differentiates a general computer from one that performs specific tasks?
In understanding the concepts of what a computer is, you will need to understand the parts that make up the computer itself.
Computers have three parts: Hardware, Operating system, and Firmware
The CompTia 1001 Cert focuses on the Hardware and Firmware. CompTia 1002 will focus on the Operating system and applications.

## Slide 3: Hardware Computer Parts
Hardware is the physical stuff that you can touch or hold in your hand. On a personal computer, hardware will include keyboards, drives, monitors, mouse, etc.
Hardware is broken down into five categories: Input, Processing, Output, Data Storage, and Network Connection.
Input: Users sends unprocessed data to the system (Keyboard, Mouse, Scanner, Microphone)
Processing: Operating systems tells the hardware what to do with the user data (Central Processing Unit –CPU and Random Access Memory –RAM)
Output: System sends processed data back to the user as visual, sound, or hardcopy (Monitor, Speakers, Printer)
Data Storage: saving a permanent copy of the processed user data so the user can come back to it later (Hard Disk Drive (HDD), Solid State Drive (SSD), Optical Drive, or Tape Drive)
Network connection: How two or more computer devices connect to each other to exchange data.

## Slide 4: 1001: Computing Hardware – Certification points
Memorize the name of components, connectors, and terms
Connectors include:
HDMI and Display Port (Ch 17) CPU (Ch 3)
Universal Serial Bus (USB) (Ch 10) SSD (Ch 8)
Sony/Phillips Digital Interface Format (S/PDIF) (CH10)
Motherboard (Ch 6) Video Card (Ch 17)
TRS Audio Jacks (Ch 10) Expansion Slots (Ch 6)
Memory (RAM) (Ch 4) Power Supply (Ch 7)

## Slide 5: Central Processing Units (CPUs)
External Data Bus (EDB): enables devices to communicate with the CPU and back by applying or removing voltage from a physical wired connection (traces on a motherboard for instance)
Series of on’s and off’s is actually a language called Binary that the CPU can understand. Equivalent to Yes or No; On or Off, True or False or 1’s and 0’s.
Registers are the workplace or sorts for the CPU. They represent temporary space for the CPU to process data. The general purpose registers are AX, BX, CX and DX.
All of the commands the CPU understands is called its instruction set and CPU manufacturers cater to either CISC or RISC designs.

## Slide 6: Central Processing Units (CPUs)
The CPU clock (CLK) tells the CPU when and how fast to complete a task. One CLK per second is measured in hertz. Most CPU’s work in the millions (Mega) or billions (Giga) hertz.
Common CPU’s run in the 3 to 4 Gigahertz (GHz) range, but some can go to 5Ghz.
The system crystal imposes a limit on CPU speed. Note: this limit can be overcome by a process called overclocking but it is NOT Recommended.
CPU storage consists of two types of internal storage; registers and cache.

## Slide 7: 1001: Modern CPU’s
Developers: Intel and Advanced Micro Devices (AMD)
Due to cross-licensing agreements, AMD was permitted to “clone” Intel CPU’s (up until 1995). From 1995 on, AMD and Intel could no longer be pin compatible
Product Line: Varies by market needs
Enthusiasts for Intel would use i7 or i9; for AMD, Ryzen, Ryzen Threadripper
Mainstream for Intel would use i3, i5 or i7; for AMD, A-Series Pro or Ryzen
Budget for Intel would use Pentium or Celeron; for AMD, A-Series or FX
Server or Workstation for Intel would use Xeon; for AMD server would use Opteron or EPYC and Workstation for AMD would be Ryzen Pro or Threadripper

## Slide 8: 1001: Modern CPU’s
Microarchitecture: about every three years, Intel and AMD design better and more powerful CPU’s
These processors tend to have the same core (like i7), but would have generational improvements. Code names are used to distinguish one generation from another
Only through research can one keep up with the generational changes
Desktop Versus Mobile CPU
By architecture, mobile CPU are identical to their desktop counterparts; except in power management.
Mobile processors are designed to be throttled down to conserve battery life and to keep the CPU cooler

## Slide 9: 1001: Modern CPU’s
Technology: broken down into clock multipliers, 64-bit processing, virtualization support, parallel execution, multicore processing, integrated memory controller (IMC), integrated graphics processing unit (iGPU) and security.
Clock multiplier takes the system bus clock speed (100,133,166, 200 or 233Mhz) and internally multiplies that bus speed to generate CPU speed. [i.e. 200MHz bus multiplied by 20 would give 4GHZ CPU]
64 bit processing: CPU address lines would allow for 64 instructions at a time at once. This would permit the CPU to address 264 bytes of memory or about 16EB (ExaByte) of memory. (32 bit is capped at 4GB)
Virtualization support: covered in Ch 22.
Parallel Execution: Process multiple commands at a time in parallel. Modern CPU’s can contain 20 lines or more in parallel

## Slide 10: 1001: Modern CPU’s
Technology: broken down into clock multipliers, 64-bit processing, virtualization support, parallel execution, multicore processing, integrated memory controller (IMC), integrated graphics processing unit (iGPU) and security.
Multicore Processing: Microarchitecture hits its peak in 2002. To keep advancing CPU functionality, they added more cores to the CPU dye. In modern CPU’s having 32 cores is becoming standard.
Integrated Memory Controller (IMC): moved from the Northbridge of the chipset to within the CPU directly to better manage L3 Cache and RAM
Integrated Graphics Processing Unit: Designed to enhance overall performance while reducing energy use and cost. Intel HD Graphics and the AMD APU [PS4 and XBOXOne utilize AMD APU custom chips]
Security: NX bit technology to allow the CPU to protect certain sections of memory

## Slide 11: Selecting and Installing CPU’s
Selecting between Intel and AMD
  Based on need. What do you plan to do with the PC?
Intel and AMD have their specific strengths: Intel is good for multitasking; AMD is great at single focus (why gamers prefer AMD)
Cost is another issue. AMD tends to be cheaper than a comparable Intel
Motherboards after 1995 have specific sockets per processor; so picking your CPU must come first so you can narrow down the motherboard
Intel Sockets are Numbered: LGA1150,1151,2011 and 2066
AMD Sockets are Lettered: FM2+, AM3+, AM4, and TR4
Processor Numbers also follow a specific pattern: Intel i7 7500 U for instance: Intel Core, i7 is brand, 7 is generation, 500 is SKU and U is ultra low-power desktop processor

## Slide 12: Installation Issues
Considerations:
Notched CPU aligns properly to socket
Sufficient Power (4 or 8 pin power)
Adequate cooling
Socket Types: LGA (Land Grid Array – connection pads) and PGA (Pin Grid Array – pins on CPU)
Intel prefers LGA ; AMD prefers PGA
Almost all current motherboards will use Zero-Insertion Force (ZIF) sockets

## Slide 13: Installation Issues
Cooling
Every CPU beyond the 486 DX2-66 requires cooling. High end processors can consume over 100Watts of power and will get very hot!
This heat can be tempered off using passive, active or liquid cooling
Passive – Block of aluminum on top of CPU, no fans
Active – Block of aluminum has a powered fan blow cooler air
Liquid – Run radiator fluid by pump to the CPU to get it cool then pump the hot fluid away to be cooled
Aluminum block is typically called a heat sink
Steps for cooling: (1) Insert CPU into ZIF socket (2) Add thermal paste to CPU (3) place heat sink on top of CPU (make sure paste is covering) (4) add cooling device (passive, active, or liquid)

## Slide 14: Overclocking
Process of increasing the bus clock to a higher than recommended speed. This can, and often does, destabilize the system
Point of it is enthusiasts will buy cheaper CPUs then just ramp up the bus rate to get better performance. This can work short term but it can also cause permanent damage that your warranty will not cover
Both Intel and AMD have applications to help with overclocking, but do so at your own peril

## Slide 15: Troubleshooting CPUs
Overheating and Catastrophic failure
Overheating: too much thermal paste can impede heat transfer (CPU will shut down); Not enough Thermal paste will cause too little eat to be transferred to CPU (CPU will shut down); No cooling at all (no Fan is plugged in; no heatsink (CPU will shut down)
Catastrophic failure: Sudden system failure (BSoD); or electrical smell like ozone could be a short (look for decolorization)

## Slide 16: Motherboards
Form Factors
Industry standard for shapes and layouts that enable motherboards to work with compatible cases and power supplies
Three main form factors: ATX, Micro-ATX and ITX
Proprietary Form Factors (BTX) exist to add functionality beyond the current form factors
  Some proprietary boards (NLX) used Riser (Daughter) cards for expansion

## Slide 17: Chipset
Adds the features to the motherboard
Facilitates the communication between CPU and other devices
  [Legacy] – Northbridge and Southbridge
  Current – CPU and Hub (PCH – Intel; FCH – AMD) + Super I/O chip
Determines what memory is supported (DDR 3 or 4)
Types of peripherals buses (USB, IEEE1394)
  Integrated Sound, Ethernet and Video
  Integrated RAID and Networking

## Slide 18: Expansion Bus
Chipset expands address and data bus to the expansion slots
[Legacy] – older platform buses (ISA and PCI) utilized an expansion bus crystal to sync the expansion bus devices separate from the front side bus
PCI (Peripheral Component Interface): 32 bit bus, 33MHz, I/O bus
Mini-PCI – used for laptop devices; allows device to lay flat
PCI Express (PCIe): 64 bit dedicated serial bus
  Utilizes “lanes” to communicate at 2.5GTps (GigaTransfers per sec)
  Lanes can be 1, 2, 4, 8, 16 or 32 wide (16 is the most common) pushing data at 32Gbps (fast enough for high end video)

## Slide 19: Troubleshooting Expansion Cards
When a card fails, try device manager (diagnostic troubleshooting tool)
Typical first fix is reinstall the card to ensure it is properly connected
  Black ! On a triangle indicates that a device is missing or is not recognized
  Black ↓ on a white field indicates a disabled device
  ! Are the easiest problems to fix (typical load a driver)
  ↓ is tricky. First make sure it is not disabled. Then try updating the driver

## Slide 20: Upgrading and Installing Motherboards
Choose a case and motherboard
  Select AMD or Intel (choice must be made first)
Select what chipset (what features are you looking for?)
  Bulk of the cost is in Chipset
Make sure your selected motherboard has a book
Select a case that works for your selected board (ATX case for ATX board)
Replacing an existing motherboard – follow the directions to carefully remove the old motherboard; then line up your new motherboard with the I/O panel and screw in the motherboard to the stand-offs of the case
Connect Front Panel connectors: Reset, HDD LED, PWR LED, Speaker, PWR switch

## Slide 21: Troubleshooting Motherboards
Symptoms: Catastrophic, burn-in and component failure
Techniques for troubleshooting
  Patience and research skills required
  Tools like a POST card / multimeter can help with more serious issues
  Swap known good parts for potential bad to see if the problem persists

## Slide 22: Power Supplies
Voltage = pressure (V); Flow of electrons = Amperes (A); Work = Watt (W); Resistance = opposition to current (Ω)
Powering PC
  Convert AC to DC (Outlet to motherboard)
  AC (Alternating Current): USA 110-125V at 60Hz; UK 220-250V at 50Hz (dual-voltage supply will offer both)
  Multimeter, volt-ohm meter, digital multimeter can all measure AC and DC
  DC (Direct Current): 3.3V +/- 5V +/- 12V common for PC
  20 (20+4) P1 power connector is main power for motherboard
  4/8 pin CPU power may also be required for current motherboards
  SATA is 15 pin, Molex is 4 pin

## Slide 23: ATX Supplies
ATX originally was 20 pin P1 with 5V constantly on (soft power the PC off)
CMOS power management managed the PC voltages
ATX12V 1.3: 2003 introduced the P4 connector (added 12V to motherboard for more power)
  Introduced 6 pin AUX connector to supply 3.3 and additional +5V
EPS12V: 24 pin P1 power connector with a unique 8 pin CPU power connector; Added rails to power higher end systems
ATX12V 2.0: requires two 12V rails for any supply higher than 230W; Added SATA power connectors and 6/8 pin PCIe power connectors

## Slide 24: Power Supplies MISC
Active PFC (power factor correction): compensates for lost power during conversion process due to harmonics
Wattage Requirements: Combine power needs of individual parts; supplying under what is required (brownout) may cause system instability
Power supplies are required to be a minimum of 70% efficient (most current supplies are 80% +)
Power supplies will provide only the power needed (recommend to have a buffer)

## Slide 25: Installing and Maintaining Power Supplies
Installing can be as simple as putting in 4 screws. Just be certain the case supports the supply purchased
Short pins 15 and 16 or 16 and 17 to activate supply without in a case
Cooling: power supply fan is main cooling for supply (not serviceable)
System requires intake and exhaust fans to maintain proper air flow
Fan speeds can be adjusted to reduce noise or you can pay more for “quiet” fans
Fans can be 80 to 120+mm in circumference
Most motherboards support 2-3 3 pin fan connectors, 4 pin is dedicated to CPU fan
BIOS monitors fan RPM and will warn you when speeds get too slow

## Slide 26: Troubleshooting Power Supplies
Supplies will either fail immediately or over time
Power Supplies ARE NOT serviceable. Do NOT open a power supply! (even to fix a fan)
Test the supply with DMM or power meter (voltages should be +/- 5% from rated value)
  Yellow is 12V – 11.4 to 12.6 volts
  Red is 5V – 4.75 to 5.25 volts
  Orange is 3.3V – 3.1 to 3.4 volts
Slow death is typically cause by failed capacitors within the supply

## Slide 27: Fuses and Fire
Power supplies are fused internally – not serviceable!
Failure to respect the power of electricity will eventually lead to fire
Fire extinguishers should be kept handy: By class:
  A – wood or paper fires
  B – Gas, solvents, paints
  C – electrical
  D – combustible metals (magnesium)
  K – cooking oils, trans-fats

## Slide 28: Modular Power Supplies
Allow only the necessary cables to be plugged in instead of all the cables
Keeps a clean cable install, helps with air flow
Not wasting cables on nonexistent devices. Only use what you need
More efficient power management

## Slide 30
END of WEEK One