## Slide 1: Week Three CIS101A
Computer hardware fundamentals

## Slide 2: LCD Displays
Liquid Crystal Displays: Composed of the following:
Pixels and subpixels arranged in rows, CCFL or LED Backlight + inverter
Twisted Nematic [TN] and In-Plane Switching [IPS]
TN: Good for gaming, Fast Refresh Rate, Fast Response Time, Poor Color
IPS: Great for graphic art, Great viewing angle, Great Color, mediocre Response Time

## Slide 3: Display Characteristics
Resolution – Number of total pixels that can be displayed on a screen
Aspect Ratio: 4:3, 16:9 (WS), 16:10, 21:9 (FWS) – How the pixels are arranged
Brightness – Strength of LCD monitor’s backlights (measured in nits)
Viewing Angle – Angle from center to see optimal picture – TN:70° | IPS:178°
Response Rate – Amt. of time for all the sub-pixels to change from one state to another
Refresh Rate – How many times in a second is the screen redrawn
Contrast Ratio – Comparison between the brightest white and darkest black
Color Depth – number of unique colors that a display can show at any given time

## Slide 4: Projectors
Most Projectors are “front view”
Started with CRT then transition to LCD
LCD: up to 2k resolution, suffers motion blur, inexpensive and portable
Transition to DLP: Digital Light Processing
DLP: Custom CPU, color wheel and millions of micro-mirrors control image
DLP: Large, expensive, get very hot but offer best picture (4K resolution)
Brightness is measured in Lumens (amt of light from a source at a given angle)
Throw: size of the image at a certain distance from the screen
Lamps are used as projection image source; why projectors get hot

## Slide 5: VR Headsets
Immerse the user into a personal projected space that they can move in 360°
Composed mostly of OLED panels, the close proximity of the screens to the eyes emulate a large screen
Requires a powerful base system to both send the data and monitor the x, y, and z space required for immersion
HTC Vive, PSVR, Oculus are examples

## Slide 6: Monitor Connections
VGA: 15 pins (3 rows of 5 pins), Analog video only, up to 2k resolution
DVI: 24 pins (8 rows of 3 pins), Analog or Digital (-A or –D, or both –I), single or dual cable, video only
HDMI: 19 pins trapezoidal connector, Video + Audio, up to 4K resolution
DisplayPort: C connector with Bevel, AKA Thunderbolt
HDBaseT: HD Video and Audio over CAT5a or CAT6 cable
Utilize Adapters to convert from one connection to another

## Slide 7: Display Adapters
Video card: dedicated task of processing data from the CPU or GPU and sending it to the display
5 Aspects defined for a display adapter:
Motherboard slot: PCI, PCIe or Integrated [legacy: AGP]

## Slide 8: Graphic Processors & Memory
Graphic Processor (GPU): Chip dedicated to handling mathematics and polygons (NVIDIA and AMD are two GPU manufacturers)
Video Memory – Dedicated GDDR memory typically comes on video adapter card; Integrated controllers use DDR main memory
GDDR3; runs at faster speeds than DDR3, different cooling requirements
GDDR5; More than doubles the input/output rate of GDDR3
GDDR6; Successor to GDDR5
High Bandwidth Memory (HBM): competitor to GDDR5 and 6 memory

## Slide 9: Integrated GPU - APU
Onboard Video is a term to describe Integrated Video
GPU is built into the Northbridge or the CPU itself
Lacks performance of dedicated video cards and utilizes Main Memory to handle video
Good cost saving measure
Accelerated Processing Unit (APU): AMD integrates 2 to 8 CPU cores, a memory controller for DDR4 support, cache and a GPU for 3-D graphics

## Slide 10: Roles Hosts play In Networks
Clients, nodes and hosts are synonymous to a PC and how it is utilized on a network
Hosts that provide a service to a user is a “Server”
Hosts that used a service provided is a “Client”
For a network to function you need 4 things:
Host: PC that stores data
Transmission Media: Copper wire, Radio waves, Light pulses
Network Interface: Network Interface card (NIC); transceiver, transducer, modem
Protocols: Rules that govern how data will be sent and received; TCP and UDP

## Slide 11: Frames and NICS
Data is moved on a network in “frames”
NIC will create and process those “frames”
Each NIC has a unique identifier called a Media Access Control address or MAC address
MAC Address is 48 bits long and in hexadecimal (0-9,A-F; A=10, B=11…)
Each decimal character is composed of 4 binary bits that make up a hexadecimal number
The “frame” is composed of the recipient MAC, sender MAC, the Data, and CRC for error checking and correcting

## Slide 12: Ethernet
Created by a consortium of companies: DEC, Intel, Xerox
Established in the 70’s, have been greatly improved by efforts of IEEE
Modern Ethernet will have speeds of 10BaseT, 100BaseT, 1000BaseT, and 10GBaseT
Utilizing a switch: you can create an Ethernet Star Bus network
With CAT Level cabling determining speeds:
CAT1 – Telephone
CAT3 – 10Mbps network
CAT5 – 100Mbps, 5e – 1000Mbps
CAT6 – 10Gbps (55m), 6a – 10Gbps (100m)
CAT7 – 10Gbps (100m) Shielded

## Slide 13: Ethernet with Twisted Pair
CAT3 and up will utilize a RJ-45 connection (8 wires, 4 pairs)
CAT1 will use RJ11 connection (4 wires, 2 pairs)
Plenum cable jackets are preferred for HVAC; fore resistant over PVC
T568A and B are wiring standards for Twisted pair cabling
A: color order – Gr/W, Gr, Or/W, Bl, Bl/W, Or, Br/W, Br
B: color order – Or/W, Or, Gr/W, Bl, Bl/W, Gr, Br/W, Br
Patch cable has same standard on both ends; crossover cable has A on one end and B on the other

## Slide 14: Ethernet with Alternate Connections
Fiber Optic: Single Mode or MultiMode Cable
Single Mode: 10 micron core, LASER as a source, up to 40km, 1 communication at a time
MultiMode: 100 micro core, LED as a source, up to 2km, multiple communications possible at one time
LC connectors will allow 2 fiber cables into a single connection
Immune to EMI but not radiation, expensive
Coaxial: rated by RG name; RG59 and RG6, 75Ω impedance
Copper conductor, insulator, mesh shielding, and PVC cabling make up Coaxial
Type F (digital cable) or BNC connector (Bus Topology)

## Slide 15: Implementing Ethernet
Typical LAN: short geographical distance (classroom or office)
Broadcast domain: all nodes will receive broadcast frames from every other node
Ethernet over Power (EoP): network over existing power lines
Structured Cabling: Basic concepts with installing network cabling
Telecommunications room: central local for all systems wiring
Horizontal cabling: Horizontal cables from telecom room to workstations
Solid versus stranded core wire: Solid wire is better conductor but not mailable
Equipment Rack: provides sturdy place for all network hardware
Go Wide! Add a router to your LAN

## Slide 16: Wireless Networking
Follows the IEEE802.11 committee guidelines
Requires 3 parts to wireless networking to function:
Wireless Access Point (WAP): Centrally connects all wireless devices (like a switch in wired network)
Need an 802.11 compatible device
Need an 802.11 Interface (transceiver / modem)
Wireless will utilize Carrier Sense Multiple Access / Collison Avoidance circuitry (CSMA/CA)

## Slide 17: Wireless Access Modes
Ad-Hoc mode: Wireless Peer to Peer networking through an Independent Basic Service Set (IBSS); good for a dozen devices or less
Infrastructure mode: Use 1 or more WAPs to connect the wireless network nodes to a wired network segment through a Basic Service Set (BSS)
Good for SOHO networking
Requires a lot of planning; especially in WAP placement

## Slide 18: Wireless Speed and Range
Two approved frequencies for Wi-Fi: 2.4Ghz and 5Ghz
Wi-Fi compatibility is based on frequency
 | 802.11a | 802.11b | 802.11g | 802.11n | 802.11ac
Max throughput | 54Mbps | 11Mbps | 54Mbps | 100+ Mbps | 1+ Gbps
Max range (optimal range) | 150ft (100ft) | 300ft (150ft) | 300ft (150ft) | 300+ ft | 300+ ft (150ft)
Security | SSID, WEP, WPA, WPA2 | SSID, WEP, WPA, WPA2 | SSID, WEP, WPA, WPA2 | SSID, WEP, WPA, WPA2 | SSID, WEP, WPA, WPA2
Compatibility | 802.11a | 802.11b | 802.11b, g | All | 802.11a, n
Frequency | 5Ghz | 2.4Ghz | 2.4Ghz | 2.4 and 5 Ghz | 5Ghz
Mode | Ad-hoc / Infrastructure | Ad-hoc / Infrastructure | Ad-hoc / Infrastructure | Ad-hoc / Infrastructure | Ad-hoc / Infrastructure
Description | 8 channels available | 11 channels available (3) | 11 channels available (3) | 11 (3) / 8 channels available | 11 (3) / 8 channels available

## Slide 19: Other Wireless Connections
Infrared: IR – IrDA protocol for communications, up to 4Mbps, 1m, no encryption, point to point ad-hoc, no obstructions or ambient light
Bluetooth – PAN geography, 2.4GHz wireless, piconets (up to 7 devices per piconet), Adaptive Frequency Hopping through 79 channels, encrypted
Class of Device determines power usage and Range:
1: 100mW power at 100m range
2: 2.5mW power at 10m range
3: 1mW power at 1m range
Near Field Communication (NFC): Requires NFC chip installed, 13.58Mhz at 424kbps speed, up to 2 inches, encrypted, payment services and passports

## Slide 20: Connecting to the Internet
Internet Tiers: Groups of providers for the Internet
Tier 1: Backbone owners: Fiber Optic lines connecting network address points
Tier 2: Lease Lines from Tier 1 to provide regional connectivity
Tier 3: Sub-lease from Tier 2 to provide local support
Internet Service Provider: Tier 1 and 2 providers. Connect user to their backbone for a fee
Connection can happen by Dial-up, DSL and Cable, Fiber, LoS and Cellular
Dial-up uses phone line and switching system to connect by modem; up to 56kbps.
ISDN upscales this with BRI: 1 128kbps bearer line with a 16kbps control or 1 64kbps voice and a 64kbps data line
PRI: 23 64kbps channels plus 1 control channel for 1.544Mbps (T1 line)

## Slide 21: DSL and Cable Connected
Digital Subscriber Line: Standard phone line (RJ11)
Microfilters are used to block harmonic frequencies from the phone line
Requires a dedicated DSL connection from the ISP to the home; generally slow upload with competitive download speeds
Cable: uses cable TV line filtered to send and receive very fast speeds (35Mbps upload / 1000Mbps + download)
F-Type RG6 cable, a DOCSIS 3.1 modem (for 1000Mbps), RJ45 CAT 5e or better cable

## Slide 22: Fiber, Line of Sight and Cellular
FTTN: Fiber to the Node
FTTP: Fiber to the Premises
Google Fiber / AT&T offered fiber from pole to home
LoS: Two directional high bandwidth antenna (up to 8 miles away), 1.5Gbps speed is possible at 24Ghz band
Cellular: Generational tech; 4G LTE, 5G being the most common now
4G LTE supports 1Gbps while 5G supports 20Gbps

## Slide 23: Connection to the Internet
SOHO: Connect a single device of a network of devices
Choose Wired / Wireless or both
SOHO router will need NAT (network address translation) to be enabled; hide all your devices and make them “look” like 1 device
SOHO router should have its default SSID, username and password changed immediately
SOHO will want static addressing; DHCP is good for individual homes, not businesses
Disable the SSID after you change it so it does not broadcast
Update the firmware of your router to keep it current with standards

## Slide 24: Internet Protocols
Protocols:
Application protocol | Function | Port Number
HTTP | Web Pages | 80
HTTPS | Secure Web Pages | 443
FTP | File Transfer | 20, 21
SFTP | Secure File Transfer | 22
IMAP | Incoming Email | 143
POP3 | Incoming Email | 110
SMTP | Outgoing Email | 25
TELNET | Terminal Emulation | 23
SSH | Encrypted Terminal Emulation | 22
RDP | Remote Desktop | 3389
SIP | Voice over IP | 5060
Utility protocol | Function | Port Number
DNS | Allows DNS naming | UDP - 53
DHCP | Automatic IP Addressing | UDP - 67, 68
LDAP | Querying Directories | TCP - 389
SNMP | Remote management of Network Devices | UDP – 161,162
SMB | Folder Sharing | TCP – 445 / UDP – 137, 138, 139
AFP | macOS file service | TCP - 548
SLP | Services discovery protocol | TCP/UDP – 427
NetBIOS | NetBIOS over TCP/IP | TCP/UDP – 137 / TCP – 139 / UDP - 138