## Slide 1
CIAT CIS101A Week 2 Day 4 |  | 
Memory and Bios Cards |  | 
Week 2 – PART 2 Day /Time Face-to-Face Online class access 24 x 7 | Chapter 3 System Components 3.7 Memory 3.8 Memory Installation 3.9 Memory Troubleshooting 3.10 BIOS/UEFI 3.11 Expansion Cards 3.12 Video 3.13 Audio 3.14 Cooling | 3.7.6 Practice Questions 3.8.8 Practice Questions 3.9.6 Practice Questions 3.10.9 Practice Questions 3.11.5 Practice Questions 3.12.6 Practice Questions 3.13.8 Practice Questions 3.14.3 Practice Questions Labs 3.10.7 + 3.13.7 Video 3.8.1 + 3.10.2 + 3.14.1

## Slide 2
3.7 Memory:
Random Access Memory (RAM) can be classified as one of two types:
Type | Description | 
Static RAM (SRAM) | SRAM stores data using four transistors for every bit of data. SRAM does not require constant power to maintain the contents of memory. (This is non-volatile memory) SRAM is more complex and less dense (e.g., lower storage capacity) than DRAM. SRAM is faster and requires less power than DRAM. Regular SRAM still requires periodic power to maintain the state of memory, but the rate of refresh is less than with DRAM. Non-volatile SRAM (nvSRAM) is able to maintain memory contents when the power is turned off. SRAM is typically used in cache memory, such as CPU cache, hard disk cache, and cache in networking devices. | 
Dynamic RAM (DRAM) | DRAM stores data using a single transistor for every bit of data (a 0 or a 1). To maintain the state of the transistor, DRAM must continually supply power to the transistor; when the power is turned off, the data is lost. (This is volatile memory). | 
 | DRAM is simple to implement. DRAM can have a very high density (e.g., high storage capacity). Because of the simplicity, DRAM is relatively inexpensive. DRAM is used in the main system memory on a computer. | 

## Slide 3
3.7 Memory: (continued)
All system memory used in personal computers is DRAM. Individual DRAM chips are packaged onto a board that contains circuitry for reading and writing to the memory. You should be aware of the following standards for DRAM:
Hardware Image | Standard | Description
 | DDR (Double Data Rate Synchronous Dynamic RAM | DDR is a variation of the original synchronous DRAM (SDRAM).
 |  | All variations of DDR are synchronized with the system clock and accept 64-bit words. DDR accepts a single command and two consecutive data sets per bus clock cycle. Operating at the same frequency, DDR has twice the bandwidth of SDRAM. DDR operates at 2.5 volts at bus frequencies between 100-200 MHz.
 |  | Note: DDR memory has a single notch, slightly off center. DDR memory has 184 pins.

## Slide 4
3.7 Memory: (continued)
All system memory used in personal computers is DRAM. Individual DRAM chips are packaged onto a board that contains circuitry for reading and writing to the memory. You should be aware of the following standards for DRAM:
Hardware Image | Standard | Description
 | DDR2 | DDR2 doubles the data transfer rate of DDR, for four times the bandwidth of SDRAM. DDR2 accepts four consecutive 64-bit words per bus clock cycle. DDR2 includes a buffer between the data bus and the memory. DDR2 operates at 1.8 volts at bus frequencies between 200-533 MHz. The internal memory frequency is half that of the bus frequency (100-266 MHz)
 |  | DDR2 memory differs from DDR memory as follows: 1. The notch is slightly closer to the middle. 2. It has 240 pins. While you don't need to count the pins, you should that the pins are smaller because they have to fit in the same space as the DDR memory.

## Slide 5
3.7 Memory: (continued)
All system memory used in personal computers is DRAM. Individual DRAM chips are packaged onto a board that contains circuitry for reading and writing to the memory. You should be aware of the following standards for DRAM:
Hardware Image | Standard | Description
 | DDR3 | DDR3 doubles the data transfer rate of DDR2, for eight times the bandwidth of SDRAM (twice that of DDR2).
 |  | 1. DDR3 accepts eight consecutive 64-bit words per bus clock cycle.
 |  | 2. DDR3 operates at 1.5 volts at bus frequencies between 400-1000 MHz. The internal memory frequency is one-fourth that of the bus frequency (100-266 MHz).
 |  | Note: DDR3 memory has a single notch more left of center than the notch for DDR or DDR2. Like DDR2, DDR3 has 240 pins.

## Slide 6
3.7 Memory: (continued)
All system memory used in personal computers is DRAM. Individual DRAM chips are packaged onto a board that contains circuitry for reading and writing to the memory. You should be aware of the following standards for DRAM:
Hardware Image | Standard | Description | 
 | DDR4 | DDR4 doubles the data transfer rate of DDR3 for ten times the bandwidth of SDRAM. | 
 |  | DDR4 accepts eight consecutive 64-bit words per bus clock cycle. | 
 |  | DDR4 operates at 1.2 volts at bus frequencies between 1066-2133 MHz. The internal memory frequency is about one-tenth that of the bus frequency (100-266 MHz). | 
 |  | DDR4 reduces the demand for power. | 
 |  | DDR4 is not compatible with earlier types of random access memory (RAM) because of the different signaling voltages, physical interface, and other factors. | 
 |  | DDR4 theoretically allows for DIMMs of up to 512 GB in capacity, compared to the DDR3's theoretical maximum of 128 GB per DIMM. | 
 |  | Note: | DDR is no longer used in modern motherboards, although you might encounter DDR memory in older systems.

## Slide 7
3.7.5 Memory Speeds:
Memory is rated based on its guaranteed stable operating frequency and bandwidth (the rate at which data can be read or written). Memory ratings help you to differentiate between slower and faster RAM.
The following rating systems are used: | 
For all DDR memory (DDR, DDR2, and DDR3), a new designation was introduced to identify that twice the data was being transferred with each bus clock cycle. | 
The number following the DDR-, DDR2-, and DDR3- prefixes is the data transfer rate (twice the bus frequency). For example, DDR-400 matches a bus frequency of 200 MHz; DDR2-800 has a bus frequency of 400 MHz; and DDR3-1600 has a bus frequency of 800 MHz. | 
For DDR past 150 MHz (and for all DDR2 and DDR3 memory), the PC- designation was changed to identify the bandwidth instead of a number derived from the bus frequency. | 
The bandwidth is 16 times the bus frequency, or 8 times the DDR- designation. For example, DDR-400 has a bandwidth of 3200 MBs (PC-3200); DDR2-800 has a bandwidth of 6400 MBs (PC-6400); and DDR3-1600 has a bandwidth of 12800 MBs (PC-12800). For a brief time, the double-frequency designation used the PC- prefix for early DDR modules. For example, PC-200 used with DDR indicates a bus frequency of 100 MHz, not a bandwidth of 100 MBs (PC-200 is equivalent to DDR-200 which is equivalent to PC-1600). | 
Note: | When listing the frequency, the frequency value usually indicates the bus speed, not the internal frequency (DDR designation) used by the memory.

## Slide 8
3.7.5 Memory Speeds:
The following table lists the various memory speed designations for the most common memory types:
Memory Type | Bus Speed | Designations
DDR | 100 MHz | PC-200 or PC-1600 or DDR-200
 | 133 MHz | PC-266 or PC-2100 or DDR-266
 | 166 MHz | PC-2700 or DDR-333
 | 200 MHz | PC-3200 or DDR-400
DDR2 | 200 MHz | PC2-3200 or DDR2-400
 | 266 MHz | PC2-4200/4300 or DDR2-533
 | 333 MHz | PC2-5300/5400 or DDR2-667
 | 400 MHz | PC2-6400 or DDR2-800
 | 533 MHz | PC2-8500/8600 or DDR2-1066
DDR3 | 400 MHz | PC3-6400 or DDR3-800
 | 533 MHz | PC3-8500 or DDR3-1066
 | 667 MHz | PC3-10600/10666 or DDR3-1333
 | 800 MHz | PC3-12800 or DDR3-1600
 | 900 MHz | PC3-14400 or DDR3-1800
 | 1000 MHz | PC3-16000 or DDR3-2000

## Slide 9
CIAT CIS101A
3.7.5 Memory Speeds:
The following table lists the various memory speed designations for the most common memory types:
Memory Type | Bus Speed | Designations
DDR4 | 800 MHz | PC4-12800 or DDR4-1600
 | 933 MHz | PC4-14900 or DDR4-1866
 | 1066 MHz | PC4-17000 or DDR4-2233
 | 1200 MHz | PC4-19200 or DDR4-2400
 | 1333 MHz | PC4-21300 or DDR4-2666
 | 1600 MHz | PC4-25600 or DDR4-3200

## Slide 10
3.7.5 Memory Speeds:
When comparing the speed of memory modules, be aware of the following:
The most useful way to compare most DDR modules will be to compare the amount of data that can be transferred per second (bandwidth), as indicated by the PC- designations. For example, PC-3200 will always indicate a "faster" memory module than one with a PC-2700 rating.
PC- numbers up to PC-266 identify the frequency (or double the frequency), not the bandwidth. For example, a PC-266 module has a greater bandwidth than a PC-1600 module (PC-266 = PC-2100).
Comparing DDR- numbers can also give you an idea of the relative bandwidth. For example, DDR-600 can transfer more data than a DDR2-400 module.
The bandwidth identifies a theoretical maximum that the memory can transfer in a given time period, and is directly related to the front size bus frequency.
If you can derive the bus frequency, you can also get a relative idea of the amount of data a module can handle. When comparing DDR modules, the frequency is relative to the bandwidth. For example, a DDR2 module operating on a 533 MHz bus is faster than a DDR3 module on a 400 MHz bus.
Other memory characteristics besides the frequency could affect the effective bandwidth or actual speed of the memory module.

## Slide 11
3.7.5 Memory Speeds:
Another method for increasing memory bandwidth is by providing multiple channels within the memory controller.
Dual-channel systems use two memory controllers, while triple-channel systems use three memory controllers. Quadruple-channel (quad-channel) systems use four memory controllers. Each memory controller can communicate with one or more memory modules at the same time.
To operate in dual-channel mode, install memory in pairs; to operate in triple-channel mode, install memory in sets of three. To operate in quad-channel mode, install memory in sets of four
Dual-channel systems theoretically double the bandwidth. However, in practice, only a 5–15% increase is gained.
Dual-channel, triple-channel, and quad-channel support is mainly a function of the motherboard (e.g., the memory controller), not the memory itself. DDR, DDR2, DDR3, and DDR4 can all work in dual-channel systems (depending on the memory supported by the motherboard); both a triple-channel and a quad-channel system use DDR3 and DDR4.

## Slide 12
3.8 Memory Fact and Installation:
The best way to ensure that you get the correct RAM for your system is to consult the motherboard documentation.
In addition, there are several websites on the Internet where you can look up your system or scan your system to find the correct memory type to install.
When selecting RAM, consider the following factors:
Characteristics | Description
Packaging (Form) | When you are purchasing RAM for a system, the most important consideration is the packaging, also called memory form. The packaging controls both the physical size of the memory module and the memory standard (e.g., DDR2, DDR3, DDR4). If you purchase the wrong type of RAM, it will most likely not fit. If it does, it might have different voltage requirements than what is supported by your motherboard. Memory packaging (memory form) and capacity must match what is supported by the motherboard.

## Slide 13
3.8 Memory Fact and Installation: Continued
Capacity | The capacity (sometimes called the size) refers to the storage capacity of the memory module (e.g., 256 MB, 512 MB, 1 GB).
 | The total capacity of memory that you can install in your system is limited by:
 | The number of memory slots on the motherboard.
 | The maximum total capacity that can be installed. For example, most systems will have a maximum capacity of between 3 GB and 16 GB of RAM.
 | The maximum module capacity. For example, the motherboard might only be able to accept up to 2 GB or 4 GB modules.
 | The maximum amount of memory that can be addressed (used) by the operating system. A 32-bit operating system can use between 3 GB and 4 GB of memory, while a 64-bit operating system can use more.

## Slide 14
3.8 Memory Facts: (continued)
The best way to ensure that you get the correct RAM for your system is to consult the motherboard documentation.
In addition, there are several websites on the Internet where you can look up your system or scan your system to find the correct memory type to install.
When selecting RAM, consider the following factors:
Characteristics | Description
Capacity (cont) | You can install more than 4 GB of memory in a system that uses a 32-bit operating system; however, the operating system will only be able to use between 3 GB and 4 GB of that memory.
 | If your motherboard had a total of three slots, with a maximum module size of 1 GB and a system maximum of 3 GB, and if you had two 512 MB modules installed, you would only be able to add a single 1 GB module bringing the total up to 2 GB.
 | You could also replace one or both of the 512 MB modules bringing the total to 2.5 or 3 GB respectively.

## Slide 15
3.8 Memory Facts: (continued)
The best way to ensure that you get the correct RAM for your system is to consult the motherboard documentation.
In addition, there are several websites on the Internet where you can look up your system or scan your system to find the correct memory type to install.
When selecting RAM, consider the following factors:
Characteristics | Description
Frequency | For optimal performance, you should match the memory frequency (sometimes called the speed) with the frequency supported by the system bus/memory controller.
 | You can install slower memory in the motherboard, but this will degrade performance.
 | You can install faster memory in the motherboard, but it will operate only up to the maximum supported by the motherboard.
 | When you mix memory with different frequencies, all memory will operate at the lowest frequency.
 | Most memory modules include an EEPROM chip that identifies its frequency. The BIOS uses the information in this chip to set the frequency automatically.
 | On many systems, you can edit the BIOS manually to change the frequency.

## Slide 16
3.8 Memory Facts: (continued)
The best way to ensure that you get the correct RAM for your system is to consult the motherboard documentation.
In addition, there are several websites on the Internet where you can look up your system or scan your system to find the correct memory type to install.
When selecting RAM, consider the following factors:
Characteristics | Description
Frequency (cont) | If the BIOS does not configure memory to run at its highest rated speed, then do the following:
 | Verify that the motherboard supports that speed. You might be able to update the BIOS to support faster memory.
 | The SPD on the memory is often set below the maximum rating for the memory. To use the maximum speed settings, you might need to manually configure the speed and timing settings for the memory (if the motherboard allows you to do this).

## Slide 17
3.8 Memory Facts: (continued)
Characteristics | Description
CAS Latency | Another factor that affects the performance of memory is the latency associated with accessing data in RAM.
 | With a read request, there is a delay between the time the data is requested and the time that the data is available on the module's output pins. This delay is called the CAS latency (CL).
 | Older memory expressed the delay in nanoseconds, but DRAM uses a ratio based on the clock frequency to describe the delay.
 | For memory modules of the same type and frequency, a lower CAS number indicates less delay (e.g., "faster" RAM).
 | Because CL is related to the frequency, you cannot directly compare the CAS latency between modules with a different frequency. For example, a DDR2 module operating at 533 MHz with a CL of 6 has more delay than a DDR3 module at 667 MHz with a CL of 7.
 | In addition to CL, there are other memory characteristics that describe the delay for performing other types of operations. Collectively, these values are referred to as the memory timings.
 | For stable operations, the bus must take into account these latencies to keep the bus and the memory synchronized.
 | Manufacturers test memory modules and rate them based on the operating frequency and the timing characteristics. Settings that produce stable performance are then encoded into the SPD module on the memory. The BIOS then reads this information to know how to configure memory settings on the motherboard.
 | For many systems, you can manually modify the memory timings and frequency. Running RAM at a lower clock speed enables you to decrease the CAS latency setting; increasing the frequency must usually be compensated for by increasing the CL (and other) settings

## Slide 18
3.8 Memory Facts: (continued)
Characteristics | Description
Error Correcting Code | Error Correcting Code (ECC) memory is a type of memory that detects and corrects the common kinds of internal data corruption. ECC memory is also called parity memory. Using ECC, a value is appended to the end of each byte so that the value of the data can be compared and recalculated if an error occurs. ECC is an improvement on parity techniques because errors in more than one bit can be detected and corrected.
 | Keep in mind the following facts about error correcting memory: Memory modules with ECC have extra memory chips on the module (typically 9 modules instead of 8). If the number of chips is divisible by 3 or 5, the module is ECC memory. ECC or parity memory must be supported by the motherboard. Because it is more expensive than non-ECC, ECC memory is typically used only in servers. ECC memory is slower than non-ECC memory. Do not mix ECC and non-ECC memory in a system. Mixing ECC and non-ECC memory disables the error correction function.
 | Note: You might hear the terms parity and ECC being used interchangeably. However, parity RAM only checks for errors while ECC RAM checks and corrects errors

## Slide 19
3.8 Memory Facts: (continued)
Characteristics |  | Description
Parity RAM |  | Parity memory is a type of memory that checks for common kinds of internal data corruption.
 |  | It does not correct internal data corruption.
 |  | Non-parity memory does not perform error checking. Parity RAM is no longer used.
 |  | Today, PC systems use ECC for error detection and correction.
Buffered (Registered) |  | Buffered (or registered) RAM has a buffer that holds memory addresses or data before it is transferred to the memory controller.
 |  | Buffered RAM improves stability on systems with a lot of RAM (over 1 GB). Buffered RAM might slow system performance. ECC modules are typically buffered. Buffered RAM must be supported by the motherboard. Some motherboards require buffered memory.
Note: | Unbuffered memory does not have a buffer to hold memory addresses or data before it is transferred to the memory controller. Unbuffered memory can be found in servers and high-end workstation. | 

## Slide 20
3.8 Memory Facts: (continued)
Characteristics | Description
Single or Double-Sided | Single-sided RAM has memory modules that are organized into a single logical bank; double-sided RAM has modules organized into two banks.
 | The computer can only access data in one bank at a time. Therefore, single-sided RAM allows access to all of the memory, while with double-sided RAM, the computer must switch between banks.
 | Originally, double-sided RAM had modules on both sides of the circuit board, and single-sided RAM had modules on only one side. However, you can also have double-sided RAM with modules on only one side, where the memory is divided into separate banks internally.
 | Single-sided memory of the same capacity as double-sided memory uses half the number of memory modules (modules are denser, with a higher individual capacity).
 | Some older motherboards are unable to use double-sided memory, while some that allow double-sided memory can only use up to half the total memory when all memory slots are filled, or mixing single- and double-sided together might not be allowed.
 | Most motherboards support both single- and double-sided memory. However, verify compatibility before purchasing.

## Slide 21
3.8 Memory Installation:
When installing memory, remember the following:
Memory modules are very sensitive to ESD. Be sure to take proper steps to prevent ESD.
You can add single memory modules to computers that use DDR (including 2, 3, and 4).
Install memory in the correct slot. Although several memory slots might be open, some system boards require that you use specific slots. Check the system board documentation for more details. For many systems, start with the first bank. The first memory bank is often closest to the processor. On some systems you should fill each bank in order.
Align the memory before inserting, and do not force the module in place. Most memory is keyed to prevent it from being installed backwards or in incompatible slots.
Most RAM is held in place with small tabs on either end. To remove RAM from a motherboard, push the tabs down to rotate them back, then pull the RAM straight up.

## Slide 22
3.8 Memory Installation:
When installing memory, remember the following (CONTINUED):
For a dual-, triple-, and quad-channel configuration: Modules must be installed in matching sets (capacity and speed), preferably of the same manufacturer and model. You can typically use different capacity modules between sets. For example, you can use two 1 GB modules as one set and two 512 MB modules in the second set. Install modules in the slots specified in the motherboard documentation. Many motherboards color the slots, with slots used within a set having the same color.
If you install single memory modules, the system will continue to use the memory, but cannot use the memory in dual-channel mode.
Following installation, power on the system and check for errors. Most BIOS programs include a memory count that displays the total amount of system memory. If it does not count the proper amount of memory, you may have installed the memory incorrectly or you may have a faulty memory module. Also, if the BIOS generates an error between 200 and 299, the error is a memory error.
Most systems will configure memory settings (frequency, voltage, and timing including latency) automatically based on information in the EEPROM chip. If necessary, edit the BIOS to manually configure memory settings.

## Slide 23
3.9 Memory Troubleshooting:
The following are common signs that a computer needs additional memory:
Symptom | Description
High Disk Usage | Some operating systems send data to the hard disk drive if there is not enough physical memory available. If you hear the hard drive constantly operating as you work, or if the hard drive light on the front of the system case stays illuminated for long periods of time, you may need to add more physical memory to the computer.
Not Enough Memory Errors | If you receive Not Enough Memory or Out of Memory errors when you try to open and use more than one program at a time, you may need more physical memory.
 | Memory problems usually are found in one of the following categories: Either more memory is installed than the system supports or the CMOS settings are incorrect Incompatible or broken modules Improperly installed modules or dirty or defective sockets

## Slide 24
3.9 Memory Troubleshooting:
You should be able to identify memory problems and meanings based on the following errors:
Error | Description
The system boot fails and sounds a beep code | Either no memory is installed or the memory was not detected.
The system boots, but the display remains blank | Either a card or memory module is not seated, or the system includes unsupported memory. Non-parity RAM is incompatible with ECC memory and SDRAM is incompatible with EDO memory.
The system boots, but the memory count is incorrect | The POST failed to recognize all of the memory. This can happen with incompatible memory installation. Remember to avoid combining dual-bank with single-bank memory. If any problem is detected during system boot, check the BIOS settings.
 | Note: The system will only check for memory installed in memory slots on the motherboard. Memory that is on expansion cards or installed on other devices will not be counted and tested.

## Slide 25
3.9 Memory Troubleshooting:
You should be able to identify memory problems and meanings based on the following errors:
Error Messages | Explantion
Memory mismatch error | These messages usually indicate a failing module or discrepancies between new and old memory. Avoid the latter problem by not mixing new and old memory. Ensure that the memory is functioning properly and is compatible with the system. If the memory is good and fully compatible, these error messages could mean that the motherboard has a problem.
Memory parity interrupt at x | 
Memory address error at x | 
Memory failure at x, read y, expecting z | 
o Memory verify error at x | 

## Slide 26
3.9 Memory Troubleshooting:
You should be able to identify memory problems and meanings based on the following errors:
Software errors include: |  | 
Software-generated memory problems | Registry error - Parts of the registry are written to faulty sections of RAM. | 
 | Exception error - A software bug can cause this type of error. | 
 | General-protection fault - A software bug can cause this type of error. | 
 | Page fault - A software bug can cause this type of error. | 
 | Note: | For software errors, check to see if the memory address indicated in the error is consistently the same. If so, check the memory. Otherwise, reboot the system or update the software.

## Slide 27
3.9 Memory Troubleshooting:
You should be able to identify memory problems and meanings based on the following errors: | 
Intermittent problems | One of the tougher detection challenges is the intermittent occurrence of error messages, crashes, or sudden reboots. The trouble in diagnosing this situation is the number of potential problems, including timing, heat, corrosion, fluctuating power, loose connections, EMI, or a combination of these problems.
 | You should be familiar with this list of critical times when memory problems manifest themselves:
 | First boot of a new computer. Memory is not properly seated, missing, or the motherboard is defective.
 | After a memory upgrade. Ensure that the memory is compatible and was installed and configured properly.
 | After software installation. New software requires more memory and can cause problems.
 | After hardware installation or removal. Incompletely or improperly installed hardware can cause errors that appear to be memory related.

## Slide 28
3.10 BIOS / UEFI
You should know the following facts about the UEFI, BIOS, EEPROM, and CMOS:
Component | Description | 
Unified Extensible Firmware Interface) (UEFI) | The UEFI was designed to replace the BIOS. Important things about UEFI are: | 
 | o The UEFI is firmware | 
 | o The UEFI program controls the startup process and loads the operating system into memory. | 
 | o The UEFI design improves the software interoperability and the address limitations of BIOS. | 
 | o The UEFI provides better security to protect against bootkit (malware attacks on the boot process) attacks. | 
 | o The UEFI provides faster startup times. | 
 | o The UEFI supports drives larger than 2.2 terabytes. | 
 | o The UEFI supports 64-bit firmware device drivers. | 
 | o The UEFI is compatible with both BIOS and UEFI hardware. | 
 | o You should check for UEFI updates from manufacturers frequently. Updating the UEFI (called flashing the UEFI) makes new features available. | 

## Slide 29
3.10 BIOS / UEFI
You should know the following facts about the UEFI, BIOS, EEPROM, and CMOS:
Component | Description
Basic Input Output System (BIOS) | The BIOS is a legacy program stored in a read-only memory (ROM) chip that the CPU automatically loads and executes when it receives power. Important things to know about the BIOS are:
 | The BIOS program controls the startup process and loads the operating system into memory.
 | The BIOS is firmware.
 | You should check for BIOS updates from manufacturers frequently. Updating the BIOS (called flashing the BIOS) makes new features available, such as allowing the BIOS to recognize newer hardware devices.
 | Most BIOS chips vary from 265 KB to 1 MB in size.
 | Video cards include a BIOS chip on the device. These devices have their own ROM chip called an optionROM (OpROM).

## Slide 30
3.10 BIOS / UEFI
You should know the following facts about the UEFI, BIOS, EEPROM, and CMOS:
Component | Description
Electrically Erasable Programmable Read Only Memory (EEPROM) | The EEPROM is a RAM chip that replaced the CMOS chip. Important things about EEPROM are:
 | o EEPROM is a type of non-volatile memory used in computers and other electronic devices to store relatively small amounts of data.
 | o EEPROM allows individual bytes to be erased and reprogrammed.
 | o EEPROM replaced EPROM chips and are used for computers BIOSes that were built after 1994.
 | o EEPROM chips allow you to update the BIOS/UEFI in your computer without having to open the computer and remove any chips.

## Slide 31
3.10 BIOS / UEFI
You should know the following facts about the UEFI, BIOS, EEPROM, and CMOS:
Component | Description
Complementary Metal-Oxide Semiconductor (CMOS) | CMOS is legacy computer chip technology that has become a general term used for the program that stores important system information related to the starting of a computer. It is often used synonymously with BIOS. Data held in CMOS includes the hard disk type and configuration, the order of boot devices, and other configurable settings related to the system hardware.
 | The following are important things to know about CMOS: Changing the data stored in CMOS required the use of a CMOS editor program that was part of the BIOS. CMOS used to refer to the real-time clock and the CMOS chip that stored system information. Both were powered by a CMOS battery. Now, the EEPROM chip stores the system information that used to be stored on the CMOS chip. EEPROM requires no power to maintain data storage. The CMOS battery is still used to keep the real-time system clock running when the computer is powered off. It can be a low-voltage dry cell, lithium mounted on the motherboard, or even AA batteries in a housing clipped on a wall inside of the case. The electric current is about 1 millionth of an amp and can provide effective power for years.

## Slide 32
3.10 BIOS / UEFI
You should know the following facts about the UEFI, BIOS, EEPROM, and CMOS:
During the computer's startup procedure, you can press one or more keys to open a CMOS editor so you can change the data stored in CMOS memory. This CMOS setup program is part of the BIOS program. The key or keys you press to open the CMOS editor depend on the BIOS manufacturer. The easiest way to find out which key to press is to read the screen as it boots or to consult the motherboard documentation. The most common keys are Delete, Insert, F1, and F2.
Common reasons for editing the CMOS settings are:
To change the boot device order. To enable or disable motherboard devices. To add a password to the setup program to prevent unauthorized access.
If you set a BIOS/UEFI password and then forget it, you will be unable to edit CMOS settings.
To remove the password for most motherboards, move or remove a jumper, then replace it after a specific period of time.
To configure processor or memory settings (e.g., when you need to set operating speeds or when you want to overclock hardware settings).
(In rare cases) To manually configure device properties for legacy devices.

## Slide 33
3.10 BIOS / UEFI
One of the main jobs of the BIOS/UEFI is to help start the system. The following process is used when you turn a computer on:
1. Power is supplied to the processor. The processor is hard-coded to look at a special memory address for the code to execute.
2. This memory address contains a pointer or jump program which instructs the processor where to find the BIOS program.
3. The processor loads the BIOS program. The first BIOS process to run is the power-on self-test (POST) process. POST does the following: a. Verifies the integrity of the BIOS/UEFI code. b. Looks for the BIOS on the video card and loads it. This powers the video card and results in information being shown on the monitor. c. Looks for BIOS programs on other devices, such as hard disk controllers and loads those. d. Tests system devices, such as verifying the amount of memory on the system.
4. After POST tests complete, the BIOS identifies other system devices. It uses CMOS settings and information supplied by the devices themselves to identify and configure hardware devices. Plug and Play devices are allocated system resources.
5. Then the BIOS searches for a boot drive using the boot order specified in the CMOS.
6. On the boot device, the BIOS/UEFI searches for the master bootloader, then loads the bootloader program. At this point, the BIOS/UEFI stops controlling the system and passes control to the bootloader program.
7. The bootloader program is configured to locate and load the operating system.
8. As the operating system loads, additional steps are taken to load all additional programs and configure devices for use by the operating system.

## Slide 34
3.10 BIOS / UEFI
One of the main jobs of the BIOS/UEFI is to help start the system. The following process is used when you turn a computer on:
From time to time, your PC's manufacturer may release updates to your BIOS firmware.
To update the BIOS, you will need to download the update along with a utility provided by your PC manufacturer that is used to rewrite data stored in the BIOS chip.
This process is called flashing the BIOS.
The actual steps you should follow to flash the BIOS will vary by manufacturer.
Note: You should connect your PC to a UPS before flashing the BIOS. If a power outage occurs during the flash process, it will irrecoverably damage the BIOS and prevent your system from booting.

## Slide 35
3.11 Expansion Cards: & 3.11.2 Expansion Bus Types:
Expansion cards are used to expand a computer's functionality or increase its performance. Expansion cards are installed into the expansion slot on a motherboard.
Expansion cards and slots use different expansion bus standards that define communication specifications as well as physical characteristics.
The following table describes the characteristics of the most common expansion bus types:
Bus Type | Characteristics
Peripheral Component Interconnect (PCI) | PCI was developed to replace the obsolete ISA and VESA bus standards. PCI:
 | o Is processor independent, meaning the CPU and PCI bus can process concurrently
 | o Supports plug and play, meaning installed devices are detected and configured automatically
 | o Used by devices such as sound cards, modems, network cards, and storage device controllers
 | o Can run at 33 MHz and transfer data at 133 MB/s or run at 66 MHz and transfer data at 266 MB/s

## Slide 36
3.11 Expansion Cards & 3.11.2 Expansion Bus Types:
Expansion cards are used to expand a computer's functionality or increase its performance.
Expansion cards are installed into the expansion slot on a motherboard.
Expansion cards and slots use different expansion bus standards that define communication specifications as well as physical characteristics.
The following table describes the characteristics of the most common expansion bus types:
Bus Type | Characteristics
PCI Extended (PCI-X) | PCI-X was built on existing the PCI architecture and aimed to overcome standard PCI bandwidth limitations. PCI-X:
 | o Uses a 64-bit interface to achieve faster data speeds
 | o Operates at 133 MHz, resulting in data rates of 1.06 GB/s
 | o Is typically used by servers for network cards or Fibre Channel adapters
 | o Is backwards compatible with standard PCI slots (i.e., a PCI-X card can be installed in a standard PCI slot)
 | Note: When installed in a standard PCI slot, PCI-X cards are throttled down to standard PCI speeds.

## Slide 37
3.11 Expansion Cards & 3.11.2 Expansion Bus Types:
Bus Type | Characteristics | 
PCI Express (PCIe) | PCIe was developed to replace PCI, PCI-X, and AGP. Instead of a shared bus, each PCIe slot links to a switch that prioritizes and routes data through a point-to-point dedicated connection and provides a serial, full-duplex method of transmission. PCIe uses several different connection types | 
 | PCI Extended types are defined by the number of transmission lanes that are used to transfer data. For example, PCIe x1 provides one lane for transmission (x1), while PCIe x16 provides sixteen lanes for transmission. PCIe defines x2, x4, x8, x16, and x32 connection types. | 
PCIe data rates depend on the protocol version and number of transmission lanes: |  | 
1.0: 250 MB/s (x1); 4 GB/s (x16) 2.0: 500 MB/s (x1); 8 GB/s (x16) 3.0: 1 GB/s (x1); 16 GB/s (x16) 4.0: 2 GB/s (x1); 32 GB/s (x16) |  | PCIe cards are cross-size compatible, as long as the slot size is the same or larger than the card size. For example, a PCIe x1 card can be installed in a PCIe x16 slot, but a PCIe x16 card cannot be installed in a PCIe x1 slot.
In addition to greatly increased speed, PCIe offers higher quality service. |  | 
PCIe can run alongside legacy PCI technology (i.e., both PCIe and PCI buses can be in the same system). |  | 
PCIe x1 slots are typically used for network cards, USB cards, and sound cards. PCIe x16 slots are primarily used for dedicated video cards. |  | 

## Slide 38
3.11 Expansion Cards:
3.11.2 Expansion Bus Types:
Bus Type | Characteristics | 
Mini PCI | Small form factor computers (e.g., laptops or Mini-ITX systems) might include a Mini PCI slot, which has either 100 or 124 pins and accepts Mini PCI cards. A typical use for a Mini PCI slot is to add internal cards (such as wireless cards) to laptops. | 
Legacy buses | Buses that have been replaced by newer types are considered legacy buses. Legacy buses are rarely used and include the following: | 
 | AGP | (accelerated graphics port) was a dedicated bus type used by dedicated video cards.
 | AMR | (audio/modem riser) was a riser card that attached to the motherboard and allowed additional cards (called daughter cards) to be installed.
 | CNR | (communications network riser) was a riser card slot that allowed for installing network, sound, or modem functions.

## Slide 39
3.12 Video Cards:
Video cards process graphical information for output to an external display. Video cards can be implemented as a dedicated expansion board or integrated with other components (e.g., the motherboard or CPU). | 
Dedicated video cards: a. Are installed in an expansion slot on the motherboard b. Have a GPU and a dedicated, high-speed video memory bank c. Are more powerful than integrated video cards, but are also more expensive | 
Integrated graphics: a. Integrate the GPU with another hardware component (e.g., a motherboard or CPU) b. Share system memory for graphic processing c. Are much cheaper than dedicated video cards, but are also less powerful | 
Note: | Intel CPU chips tend to have integrated graphics, whereas AMD usually requires a dedicated video card.

## Slide 40
3.12 Video Cards:
When selecting a video card, keep in mind the following characteristics:
Characteristic | Description
Display connectors | Video cards have one or more connectors for attaching an external display. Always try to select a video card with connectors that match your display
 | o VGA monitors use a VGA (DB-15) connector. o LCD and LED monitors use one (or more) of the following connectors: a. DVI-Integrated (DVI-I) connector b HDMI connector (also used by HDTVs) c. DisplayPort connector
 | DVI-I connectors are able to send either analog or digital signals. Older video cards might use DVI-A (analog) or DVI-D (digital) connectors.
 | Some video cards have dual heads (two output connectors capable of displaying video simultaneously) and are able to support dual monitors.
 | Note: If necessary, you can use special connector adapters to convert from one connector type to another (e.g., DVI to HDMI). However, it's usually best to match the connector type of the video card with the display connectors.

## Slide 41
3.12 Video Cards:
When selecting a video card, keep in mind the following characteristics:
Characteristic | Description | 
Display Quality | The quality of images and animations is determined by both the video card and the external display. | 
 | When selecting a video card, the following specifications should be considered: | 
 | The resolution is the number of pixels displayed on screen. A higher resolution means that more information can be shown on the screen. A video card is rated by its max resolution, which is the highest possible resolution it can display (e.g., 1920 × 1080 or 4096 × 2160). | 
 | The refresh rate is the number of times in one second that the GPU draws a frame. Refresh rates are measured in hertz. A refresh rate of 70 Hz or lower may cause eye fatigue. An optimal refresh rate is between 75 Hz and 85 Hz. | 
 | Note: | For optimal image quality and graphic performance, it is best to select a display that matches the video card specifications, and vice versa.

## Slide 42
3.12 Video Cards:
When selecting a video card, keep in mind the following characteristics:
Characteristic | Description
Processing Capabilities | The graphics processing unit (GPU) handles all video rendering tasks. GPUs are much more efficient at processing graphic data than a traditional CPU.
 | o Using the GPU to render graphics is often referred to as video hardware acceleration.
 | o Settings in the operating system can be used to control how much video processing is offloaded to the GPU.
 | o GPUs have a clock speed that is rated in MHz. A higher speed means better performance.

## Slide 43
3.12 Video Cards:
When selecting a video card, keep in mind the following characteristics:
Characteristic | Description | 
Memory | Dedicated video cards use high-speed memory to store graphic data. The amount of memory on the card affects performance as well as other characteristics. | 
 | The amount of memory on a card can be as low as 512 MB or as high as 16 GB. | 
 | Dedicated video cards use the following types of memory: | 
 | DDR, DDR2, and DDR3 memory are similar to system memory. This type of memory is cheaper, but provides less performance features than special graphics memory. | 
 | GDDR2, GDDR3, and GDDR5 are DDR memory specifically designed and optimized for graphical data. This memory is more expensive, but results in better performance. | 
 | Note: | Integrated graphics (onboard video cards) share system memory with the CPU for video processing.

## Slide 44
3.12 Video Cards:
When selecting a video card, keep in mind the following characteristics:
Characteristic | Description | 
Bus Type | Video cards must be compatible with the expansion slots on the motherboard. | 
 | Common slot types used by video cards include the following: PCIe x16 PCI AGP and VESA (used by older video cards) | 
 | Note: | Motherboards with integrated graphics embed the functionality with the buses on the system (e.g., PCIe, AGP, or PCI).

## Slide 45
3.12 Video Cards:
When selecting a video card, keep in mind the following characteristics:
Characteristic | Description | 
Multi-GPU | Some video cards can be linked together and share the graphic processing load between the two GPUs | 
 | Multi-GPU configurations are manufacturer-specific: NVIDIA uses SLI (Scalable Link Interface). 2. AMD uses CrossFire. | 
 | Video cards are linked using a special bridge clip or through software (depending on the implementation). | 
 | The motherboard and each video card must use the same connection method (SLI or CrossFire). The motherboard must also have multiple PCIe x16 slots. | 
 | In most cases, both video cards must be identical. | 
 | Note: | Some motherboards allow you to link an integrated graphics controller with a video card installed in the expansion slot; however, this offers a negligible performance boost.

## Slide 46
3.12 Video Cards:
When selecting a video card, keep in mind the following characteristics:
Characteristic | Description
HDMI Audio | HDMI cables are able to carry both video and audio signals; however, most video cards only send a video signal.
 | The following techniques can be used to send an audio signal through the video card:
 | A graphics card with an onboard audio processor can decode and process audio and send it out the HDMI port. This option is often referred to as onboard sound.
 | With audio pass-through, an audio output cable is connected to the video card. The video card combines the audio signal with the video signal for HDMI output. This option is often called HDTV out.

## Slide 47
3.12 Video Cards:
When selecting a video card, keep in mind the following characteristics:
Characteristic | Description
DirectX/OpenGL | DirectX is a collection of application program interfaces (APIs) that improves graphic, animation, and multimedia creations.
 | DirectX includes multiple components targeted to a different aspect of multimedia. For example, Direct3D is the 3D rendering component of DirectX.
 | Applications (typically games) are written using features included in specific DirectX versions.
 | To view content written to a specific DirectX version, your video card must also support that (or a higher) version.
 | OpenGL is an alternative standard to DirectX that is used by some applications. Most video cards support both DirectX and OpenGL.

## Slide 48
3.12 Video Cards:
When selecting a video card, keep in mind the following characteristics:
Note: Video capture for digital sources can also be done through a FireWire connection or today a USB connection.
Characteristic | Description
TV Input/Output | Some video cards include features that allow them to receive video signals and output them to a TV source.
 | You can display the computer screen on a TV using the following methods: Analog TVs use an S-video port for video input. Digital TVs use the HDMI port for input. Some TVs have a VGA or DVI input.
 | Video input allows your video card to accept a video signal from an external source (e.g., a DVD player or an external TV tuner box) and display it on the monitor.
 | A TV tuner allows your video card to accept a cable TV input and change channels from within the computer. TV tuners can process one or more of the following signals: NTSC, PAL, and SECAM are analog TV signal standards. NTSC was used in North America but is being phased out. ATSC signals are digital TV signals. When purchasing a new TV tuner, make sure it supports ATSC.
 | Most TV tuners use an S-video, F-type, or RCA composite port for video input.
 | A video capture card allows you to record the video signal that is coming into the computer from an external source. For example, you would use a video capture card to create digital copies of home movies stored on an analog tape, or a TV tuner with video capture would allow you to record TV shows. A video capture card might include both video and audio inputs.

## Slide 49
3.12 Video Cards:
When selecting a video card, keep in mind the following characteristics:
Characteristic | Description
High-bandwidth | HDCP is a method for protecting digital media. The purpose of HDCP is to prevent the interception and copying of protected data streams as they are sent from a playback device to a display device (e.g., from a DVD player to an HDTV).
 | When playing protected content from a PC, the DVD player, video card, and display device must all support HDCP.
 | o If you plan on watching protected content on your PC, or playing content from your PC to an external TV, make sure the video card supports HDCP.

## Slide 50
3.12.4 Video Card Installation:
Use the following process to install a dedicated video card: | 
Video cards must be compatible with the expansion slots on the motherboard. If the motherboard has integrated graphics, disable it in the CMOS configuration when installing a dedicated video card. Install the video card in the first open expansion slot. If using a multi-GPU configuration (SLI or CrossFire): Install the secondary video card in the next open expansion slot. Link the two video cards together using the bridge clip. Connect any additional power connectors to the video card(s) (e.g., 6-pin or 8-pin auxilary power). | 
Note: | Some motherboards have an additional power connector near the expansion slots that are used with multi-GPU configurations.
o Connect the external display to the video card using the appropriate cable. When using a multi-GPU configuration, connect the monitor to the primary (first) video card. o After installing the video card and making all necessary connections, turn on the computer. o In the operating system, install the video card drivers. o If using a multi-GPU configuration, install all necessary configuration software. | 

## Slide 51
3.13 Audio Cards:
A sound card is an expansion card (or an integrated component on the motherboard) that manages sound input and output. |  | 
Because computers use digital data, sound cards must convert: |  | analog sound into digital data
 |  | digital data into analog sound.
The following components are used to do this: |  | 
Analog-to-Digital Converter (ADC) | converts analog sound into digital data. | 
Digital Signal Processor (DSP) | is an onboard processor that handles analog and digital conversion. | 
Digital-to-Analog Converter (DAC) | converts digital data into analog sound (in preparation to be played on speakers). | 

## Slide 52
3.13 Audio Cards:
When purchasing a sound card, be aware of the following considerations:
Component | Description | 
Bus support | Sound cards can be installed via an expansion slot (e.g., PCI or PCIe x1) on the motherboard. When selecting a sound card, make sure the bus type is compatible with your motherboard. | 
 | Note: | Most new motherboards have an onboard sound card.
Channels | Audio can be split into multiple channels, which increases the sound quality and makes it more realistic. | 
 | Some standard channel configurations are as follows: | 
 | 2 channel audio is stereo. Examples of 2 channel audio include standard TV and radio. 4 channel audio is quadraphonic audio and was an early attempt at surround sound. 5.1 channel audio, also known as surround sound, has 6 audio channels: five speakers and one low-frequency effects subwoofer (LFE) channel. 7.1 channel has 8 audio channels: 7 speakers and one LFE subwoofer channel. This is the first technology providing error correction | 

## Slide 53
3.13 Audio Cards:
When purchasing a sound card, be aware of the following considerations:
Component | Description
Sampling Rate | The sampling rate is the number of analog signal samples taken in over a period of time. Sample rates are expressed in cycles per second, called hertz (1,000 hertz (Hz) = 1 kilohertz (kHz)). A high sampling rate gives a more accurate representation of the sound.
 | Examples of different sampling rates include:
 | 8 kHz (telephone) This is adequate for conversation because the human voice's full range is about 4 kHz. 22 kHz (radio quality) 44 kHz (CD quality) This sample rate can accurately reproduce the audio frequencies up to 20,500 hertz, covering the full range of human hearing. 48 kHz (Digital TV, DVD movies) 96 kHz (DVD audio) 192 kHz, used by: LPCM (Linear Pulse Code Modulation), a DVD-music production format BD-ROM (Blu-ray Disc-ROM)

## Slide 54
3.13 Audio Cards:
When purchasing a sound card, be aware of the following considerations:
Component | Description | 
Sampling Rate | The sampling rate is the number of analog signal samples taken in over a period of time. Sample rates are expressed in cycles per second, called hertz (1,000 hertz (Hz) = 1 kilohertz (kHz)). A high sampling rate gives a more accurate representation of the sound. | 
 | Examples of different sampling rates include: | 
 | Higher sample rates require more bits of data per sample: 8-bit sound cards use a sampling size of 256. 16-bit sound cards use a sampling size of 65,536. 20-bit sound cards use a sampling size of 1,048,576. 24-bit sound cards use a sampling size of 16,777,216. 32-bit sound cards use a sampling size of 4,294,967,296. | 
 | Note: | The bit portion of a sound card's sampling size does not correspond with the bus size.

## Slide 55
3.13 Audio Cards:
When purchasing a sound card, be aware of the following considerations:
Component | Description |  | 
 | Additional features on sound cards provide higher quality sound or additional functionality |  | 
Feature Support | DirectSound 3D | allows a computer to play audio in surround sound. | 
 | EAX | is a high-definition sound technology originally developed for video games. | This technology provides such realistic nuances that audio can actually cue gamers.
 | THX | is a sound quality standard, originally created for film, now available on sound cards. | This is a sound card feature that allows computers to present theater quality sound output.
 | Dolby Digital | is a technology that broadcasts sound at a frequency the human ear can hear and diminishes collateral sound. | This is a sound card feature that allows computers to present higher quality sound output.
 | DTS | (Digital Theater Systems) Digital requires an optical reader to decode physical data and send it to a computer for processing. | This is a sound card feature that allows computers to present theater quality sound output.
 | SDDS | (Sony Dynamic Digital Sound) was originally developed for theater sound. | SDDS decoders provide error correction.
 | MIDI | (Musical Instrument Digital Interface) is a protocol for recording and playing audio created on digital synthesizers. | This feature allows the computer to become an integrated component to a musical instrument.

## Slide 56
3.13 Audio Cards:
When purchasing a sound card, be aware of the following considerations:
Component | Description | 
Analog Input and Output | Analog output jacks allow you to play sound on your computer through external devices: | 
 | The speaker out connector sends signal to external speakers. This signal is amplified and the computer controls the sound level that is sent. | 
 | The line out connectors send audio to other sound devices. This signal is unamplified. | 
 | Note: | Analog input jacks allow you to record audio through the sound card.
 | The line-level (line-in) connector receives signals from CD players and musical instruments coming from the line out port of the other device. | 
 | The mic-level (mic in) connector receives signals from a microphone. | 

## Slide 57
3.13 Audio Cards:
When purchasing a sound card, be aware of the following considerations:
Component | Description
Digital Audio | Most audio devices, such as stereo consoles, TVs, and speakers require analog audio. Newer devices, such as some CD players, DVD players, and HDTVs, are capable of processing digital audio signals.
 | Digital audio support in a sound card:
 | Allows you to play digital audio directly from an internal CD player
 | Allows for compression of audio data to support Dolby Digital or DTS surround sound
 | Can use fiber optic cables to eliminate electrical interference

## Slide 58
3.13 Audio Cards: Continued
When purchasing a sound card, be aware of the following considerations:
Sound cards support digital audio in the following ways:
An internal connector on the sound card connects to a digital audio output connector on a CD/DVD drive. Through this connection, you can play CDs directly through the sound card.
An internal connector on the sound card sends HD audio, such as from a DVD or Blu-ray disc, to an audio pass-through on a video card. This allows the HD audio signal to be combined with the video signal through an HDMI connector.
Sony/Philips Digital Interface Format (S/PDIF) is a consumer standard for digital audio. These are either optical or coaxial external connectors and allow input and output between other digital audio-capable devices.

## Slide 59
3.13 Audio Cards:
When purchasing a sound card, be aware of the following considerations:
Sound card drivers and other software save digital audio into several different file types. Common file types include: | 
WAV | (Windows standard), a widely used and compatible file type
AIFF | (Audio Interchange File Format), the Macintosh equivalent of the WAV
AU | (UNIX standard), supported by most web browsers
MP3 | (MPEG-2 Layer III), a highly effective audio compression standard
AAC | (Advanced Audio Coding), also known as MPEG-2, a compression expected to replace MP3
WMA | (Windows Media Audio), a highly compatible standard developed to compete with Real Audio
MIDI | not a true audio file, but contains data to reproduce sounds through electronic synthesis
Component | Description
Additional Ports | In addition to audio input and output ports, some sound cards also include the following ports:
 | MIDI port to interface with MIDI sound devices FireWire Some high-end audio cards include HDMI video processors and video output, combining the features of an audio card with a video card. The sound card might have 1 or 2 HDMI ports (for input and/or output).

## Slide 60
3.13.6 Sound Card Connectors:
Sound cards provide input and output (I/O) ports for connecting external, audio-related devices to the computer. The most commonly found ports are described in the following table:
Port | Description |  |  | 
Mini TRS | Mini TRS ports on the sound card accept 3.5mm plugs for analog audio I/O. The number of ports on the sound card depends on the type of I/O support (e.g., the number of speaker channels, microphone, or line in support). |  |  | 
 | Ports are often labeled with text or graphics to identify its function. Standardized color coding might also be helpful in determining the proper connection. |  |  | 
 |  | Pink |  | Mic in (mic-level)
 |  | Light blue |  | Line-in (line-level)
 |  | Lime green |  | Line out (front speakers or headphones)
 |  | Black |  | Line out (rear speakers)
 |  | Orange |  | Line out (center and subwoofer)
 | Note: |  | Although these colors are standard, be sure to consult the sound card documentation for specific details. | 

## Slide 61
3.13.6 Sound Card Connectors:
Sound cards provide input and output (I/O) ports for connecting external, audio-related devices to the computer. The most commonly found ports are described in the following table:
Port | Description
TOSLINK | A TOSLINK (or optical audio cable) connector is used with digital optical I/O for S/PDIF audio.

## Slide 62
3.13.6 Sound Card Connectors:
Sound cards provide input and output (I/O) ports for connecting external, audio-related devices to the computer. The most commonly found ports are described in the following table:
Port | Description
RCA | An RCA connector on a sound card is used for coaxial digital I/O for S/PDIF audio
 | Note: While RCA connectors can be used for analog audio, RCA connectors on a sound card are normally used for S/PDIF digital audio.

## Slide 63
3.13.6 Sound Card Connectors:
Sound cards provide input and output (I/O) ports for connecting external, audio-related devices to the computer. The most commonly found ports are described in the following table:
Port | Description
IEEE 1394 | Some sound cards include one or more IEEE 1394 (FireWire) ports. These ports function as normal IEEE 1394 ports. (runs at 400 or 800 M/bps)
 | Note: Apple calls this technology Firewire, whereas Sony calls it iLink.

## Slide 64
3.13.6 Sound Card Connectors:
Sound cards provide input and output (I/O) ports for connecting external, audio-related devices to the computer. The most commonly found ports are described in the following table:
Port | Description
HDMI | A sound card with an HDMI port is capable of sending HD audio to an HDMI device.
 | Some sound cards are able to output video or combine a video signal from a video card and output the combined audio/video signal through the HDMI port.

## Slide 65
3.14 System Cooling:
The normal operation of computer components produces heat. Overheated components can cause intermittent errors and reduce component life. If components are overheated for an extended period of time, they will fail. To keep component temperatures optimal, computer cases maintain a consistent, one-way flow of air through the case. The following diagram shows how air should flow through a computer case:

## Slide 66
3.14 System Cooling:
Because proper airflow is necessary to keep components cool, consider the following recommendations to ensure optimal system cooling:
Keep the case free of dust and debris. Excess dust can restrict airflow and prevent proper heat transfer.
Reduce the number of airflow obstructions. Employ proper cable management (e.g., bundle cables together and secure unused cables to the case). Space out multiple hard disk drives instead of stacking them next to each other. Do not use an excess number of expansion cards.
Maintain appropriate ambient temperatures. Optimal ambient temperatures are between 60 and 80 degrees Fahrenheit. For server rooms, the ambient temperature might be as low as 45 degrees.
Ensure proper ventilation. Keep air intakes and exhausts free from obstructions. Leave space between the computer and any walls or desks.
Preserve negative pressure inside the case by keeping all covers and shields installed (e.g., unused expansion cards, I/O shield, front drive bays).

## Slide 67
3.14 System Cooling:
The following table identifies several components that are used to help regulate a computer system's internal temperature:
Component | Description
Case Fans | Case fans create a pressurized system that allows air to flow through the case in a specific way.
 | o Intake fans (at the front) pull air inside the case to cool components. o Outtake fans (at the back and top) exhaust warm air from inside the case. o Some cases have intake fans on the side case cover. o Fan filters can be installed to keep dust and debris inside the case to a minimum.
Power Supply | ATX power supplies aid in cooling by exhausting hot air out the back of the case.

## Slide 68
3.14 System Cooling:
The following table identifies several components that are used to help regulate a computer system's internal temperature:
Component | Description
Heat Sink | Heat sinks are made of a heat conductive material (usually aluminum or copper) and are attached to components using a thermal paste or pad. Heat sinks are designed with fins to increase the surface area exposed to air, allowing heat to dissipate from the component much faster. Heat sinks can be either active or passive.
 | o Active heat sinks have an attached fan that helps cool off the component at a faster rate. Active heat sinks are used with the following components: a. CPUs b. High-end video cards c. Some motherboard chipsets with integrated graphics
 | o Passive heat sinks do not have a fan and instead rely on increased surface area and passive air movement to cool the component. Passive heat sinks are used with the following components: a. Most motherboard chipsets b. Low-end video cards c. Memory modules (heat sinks on memory modules are also called heat spreaders)
 | Note: Because passive heat sinks do not use a fan, they are 100% reliable. However, active heat sinks can dissipate heat much faster than passive ones.

## Slide 69
3.14 System Cooling:
The following table identifies several components that are used to help regulate a computer system's internal temperature:
Component | Description
Heat Sensors | Most motherboards include the following heat sensors:
 | CPU sensor (located on the circuit board underneath the processor) System case sensor (located either on the motherboard or on a cable attached to the motherboard) Room temperature sensor (usually connected to the motherboard by a cable and mounted on a case slot)
 | Special software can monitor the temperature levels and be configured to send warnings when high temperature conditions exist. The BIOS in most motherboards can also be configured to automatically shut the system down when a specified thermal threshold is exceeded.

## Slide 70
3.14 System Cooling:
The following table identifies several components that are used to help regulate a computer system's internal temperature:
Component | Description | 
Liquid | Cooling | Liquid cooling systems are used when air cooling is not sufficient. Liquid-based cooling systems are composed of tubes, cooling plates, a reservoir, and a radiator. Cooling plates have tubes connected to them and are attached to components. Liquid coolant is then circulated through the system, cooling it. Because liquid cooling can dissipate heat much faster than air cooling, it is primarily used for high-end gaming computers and high-performance systems.
Note: | Issues related to insufficient cooling are sometimes difficult to identify. | 
 | They usually manifest as random errors or system lockups. | 
 | One tool that can be used to troubleshoot cooling problems is freeze spray. | 
 | If a system is starting to fail due to overheating, spraying it with freeze spray reduces the temperature and could restore it to normal functionality. | 
 | If the problem goes away after spraying a suspected component, implement additional cooling solutions for that component. | 
- END of CLASS 4 - |  | 

## Slide 71
End of CIS101A Class Session 4