## Slide 1: Week 1
CIS101B - 1002

## Slide 2: Command Line
Linux is an open source operating system. You can even create your own custom version of Linux called a distribution. Some of the more popular Linux distributions include openSUSE, Fedora, and Ubuntu.
Like Windows, Linux provides two different user interfaces. There is a a graphical interface where you can click on things with a mouse and make selections to bring up applications. There is also a command line interface called the shell that allows you to enter commands at the shell prompt to manage the system. The command line interface is consistent across all distributions of Linux. Each Linux distribution uses a slightly different graphical user interface. If you learn how to manage Linux systems from within a shell, then you can manage just about any Linux distribution.
The shell is often referred to as the bash (Bourne-again shell) shell.
A superuser in Linux is equivalent to an administrator in Windows.
Linux has two especially important features, command history and command completion. Command history saves commands entered at the shell prompt. The command completion feature tries to guess a command you are entering and will complete the command for you if you press the TAB key.

## Slide 3
pwd | Displays the path of the current directory on the screen. pwd stands for print working directory.
ifconfig | Displays the IP address and the subnet mask assigned to this system.
ls | Displays a list of files and subdirectories that exist within a directory. Several options are commonly used with this command: -a displays all files, including hidden files. -l displays a detailed (long) listing of directory contents including ownership, permissions, modification dates, and file sizes. -R displays the contents of the directory and all of its subdirectories.
--help | Displays a brief summary of how to use the command.
bash | Starts a new Bourne-again shell (bash) session.
man | Displays the manual page for a command. It's very similar to the help screen, but it provides more detail. Use the Qkey to quit and go back to the shell prompt.
Linux Commands

## Slide 4
Linux Commands
info | Displays more extensive documentation about the command. Use the Q key to quit and go back to the shell prompt.
cd | Changes directories in the file system. For example, to change to the /home directory in the file system, you would enter cd /home at the shell prompt.
cp | Copies files and directories from one location in the file system to another. For example, to copy the widget.odt file to the /home/rtracy directory, you would enter cp widget.odt /home/rtracy at the shell prompt. To copy an entire directory structure, include the -R option, which specifies that the directory contents be recursively copied.
mv | Moves files and directories from one location in the file system to another. For example, to move the widget.odt file to the /home/rtracy directory, you would enter mv widget.odt /home/rtracy at the shell prompt.
rm | Deletes files and directories from the file system. For example, to delete the widget.odt file, you would enter rm widget.odt at the shell prompt.
cat | Displays the contents of a text file on the screen. For example, to view the contents of the widget.txt file, you would enter cat widget.txt at the shell prompt.
less | Displays the contents of a text file on the screen, pausing the output one screen at a time. For example, to view the contents of the widget.txt file one page at a time, you would enter less widget.txt at the shell prompt.
head | Displays the first few lines of a text file on the screen. For example, to view the first lines of the widget.txt file, you would enter head widget.txt at the shell prompt.
tail | Displays the last few lines of a text file on the screen. For example, to view the last lines of the widget.txt file, you would enter tail widget.txt at the shell prompt. The -f option can be used with tail to monitor a file for changes. If new content is added to the end of the file (such as a log file), the new lines will be displayed on the screen.

## Slide 5
Linux Commands
vi | Edits the contents of a text file. The vi uses four different operating modes: Command mode Command-line mode Insert mode Replace mode For example, to edit the contents of the widget.txt file, you would enter vi widget.txt at the shell prompt. You would then press the i key to enter Insert mode and make the necessary changes to the file. When done editing the file, you would press the Esc key to enter Command mode. Then you would press the : key to enter command-line mode where you would enter exit to save your changes and exit the vi editor.
su | Allows you to switch user accounts. su - (su with a space and a hyphen) is used to switch to the root user with the home directory and environment variables assigned to the root user.
shutdown | Shuts down or reboots the system in a secure manner. The syntax of the shutdown command is shutdown -h¦-r +m message. The options for the shutdown command include: +m specifies when to perform the shutdown operation. m is the amount of time is specified in minutes. -h instructs the system to shut down and power down. -r instructs the system to reboot after the shutdown. -p powers off the machine. message specifies a message that is sent to all users that accompanies the standard shutdown notification.

## Slide 6
Mac OS is a proprietary closed-source operating system. Mac OS uses the HFS Plus (HFS+) file system. HFS stands for Hierarchical File System and is the primary file system used by Mac OS.
Apple devices have several features that are unique to the Mac OS. The following table describes some of these features.

## Slide 7
Gestures | Gestures are specific finger motions that are used to perform a specific function on a Mac OS system. They are used by Apple systems that use an Apple Multi-Touch trackpad, a Magic Mouse, or a touchscreen. Below are just some of the gestures that are available on Mac OS: Right-click: Tap with two fingers to right-click. Smart zoom: Double-tap with two fingers to zoom in on a web page, image, or document (double-tap again to zoom out). Scroll: Slide up or down using two fingers to scroll up or down. Zoom: Spread two fingers apart to zoom in. Bring fingers back together to zoom out. Page navigation: Slide two fingers left or right to navigate between pages in a document. Mission Control: Slide four fingers straight up to open Mission Control. All apps: Slide four fingers straight down to display all windows of the active app.
Remote Disc | Because many modern Apple devices are being manufactured without a CD or DVD installed, Mac OS offers the Remote Disc feature. With Remote Disc: The CD or DVD can be shared on the network. Devices on the same network can access the shared remote CD or DVD. Only data CDs and DVDs can be accessed. Media discs such as audio CDs, Blu-ray and DVD movies, or installation discs cannot be accessed remotely.

## Slide 8
Boot Camp | Boot Camp is a Mac OS feature that allows an Apple device to install the Microsoft Windows OS. Boot Camp makes installing Windows a very simple process by using the Boot Camp Assistant app. The Boot Camp Assistant: Automatically creates a BOOTCAMP partition on the hard drive and prepares it for installing Windows. Reboots the system and starts the Windows install process from the selected installation media. Creates a Boot Camp system tray icon in both Mac OS and the Windows installation to switch between the Windows and Mac OS installation. Boot Camp has the following system requirements: Intel-based Mac Installation media containing 64-bit version of Windows 8 or later 55 GB of free space
System Preferences | System Preferences is the utility used to change settings for nearly every aspect of Mac OS. Settings are grouped by category and can be accessed by selecting the category icon. Each category has multiple tabs or dialogs that are used to change different system settings. The search box can be used to search for the location of a specific setting.
Mission Control | Mission Control is a desktop and windows management utility used to access several Mac OS features. Multiple Desktops - At the top of Mission Control is the Multiple Desktops feature that is used to manage and navigate between multiple desktops. All Windows - When activated, Mission Control tiles all application windows on the screen and groups multiple windows from the same application together. Dashboard - From Mission Control, the Dashboard containing Mac OS widgets can be accessed.

## Slide 9
Keychain | Keychain is Mac OS's password management utility. Keychain can hold password-protected data for the following categories: Passwords (including passwords for websites, system logins, wireless networks, encrypted disks) Private keys Certificates Secure notes In order to access information contained in Keychain, the system administrator password must be provided.
Spotlight | Spotlight is an indexing utility that can perform system-wide searches to locate folders, files, apps, and internet results that contain the specified search phrase. Spotlight is access pressing Command(⌘)+Spacebar or by selecting the Spotlight icon on the Status menu.
Dock | The Dock is the main taskbar in Mac OS. The Dock is used to launch apps, switch between running apps, access the Trash, and access specific folders. Dock settings can be accessed in System Preferences or by right-clicking the Dock and selecting Dock Preferences. Apps and folders can be pinned to the Dock for quick access. Running apps on the Dock have an illuminated dot below them.
Force Quit | Force Quit is used to stop non-responsive processes and applications. It can also be used to restart the Finder service. Force Quit can be accessed from the Apple menu or the keyboard shortcut Command+Option+Esc.
Terminal | Terminal is Mac OS's command line interface utility. It is similar to the terminal used in Linux systems. Terminal: Uses many of the same commands as the Linux terminal. Can be used to perform system management tasks, such as deleting files, changing permissions, etc. Is an excellent troubleshooting tool.

## Slide 10: MAC Special Keys
The Command (⌘) key is the primary modifier key on Apple systems. For example, Command+C copies the selected item to the clipboard, and Command+V pastes the contents of the Clipboard.
When used in a Boot Camp Windows installation, the Command key serves the same function as the Windows key.
The Option (⌥) key is used for application shortcuts and navigation shortcuts. For example, Option+Right/Left Arrow navigates between words in a text document.
When used in a Boot Camp Windows installation, the Option key serves the same function as the Alt key.
The Control (^) key is primarily used for text document navigation. For example, Control+H deletes the character to the left of the cursor. The Control key can also be used in conjunction with other keys to perform system tasks. For example, Command+Control+Power button forces the Mac OS to restart.
When used in a Boot Camp Windows installation, the Control key serves the same function as the Ctrl key
The Fn key is typically only found on Apple notebooks and is used to access the F1–F12 keys on the keyboard. It can also be used to access the special icon function on particular keys

## Slide 11
Make a Good First Impressions
  Arrive to appointments on time and prepared. If you are going to be late, contact the client and let them know.
  Dress professionally and following any company dress codes. This includes appearing well-groomed.
  Greet the client and introduce yourself.
  Ask permission before entering the client's office or home.
  Address the client using the appropriate title.
  Be sensitive to cultural differences between the two of you.
  Use clear, concise, and direct statements.
  Ask the client open-ended questions so the client will talk about the issue and you can gather information.
  Allow the client to speak and avoid interrupting.
  Clarify client statements—restate what the client said and ask pertinent questions.
  Take notes on complicated or important information.
  Avoid using jargon, abbreviations, and acronyms. Take time to explain technical terms and issues in a simple way.
  Clearly explain the problem and any repair options. Be sure to explain the advantages, disadvantages, and cost of a repair.
  Set realistic expectations for finishing work—when in doubt, overestimate
Communicate Effectively

## Slide 12
Show Respect
  Never argue with a client or become defensive.
  Avoid accusing the client. Even if the client caused the problem, do not point fingers.
  Ask before moving items on desks or making changes to computer systems.
  Stay calm and avoid being judgmental or insulting.
  Avoid distractions or interruptions, including texting and social media notifications. Don't take personal phone calls. Ask permission before taking work-related calls.
  Do not browse files on computers that are not necessary or related to the repair and never complain about clients on social media platforms
Being Professional
Get authorization to proceed before making any unexpected repairs or fixing items that were not part of the original problem, especially if the extra repairs result in an additional charge.
After you have fixed the problem, try it out (or let the client try it out) to make sure that other problems don't exist.
After the repairs are finished, provide the client with a detailed invoice of the work performed. Also include any manuals or documentation related to new hardware.
Ask the client if they would like to keep the failed components.
If necessary, take the time to briefly explain any new software or hardware that was installed.
If applicable, offer additional services or training that might be beneficial to the client.
If the problem is related to user error or is caused by actions taken by the client, tactfully explain the problem without accusing or judging the client.
Before leaving, make sure the client is satisfied that the problem has been resolved. For best client service and based on your company policy, follow up with the client at a later time to verify that the problem remains fixed.
If a request is outside of your ability or responsibility, help the client get in contact with the appropriate resources, such as another technician or an authorized manager

## Slide 13: HVAC – Interference
Heating, Ventilation, and Air Conditioning (HVAC) | For computer components, design HVAC systems with the following in mind: Keep temperature between 70 and 74 degrees to prevent components from overheating. Keep humidity between 40 and 70 percent to prevent electrostatic discharge (ESD). Make sure server rooms have separate ducting or HVAC systems from the rest of the building for better temperature control. Use positive pressure systems. Positive pressure systems protect the air quality in the facility by causing air to be forced out through doors, windows, and other openings. Negative pressure systems draw air in, potentially bringing in airborne particles such as dust or smoke. Positive pressure systems are more energy effective. In areas with heavy smoke or dust, add filters to air intake systems to filter out airborne particulates.
Interference | Interference is a signal that corrupts or destroys regular signals. Interference affects signals used by two devices to communicate on a network. Listed below are two types of interference that affect computer networks: | 
 | Electromagnetic Interference (EMI) | EMI is interference that affects wired networking signals. EMI is caused by motors, heavy machinery, and fluorescent lights. Use shielded twisted pair cable to protect signals sent on Ethernet twisted pair cabling. If necessary, use fiber optic cables to eliminate the effects of interference.
 | Radio Frequency Interference (RFI) | RFI is interference on the radio channel used by wireless networking devices. RFI can be caused by nearby wireless devices using the same channel, cordless phones, or microwave ovens. Wireless networks that use the 2.4 GHz frequency range (801.11b and 802.11g) are susceptible to RFI. You can reduce RFI by using a wireless networking standard that operates in the 5.75 GHz range or using a different channel for wireless devices.

## Slide 14
Computer Cleaning
One of the best things you can do to keep your system running efficiently is to keep it clean. Be aware of the following facts about cleaning your computer:
Common computer cleaning supplies include:
  Lint-free cloth
  Compressed air or an air compressor
  Small anti-static vacuum
  Denatured or isopropyl alcohol
Regular cleaning gives you the chance to inspect all components. Look for worn or failed components. On electrical components, dark areas might indicate a burned-out component.
Prior to cleaning computer components, power down and unplug components and let them sit for at least 30 minutes to cool.
Use caution with liquid-based cleansers. Use small amounts and always apply cleaning solutions to cloths and cleaning instruments, never directly to component surfaces.
Dust buildup inside a computer acts as an insulator for internal components, trapping heat and preventing adequate cooling of components. Use:
  Compressed air to blow dust off.
  A non-static vacuum to remove dust.
  A natural bristle paintbrush to wipe components off.

## Slide 15
Computer Cleaning
Use a small amount of denatured alcohol on a cotton swab to clean electrical connectors (such as those on expansion cards).
For LCD screens, use a lint-free dry cloth or a small amount of isopropyl alcohol (do not use window cleaner, ammonium-based cleaners, paper towels). You can also use special monitor-cleaning solutions or pre-packaged wipes with monitor-safe solution.
For a mouse with a roller ball, clean the ball and the roller contacts on a regular basis.
For keyboards, use a vacuum or compressed air. For keys that stick, use a lint-free cloth and/or cleaning swabs, lightly dampened, to gently wipe each key.
To clean a printer, use a damp or dry cloth.
  On inkjet printers, use the printer's cleaning function to clean the print heads.
  For laser printers, use an anti-static vacuum to remove excess toner.
A regular vacuum will build up an electrostatic charge from the toner.
On removable media devices, use:
  Compressed air to blow dust and debris off of CD-ROM and DVD disc surfaces, out of drive bays, and off of drive heads.
Soft, dry lint-free cloths to wipe smudges off of CD-ROM and DVD disc media surfaces

## Slide 16: Power Conditions and Devices
Surge | Overvoltage that lasts seconds
Spike | Overvoltage that lasts milliseconds
Sag | Undervoltage that lasts milliseconds
Brownout | Undervoltage that lasts seconds (lights dim)
Blackout | Complete power failure
Surge Suppressor | A surge suppressor conditions power so that overvoltages don't reach devices.
Surge Protector | A surge protector protects against overvoltages by switching a device off before an overvoltage can damage it. A power strip provides multiple power outlets from a single plug-in, but is not necessarily a surge protector. Surge protectors can be destroyed by surges and lose their ability to protect. Consider using a surge protector with an indicator light to show whether it is working correctly.
Line Conditioner | A line conditioner modifies the power signal to remove noise and create a smooth alternating current (AC) signal.
Standby Power Supply (SPS) | A standby power supply is an offline device that switches over to provide power when an undervoltage occurs. If the switchover is not fast enough, the computer loses power.

## Slide 17: Uninterruptable Power Supply
 | An uninterruptible power supply is an online device that is constantly providing battery power to the computer and being recharged by the wall outlet. There are two types of UPS systems: An online UPS constantly powers the computer from the battery. An offline UPS powers the computer from the wall power. When the power fails, a switch inside the UPS switches to power the computer from the battery. This is the most common form of UPS. UPS size is measured by the volt-amp (VA) rating. The capacity of the UPS determines the number of devices and how long the devices can run when power is interrupted. When purchasing a UPS, purchase one with enough battery power to power only critical devices such as the computer and a single monitor. To reduce the amount of power required by the UPS, do not plug non-critical devices in to the UPS. Laser printers require more power than most UPS systems are capable of providing. For this reason, you should not connect a laser printer to a UPS. If you must provide power to a laser printer, get a dedicated UPS for that device. A UPS is designed to provide enough power to shut a system down safely during an extended power outage. Most are not intended as long-term power solutions. The UPS connects to the power source (usually a wall socket), the computer plugs into the UPS, and the UPS is connected through a serial or USB port to the computer. Software on the computer uses this connection to monitor battery life and to detect when the regular power is lost. You can configure the software to shut the system down automatically when the battery charge reaches a certain level. You usually need to configure the following settings when working with UPS software: Time to wait before sending a warning to clients Time to wait before beginning a shutdown Name of programs or commands to run during shutdown In addition to providing power when the power is lost, most UPS systems also condition the line and remove power spikes and sags. Most UPS devices sound an alarm when the AC power is lost. This alarm continues until AC power is restored, although many UPS devices have a switch to mute the alarm.

## Slide 18: Troubleshooting Steps
1. Identify the problem | When identifying the problem, resist the urge to start fixing things at this point. To identify the problem: Ask the user to describe the problem, check for error messages, or recreate the problem. Establish what has changed. Most often, problems are caused by new hardware, software, or changes to the configuration. If necessary, carefully ask users to discover what might have changed that could have caused the problem. Remember to inquire about environmental and infrastructure changes that could be relevant. Review system and application logs. Check knowledge base articles, network topology diagrams, and any other documents that may provide helpful information.
2. Back up the system | Before making changes to the system, back up user and system data (or make sure a recent backup exists). While some changes can be made without affecting user data, you should back up data to protect against unintentional data loss caused by making changes.
3. Identify possible causes and identify a theory of probable cause | Check for simple, obvious, and common problems first. For example, check power cords, connectors, and common user errors.
4. Test your theory | Test your theory to verify the cause of the problem. If your theory is not correct, examine other possible causes (return to the previous step). At this point, if the problem is caused by simple things like an unplugged system, you can safely take actions to resolve the problem. If the cause is not a simple one, identify the necessary steps to correct the problem. If you cannot identify the cause of the problem, or if the problem is beyond your ability or responsibility to fix, escalate the problem. Escalation means turning the problem over to someone more capable of handling the problem. When escalating the problem, be sure to detail the actions you took and the information you have discovered up to this point.

## Slide 19: Troubleshooting Steps
5. Create an action plan | To create an action plan, address the most likely problem and account for side effects of the proposed plan. For example, Will the fix result in significant system downtime? Is the resolution best left for other times of the day? Is there a temporary solution that should be implemented immediately? When side effects have been weighed against the fix and all concerns have been addressed, fix the problem.
6. Test the solution | When you are testing your solution, do the following: Ensure that the problem is fully resolved and that implementation did not cause any new problems. If necessary, take additional actions to prevent the problem from happening again.
7. Ensure satisfaction | After the problem is fixed, ensure the customer's satisfaction and explain what you did to fix the problem. If possible, have the user perform the task to make sure that they understand and accept that the problem has been resolved.
8. Document the solution and process | Documenting the solution and process provides you with a record of what the problem was and what you did to solve the problem. In the future, you can check your documentation to see what has changed or to help you remember the solution to common problems. It will save you time and money when troubleshooting problems.

## Slide 20: Processor Selection
CPU Manufacturer | Intel and AMD are the two major producers of processors used in modern PCs. Both Intel and AMD processors work in PC systems and support Windows software. Intel has a larger market share, while AMD processors generally cost less. Processor performance and special features vary between models and manufacturers.
Multi-Core | A multiple core processor has multiple processors within a single processor package. Dual-core, triple-core, and quad-core processors are typical in desktop systems. Multi-core systems enable the operating system to run multiple applications simultaneously. Without multiple processors, applications appear to run at the same time, but must wait their turn for processing time from the single processor. Some applications can be written to execute on multiple processors at the same time. Some motherboards use two (or more) processor sockets to provide a multiple processor solution. Multi-core processors use a single motherboard socket to support multiple processors.
Speed | Processors operate using an internal clock that is the same as, or is a multiple of, the motherboard bus speed. The speed is represented in megahertz (MHz) and is also referred to as the frequency. You can purchase processors of the same type but with different speed ratings. When selecting a processor, make sure the motherboard supports the processor speed by reading the motherboard documentation first. Most motherboards automatically detect the processor speed. If not, you might need to use jumpers or edit the CMOS to configure the processor speed.
Process Size | The process size refers to the manufacturing process used to etch transistors onto the silicon wafer that will become the CPU. A smaller process size means smaller transistors, which translates into a smaller CPU die with more transistors and less power consumption. Process size is expressed in microns (such as .25 microns) or nanometers (90 nm which equals .09 microns).

## Slide 21: Processor Selection
Cache | Cache is memory that the processor can access directly without using the system RAM. There are four types of processor cache: Level 1 (L1) cache is integrated on the processor die itself and stores instructions for the processor. On multi-core systems, each processor typically has its own L1 cache. Some processors might have two L1 caches, one for instructions and one for data. Level 2 (L2) cache is additional cache used for both instructions and data. Depending on the processor, L2 cache might be shared between two or more cores, or exclusive to a single core. Level 3 (L3) cache is additional cache beyond the level 2 cache. For multi-core systems, L3 cache is shared between all cores. Level 4 (L4) cache is shared dynamically between the on-die graphics processor unit (GPU) and CPU. Be aware of the following regarding processor cache: The size of the cache increases as you move from L1 to L4, with L1 cache being the smallest. As a general rule, a processor with more cache performs better than a processor with less cache (all other things being equal). Originally, only L1 cache was on the processor die, with L2 cache being on the motherboard between the CPU and the RAM. As processor technology has advanced, L2 cache moved to the processor die, with L3 cache being on the motherboard. Today, all three cache levels are located on the processor. The L4 cache acts an overflow cache for the L3. Information evicted from L3 is dumped into L4.
Mobile Processors | Mobile CPUs are used in mobile computers and cell phones where portability and mobility are a concern. Special versions of processors are built to minimize power consumption and the amount of heat generated.

## Slide 22: Processor Selection
Hyper-Treading | Hyper-threading is a feature of some Intel processors that allows a single processor to run threads (instructions) in parallel, as opposed to processing threads linearly. Hyper-threading enables a processor to execute two threads at the same time. For example, on a quad-core Intel system that supports hyper-threading, the processor can execute 8 threads at a time (2 on each core). Hyper-threading is not the same as multithreading. Multithreading is a feature of an application that allows it to send multiple threads at the same time. Applications are typically written to support multithreading to take advantage of multiple cores (executing threads on two or more processors at the same time) or hyper-threading features.
Overclocking | Overclocking is pushing a CPU beyond its designed specifications. Overclocking can give you a marginal increase in performance, but will decrease your CPU's life. Some Intel processors include a Turbo Boost feature. Turbo Boost, the opposite of throttling, allows the processor to dynamically run above its rated speed to improve performance. Unlocked processors are processors whose speed can be changed above their rated speed through overclocking. With overclocking, you increase the speed and often the voltage to increase the performance of the processor. Overclocking typically voids the CPU warranty and could lead to shorter component lifetimes. Some multi-core processors (such as a triple-core CPU) have additional cores that have been disabled. With the appropriate motherboard support, you might be able to unlock and use the additional core(s). However, stability of the extra cores is not guaranteed.
Integrated Memory Controller | To improve performance, some processors include the memory controller with an integrated graphics processing unit (GPU) on the processor die, resulting in faster memory access by the processor.
Cooling | Processors require some form of heat dissipation system to function properly. Without a heat dissipation system, a processor will overheat and burn out in less than a minute. CPUs use a heat sink, fan, thermal paste, liquid, or fanless cooling system to transfer heat from the CPU to the cooling unit.
Virtualization | Virtualization is the ability to install and run multiple operating systems simultaneously on a single physical machine. Virtualization typically includes the following components: a physical machine, hypervisor, virtual machine, and virtual hard disk (VHD). The virtual machines appear as self-contained and separate physical systems.

## Slide 23: Processor Socket
Processor sockets can be categorized according to how the processor makes contact with the leads in the processor socket.
Pin Grid Array (PGA): PGA processors implement a series of pins on the underside of the processor package in an array. The pins are inserted into corresponding receptacles within the processor socket on the motherboard.
Land Grid Array (LGA): The LGA socket moves the connecting pins from the processor package to the socket itself. Conducting pads are implemented on the bottom of the processor that contact the protruding pins from the processor socket.
Some commonly-implemented processor sockets include the following:
Intel:
  775: Used with the Intel Pentium 4, Celeron D, Intel Pentium 4 Extreme Edition, Pentium D, Pentium Dual-Core, Core 2 Duo, Core 2 Extreme, Core 2 Quad, Xeon, and Celeron processors.
  1155: Used with the Intel Pentium 4, Celeron, Core i3, Core i5, Core i7, Core i7 Extreme, and Xeon processors.
  1156: Used with the Intel Pentium 4, Celeron, Core i3, Core i5, Core i7, and Xeon processors.
  1366: Used with the Intel Celeron, Core i7, and Xeon processors.
  1150: Used with the Intel Celeron Dual-Core, Pentium Dual-Core, Core i3, Core i5, Core i7, Core i7 Extreme, and Xeon processors.
  2011: Used with the Intel Core i7 and Xeon processors.
AMD:
  AM3: Used with the AMD Phenom II, Athlon II, Sempron, and Opteron processors.
  AM3+: Used with the AMD Phenom II, Athlon II, Sempron, and Opteron processors.
  FM1: Used with the AMD Athlon II processor along with the A-series APUs.
  FM2: Used with the AMD A4 series, A6 series, A8 series, A10 series, Athlon X2, Athlon X4, FirePro, and Sempron processors.
  FM2+: Used with the AMD A4 series, A6 series, A8 series, A10 series, Athlon X2, and Athlon X4 processors.

## Slide 24: Sound Card File Types
WAV (Windows standard), a widely used and compatible file type
AIFF (Audio Interchange File Format), the Macintosh equivalent of the WAV
AU (UNIX standard), supported by most web browsers
MP3 (MPEG-2 Layer III), a highly effective audio compression standard
AAC (Advanced Audio Coding), also known as MPEG-2, a compression expected to replace MP3
WMA (Windows Media Audio), a highly compatible standard developed to compete with Real Audio
MIDI, not a true audio file, but contains data to reproduce sounds through electronic synthesis

## Slide 25: Configure a Sound Card
In Control Panel, use the Sound applet to:
  Configure settings for sound card connections such as speakers, audio input, and microphone.
  Identify the sources that you want to record.
  Configure sounds to play with system events or to play a sound to test your configuration.
An audio codec is a specific method of formatting sound files. Common codecs include WAV, WMV, AIFF, and MP3. To play sounds saved using these formats, your computer must have the corresponding codec installed.
  You can see the list of installed codecs in System Information.
  By default, Windows comes with common codecs installed. Other codecs might be installed as you add other software.

## Slide 26: End of Week 1 – 101B