## Slide 1: Week 3
CIS101A

## Slide 2: Wireless Networking Architecture
Devices
Network Interface Card (NIC)
Wireless Access Point (WAP) / Bridge,Router
An STA (station) is any device that can use the 802.11 protocol to communicate on a wireless network
A wireless NIC for sending and receiving signals. Act as a modulator/demodulator (modem) and transceiver (transmitter/receiver)
It receives wireless signals from several nodes and retransmits them to the rest of the network. A wireless bridge connects two wireless APs into a single network or connects your wireless AP to a wired network
Many wireless access points include ports (i.e., switches or routers) to connect the wireless network to the wired portion of the network.

## Slide 3: Connection Method
Ad-hoc: An ad hoc network works in peer-to-peer mode. The wireless NICs in each host communicate directly with one another. An ad hoc network is difficult to maintain for a large number of hosts because connections must be created between a host and every other host, and special configurations are required to reach wired networks. You will typically use an ad hoc network only to create a direct, temporary connection between two hosts.
Infrastructure: An infrastructure wireless network employs an access point that functions like a hub on an Ethernet network. With an infrastructure network, you can easily add hosts without increasing administrative efforts (scalable), and the access point can be easily connected to a wired network, allowing clients to access both wired and wireless hosts
Service Set Identifier: The SSID, also called the network name, groups wireless devices together into the same logical network. All devices on the same network must use the same SSID.

## Slide 4
Specification |  |  | Standards |  | 
 | 802.11a | 802.11b | 802.11g | 802.11n | 802.11ac
Frequency | 5Ghz | 2.4GHz | 2.4GHz | 2.4 / 5 GHz | 5Ghz
Maximum Speed | 54Mbps | 11Mbps | 54Mbps | 600Mbps | 1.3Gbps
Maximum Distance | 100 ft. | 150 ft. | 150 ft. | 300 ft. | 150 ft.
Channels (non-overlap) | 23 (12) | 11 (3) | 11 (3) | 11 (3) / 23 (12) | Depends on configuration
Modulation Technique | OFDM | DSSS, CCK, DQPSK, DBPSK | DSSS / OFDM, QPSK, BPSK | OFDM | OFDM
Compatibility | 802.11n/ac | 802.11g/n | 802.11b | 802.11a/b/g/ac | 802.11a/n
802.11n Technology is unique that it implements multi-frequency atennas. Because of this it integrates MIMO and Channel Bonding
MIMO increases bandwidth by using multiple antennas for both the transmitter and receiver. A system is described by the number of sending and receiving antennas. The 802.11n specifications allow up to four sending and four receiving antennas. The benefit of adding additional antennas declines as the number increases; going above 3x3 provides a negligible performance increase.
Channel bonding combines two, non-overlapping 20 MHz channels into a single 40 MHz channel, resulting in slightly more than double the bandwidth.
The 5 GHz range has a total of 23 channels, with 12 non-overlapping. This allows for a maximum of 6 non-overlapping bonded (combined) channels.
The 2.4 GHz range has a total of 11 channels, with 3 non-overlapping. This allows for a maximum of 1 non-overlapping bonded channel. For this reason, channel bonding is typically not practical for the 2.4 GHz range.

## Slide 5
802.11ac Technologies
Technology | Details
Multi-User MIMO (MU-MIMO) | MU-MIMO is an enhancement to MIMO that allows multiple users to use the same channel. In addition to adding MU-MIMO, 802.11ac doubled the number of MIMO radio streams from four to eight.
Channel Bonding | Channel bonding is used to combine even more channels in the 5 GHz band, allowing for up to 160 MHz wide channels.
Additional Speed Facts
Transmission speeds are affected by distance, obstructions (such as walls), and interference.
Maximum signal distance depends on several factors, including obstructions, antenna strength, and interference. For example, for communications in a typical environment (with one or two walls), the actual distance would be roughly half of the maximum.
Because transmission speeds decrease with distance, you can either achieve the maximum distance or the maximum speed, but not both

## Slide 6: Authentication Methods
Method | Description
Open | Open authentication requires that clients provide a MAC address in order to connect to the wireless network. You can use open authentication to allow any wireless client to connect to the AP. Open authentication is typically used on public networks. You can implement MAC address filtering to restrict access to the AP to only known (or allowed) MAC addresses. Because MAC addresses are easily spoofed, this provides little practical security.
Shared Key | With shared key authentication, clients and APs are configured with a shared key (called a secret or a passphrase). Only devices with the correct shared key can connect to the wireless network. All APs and all clients use the same authentication key. Shared key authentication should be used only on small, private networks. Shared key authentication is relatively insecure, as hashing methods used to protect the key can be easily broken.
802.1x | 802.1x authentication uses usernames and passwords, certificates, or devices such as smart cards to authenticate wireless clients. Originally designed for Ethernet networks, the 802.1x standards have been adapted for use in wireless networks to provide secure authentication. 802.1x authentication requires the following components: A RADIUS or TACACS+ server to centralize user account and authentication information. A centralized database for user authentication is required to allow wireless clients to roam between cells but authenticate using the same account information A PKI for issuing certificates. At a minimum, the RADIUS server must have a server certificate. To support mutual authentication, each client must also have a certificate Use 802.1x authentication on large, private networks. Users authenticate with unique usernames and passwords

## Slide 7: Wireless Security Standards
WEP: Wired Equivalent Privacy
WEP is an optional component of the 802.11 specifications that were deployed in 1997. WEP has the following weaknesses:
A static pre-shared key (PSK) is configured on the AP and the client. It cannot be dynamically changed or exchanged without administration. As a result, every host on large networks usually uses the same key.
Because key values are short and don't change, the key can be captured and easily broken.
WPA: Wi-Fi Protected Access
WPA is the implementation name for wireless security based on initial 802.11i drafts that was deployed in 2003. It was intended to be an intermediate measure to take the place of WEP while a fully secured system (802.11i) was prepared. WPA:
Uses Temporal Key Integrity Protocol (TKIP) for encryption
Supports both pre-shared key (WPA-PSK or WPA Personal) and 802.1x (WPA Enterprise) authentication
Can use dynamic keys or pre-shared keys
Can typically be implemented in WEP-capable devices through a software/firmware update
WPA2 (802.11i): Wi-Fi Protected Access 2
WPA2 is the implementation name for wireless security that adheres to the 802.11i specifications. It was deployed in 2005. It is built upon the idea of Robust Secure Networks (RSN). Like WPA, it resolves the weaknesses inherent in WEP. It is intended to eventually replace both WEP and WPA. WPA2:
Uses Advanced Encryption Standard (AES) as the encryption method
Supports both pre-shared key (WPA2-PSK or WPA2 Personal) and 802.1x (WPA2 Enterprise) authentication
Can use dynamic keys or pre-shared keys
WPA3: Wi-Fi Protected Access 3 – Adds password-based authentication and Simultaneous Authenication of Equals (SAE) to protect against guessing

## Slide 8: Additional Wireless Communication Methods
IR: Infrared
Infrared uses invisible light waves for communication. Infrared:
Is a line-of-sight medium. Objects cannot be in the path of communications.
Communicates at 9600 bps up to 4 Mbps and uses the resources of a COM port.
Works best for devices within 1 meter but can operate up to 30 meters in areas without ambient light interference.
Offers no security for transmissions.
Infrared is typically used for remote control devices or for sending data between two devices. Most smart phones have integrated IR capabilities
Bluetooth
Bluetooth uses radio waves in the 2.4 GHz frequency range for communication.
Bluetooth uses ad hoc connections between devices to create personal area networks called piconets. A piconet can have up to 7 devices, and each device can participate in multiple piconets at the same time.
By using adaptive frequency hopping (AFH), Bluetooth can automatically detect other devices in the area and avoid the frequencies used by those devices. It can switch between 79 channels to avoid interference.
A 128-bit proprietary encryption mechanism is used to encrypt signals.
NFC: Near Field Communication
NFC operates in the 13.56 MHz frequency and has a maximum transmission speed of 424 Kbps.
In order to communicate, devices must be within 2 inches of each other.
Data transmissions can be secured by using encryption algorithms.
NFC has seen widespread use in the following areas:
  Contactless payment (e.g., using a smart phone as a payment method)
  Identification (e.g., passports that contain an NFC chip)
  Video gaming
Version | Speed
1.2 | 1 Mbps
2.0 | 3 Mbps
3.0 | 24 Mbps
4.0 | 
Class | Distance
1 | 100 m
2 | 10 m
3 | 1 m
Bluetooth

## Slide 9: Configure a Small Office|Home Office
Change Default SSID: Many manufacturers use a default SSID that contains identifying information (such as device manufacturer and model number), so it is important to change the device's SSID from the default. In addition to changing the default SSID, it is also possible to disable the SSID broadcast.
Configure Wireless Protocol: Mostly involving 802.11n networks; select single band (all 2.4 or 5GHz) or mixed mode
Configure the Channel: Mostly defaults to auto. Remember that the frequencies used by channels 2–5 compete with the frequencies used by channels 1 and 6, while the frequencies used by channels 7–10 compete with the frequencies used by channels 6 and 11
Configure Encryption and Authentication: WPA2 – AES or better (WPA3) should be used. Only use WEP as a last resort
Enable MAC Filtering: Either filter traffic by allowing specific MAC Addresses or by blocking specific MAC addresses
Disbale DHCP for Wireless Clients: Allows only users with specific, vlaid static IP addresses in range to connect
Determine best AP Placement: Can affect signal strength and network access. Place access points in central locations. Radio waves are broadcast in each direction, so the access point should be located in the middle of the area that needs network access.
  Place access point to take advantage of the fact that devices often get better reception from access points that are above or below.
  In general, place access points higher up to avoid interference problems caused by going through building foundations.
  For security reasons, do not place access points near outside walls. The signal will extend outside beyond the walls. Placing the access point in the center of the building decreases the range of the signals available outside of the building.
  Do not place the access point next to sources of interference, such as other wireless transmitting devices (cordless phones or microwaves) or other sources of interference (motors or generators)
Configure Wi-Fi Protected Setup (WPS): The WPS security protocol makes it easier for WPS-enabled devices (e.g., a wireless printer) to connect to the wireless network

## Slide 10: Internet of Things (IoT)
IoT Overview: An IoT ecosystem is made of web-enabled smart devices that use embedded processors, sensors, and communication hardware to collect, send, and act on data they gather from their environments.
IoT devices share the data they gather by connecting to an IoT gateway or other edge device where data is sent to the cloud to be analyzed. In certain instances, these devices can communicate with other related devices and act on the information they get from one another. The devices do most of the work without human interaction. The only times humans would need to communicate with such devices would be to do such things as setting them up, giving them instructions, access their data, and so on. The connectivity, networking and communication protocols used with these web-enabled devices largely depend on the specific IoT applications deployed.
IoT Security: Because IoT devices are closely connected, all a hacker has to do is exploit one vulnerability to manipulate all the data, rendering it unusable.
One of the most notorious recent IoT attacks was Mirai, a botnet that infiltrated domain name server provider Dyn and took down many websites for an extended period of time in one of the biggest distributed denial-of-service (DDoS) attacks ever seen. Attackers gained access to the network by exploiting poorly secured IoT devices.
Device | Description
Thermostat | Smart thermostats learn from your habits and schedule, give you the freedom to control the climate in your home remotely
Switch | A smart switch is a device that allows you to control hardwired lights, ceiling fans, certain fireplaces, small appliances
Bulb | Smart bulbs normally work with conventional lighting fixtures and bulb holders
Plug | Smart plugs automate anything with a plug on it
Security Camera | Wireless cameras transmit video through a RF transmitter
Door Lock | A smart lock is an electromechanical lock that can be locked and unlocked using a smart phone
Speaker / Digital Assistant | Smart speakers use voice recognition software; The voice recognition service uses algorithms to familiarize itself with your way of speaking and choice of words

## Slide 11: IoT Protocols
Zigbee: Zigbee is a standards-based wireless technology that enables wireless machine-to-machine (M2M) and IoT networks. It is designed for low-data rate, low-power applications, and is an open standard. Zigbee is a specification based on IEEE 802.15.4 and the WPANs operate on 2.4 GHz, 900 MHz and 868 MHz frequencies. Its networks are secured by 128-bit symmetric encryption keys. Zigbee has a defined rate of 250 kbps, best suited for intermittent data transmissions from a sensor or input device.
Z-Wave: Z-Waves work in the following way:
Z-Wave was created by a Danish company named Zensys. It is a simpler and less expensive alternative to Zigbee. It uses the same AES-128 symmetric encryption as Zigbee. But, unlike Zigbee that operates on 2.4GHz, which is a major frequency for Wi-Fi, Z-Wave operates on the 800-900 MHz radio frequency range, so it doesn’t suffer any major interference issues like Zigbee does.
Like Zigbee, Z-Wave devices all link up together to form a mesh network. There's one central hub that connects to the internet and then the devices themselves don't have Wi-Fi at all, they use Z-Wave connectivity to talk to the hub either directly or through the mesh network. This is called a "source-routed mesh network topology." Z-Wave allows up to 232 nodes on the mesh network.

## Slide 12: Printer Types
A dot matrix printer is an impact printer that transfers characters by striking a pattern (from a matrix) through an inked ribbon and onto paper.
The most common number of pins on a dot matrix printer is 9, 18, or 24, with more pins providing a higher resolution. 24-pins create a near-letter quality print and anything with less than 24-pins provides a draft quality print. The overall print quality of a dot matrix printer is quite poor when compared to that of other types of printers.
The speed of dot matrix printers is measured in characters per second (CPS). Common speeds for a dot matrix printer are 32 to 72 CPS.
Dot matrix printers operate in either a font (letters, numbers and symbols) or dot-addressable (graphs and charts) mode.
Dot matrix printers can use either a friction feed or a tractor feed system to move paper through the printing assembly.
Because dot matrix printers strike the image onto paper, it is a good printer to use when carbon-copy documents are being printed.
The print head can become dangerously hot due to pin friction.
Can be loud because printing takes place by pins physically striking the ink ribbon, paper and the platen
Inkjet printers are quiet, non-impact printers with ink stored in a reservoir. Bubble jet printers are the most popular form of inkjet printers.
The ink reservoir is in a disposable cartridge that includes the printing mechanism.
Bubble jet printers print by heating the ink and squirting it through tiny nozzles in the print head and onto the paper.
The crispness of an inkjet printer's image is usually rated as dots per inch or dpi. Inkjets range from 150 to over 1400 dpi.
A new generation of inkjet printers produce photo-quality printouts when used with photo-quality paper.
Photo-quality inkjet printers mix up to 16 drops of ink to form a single dot of color on the page.
Inkjet printers feed single cut sheets of paper from a feed tray by clamping them between rollers and advancing them one print line at a time, from top to bottom, through the printer. The newly printed paper is then placed into a tray other than the feed tray.
Inkjet printers are an inexpensive way to produce color printouts
Dot Matrix
Inkjet

## Slide 13: Printer Types
A dye sublimation printer is a non-impact printer that uses film-embedded dye.
The print head heats and passes over the film, causing the dye to vaporize and soak into the film paper.
Dye sublimation printing prints in transitioning colors rather than pixels.
Produces photographic quality images.
Solid ink printers melt ink onto the print head (which is as wide as the paper). The head jets the melted ink onto the paper as the paper passes by on the print drum (similar to the laser printing process).
Solid ink printers offer the following advantages:
  Simple design
  Excellent print quality
  Easy set up and maintenance
The head takes as long as 15 minutes to heat prior to printing
Dye Sublimation
Solid Ink

## Slide 14: Printer Types
A thermal printer is a non-impact printer that uses heat to cause a reaction on specially treated paper.
Monochrome thermal paper is chemically treated to darken where heated (photosensitive). Many cash registers use this type of printer for creating receipts.
Color thermal paper is chemically treated to absorb color from a ribbon where heated.
Ink is applied using the ribbon in a similar manner to a solid ink printer.
The color system used by thermal printers is CMYK (cyan, magenta, yellow, and black).
The paper must make one pass for each application of a different color.
The feed assembly takes the thermal paper off the roll and it sends it through the printer to the outside of the printer.
Color thermal printers are very expensive, high quality, and operate quietly
A 3D Printer creates a physical object by taking a digital model and manufacturing the object layer by layer.
There are many different 3D printing technologies and materials that can be used depending on the object to be created.
The materials that 3D printers use to create objects are called filaments.
The most popular filaments are ABS (Acrylonitrile Butadiene Styrene) and PLA (Polylactic Acid).
3D printing can be done using many different kinds of filaments such as PVA, PET, PETT, HIPS, nylon, wood, sand stone, metal, magnetic iron, conductive PLA, carbon fiber PLA, flexible/TPE 3D printer filament, glow in the dark, and amphora 3D printer filament
Thermal
3D Printer

## Slide 15
Laser Printer Components
Laser printers use a laser and electrical charges to transfer images to paper.
Laser printers move paper through the printer via motorized rollers.
Each laser printer has a high-voltage power supply to charge the drum. This power supply converts AC current into higher voltages required for the printing process.
Each laser printer has a DC power supply to operate most of the electronic components inside the printer.
Each laser printer has a controller, which is a circuit board that acts like a motherboard in the printer. This controller board makes it possible for the printer to have and add its own memory.
Laser printers are classified as page printers, because they print text and graphics simultaneously one complete page at a time.
Laser printers use a laser to charge a metal drum. The drum picks up plastic toner, and the toner is then fused onto the paper (using rollers and heat).
Of all the types of printers discussed in this course, laser printers have the highest print quality.
A duplexing assembly is required to print two-sided output on a laser printer. Many inkjet printers also use duplexing assemblies to print two-sided paper. Duplexing assemblies are typically mounted on the back of a laser or inkjet paper.
A transfer belt is used on some high-end color laser printers. Colors are applied to the transfer belt and then to the paper. This step is repeated for different colors
Step | Description
Cleaning | The cleaning phase prepares the drum by removing the previous image printed. It uses a rubber cleaning blade to remove any excess toner on the drum and then it scrapes off the debris into a debris cavity. Next, a heat roller is lubricated to ensure that enough heat will be evenly applied to transfer the next image printed. Then an electrostatic erase lamp neutralizes the electrical charges that remain on the drum from the previous printed image.
2. Processing | The printer receives a document to be printed from the connected computer and converts it into a bitmap raster image, which is divided into horizontal raster lines
3. Charging | The primary corona prepares the photosensitive drum for writing by causing it to receive a negative electrostatic charge. Depending on the printer, the primary corona will be wires or rollers
4. Exposing | A laser beam changes the charge on the surface of the drum in a pattern of the page's image
5. Developing | The developing roller applies toner to the drum. The toner sticks to the charged areas on the drum
6. Transferring | The transfer roller charges the paper to attract the toner
7. Fusing | The fusing assembly attaches the toner to the paper using rollers that press and melt the toner to the paper. As the paper leaves the printer, a static eliminator strip removes the static charge from the paper.

## Slide 16
Connection Types
Connection Type | Deacription
USB | Most printers use a USB connection, allowing for configurations that also include scanners, external drives, or additional printers. The USB connection increases speed considerably over a standard serial or parallel port.
Wireless | Many printers allow you to connect using a wireless connection. This is especially useful when working with laptop computers. Bluetooth is a wireless technology for creating simple connections between two devices. Unlike infrared, line-of-sight connections are not required. 802.11a/b/g wireless standards use radio waves and are used to create wireless networks between multiple devices
Network | Some printers also have their own network interface card, which allows them to connect directly to a network. Network printers can also be connected to a computer that is connected to the network. Another way to connect a non-network-ready printer to a network is with a network interface device. Network printers are useful for allowing multiple people to share the same printer. This is a common way to connect printers used in a business environment

## Slide 17
Printer Considerations
Consideration | Description
Interface | IEEE1284 [legacy 25 pin], USB, Wireless, RJ45
Quality | [CPL-Dot Matrix], DPI [Inkjet / Thermal]
Speed | [PPM – Pages Per Minute]. B/W and Color have their own rating
Memory | Built in memory (more the better). Laser can be upgraded
Additional Features | Additional paper sizes Double-sided (duplex) printing Document or sheet feeders
 | Built-in scanners, copiers, or faxing capabilities Automatic collation or stapling Color printing Built-in network support
 | Built-in hard drives or memory for storing and recalling printed documents

## Slide 18
Printing Terms
Term | Definition
Print Device | The physical device connected to the print server where print output occurs.
Print Driver | The software that allows the printer to communicate with the print device
Printer | A virtual device (logical software entity) inside the print server that can be configured to send output to a print device
Print Queue | The portion of the hard drive where print jobs are stored before going to the print device
Printer Port | The means by which a print device connects to a print server (the printer's NIC)
Printer Configuration
Connect the print device to an available port.
Create a printer object. For plug-and-play printers connected to a USB port, the printer might be configured automatically.
Edit the printer object to configure device-specific settings such as color profiles and paper trays, or features such as stapling or double-sided printing.
Verify that the printer works by sending a test print.
Ensure that the customer or user knows how to use the printer and any additional features
Printing Process
An output file is created that contains commands that the printer understands. The output file is sent to a virtual printer where the print job may be configured.
A Device Driver Interface (DDI), which allows the document to interface with a printer driver, is created.
A local spooler sends the file (print job) to the print driver.
The spooler tracks the printer ports and printer configuration and assigns print queue priority to the print job.
The print job is concurrently stored on a disk file.
The printer driver creates the correct print document format.
The print job is then sent to the printer and is physically printed

## Slide 19
Printer Languages
Language | Description
Escape Codes | Used to control dot matrix printers. Escape codes are primitive compared to today's standards
Printer Command Lanuage (PCL) | Hewlett-Packard has created several versions of a printer command language called PCL. Many modern printers understand PCL
Postscript | Adobe created a printer language called PostScript that easily handles scaling of certain fonts and images. Printers that understand PostScript are usually more expensive than other printers
*PDF: Adobe created PDF as a successor to PostScript. PDF allows you to distribute documents on the web and have them displayed consistently in a wide variety of environments. Adobe has also provided Acrobat Reader free for multiple platforms and promoted PDF extensively, so it has become the de facto standard for page description languages

## Slide 20
Virtual Printing
Virtual Print Option | Description
Print to File | If you use Print to File, Windows saves the formatting and layout information of your file so a printer can create the document without the program or computer that created it
Print to PDF | Microsoft Print to PDF allows you to print your document to PDF format (Req. Acrobat)
Print to XPS | Print to XPS allows you to create .xps files using any program that you can print from in Windows (default Windows printer)
Print to Image | Print to Image allows you to print any document into an image file that is independent of the application you use to view them

## Slide 21
Network Printing Considerations
Considerations | Description
Connect the Printer to the Network | The printer must have a connection to the network (either wired or wireless). This can be done in one the following ways: Install a network interface card in the printer. Connect the printer to a workstation or server that is connected to the network. The printer is shared to make it available to other computers. Connect the printer to a special print server that has a network connection. Use Bonjour networking technology service to allow you to share a printer on your local area network. Use AirPrint to enable wireless printing capability on Apple iOS devices. Use Google Cloud Print to wirelessly send jobs from internet-connected devices to a remote printer. If the printer itself does not have a network connection, use the USB port to connect the printer to another device
Use a Print Server | The print server manages the flow of documents sent to the printer. Using a print server lets you customize when and how documents print. The print server can be any one of the following devices: An internal print server is inside the printer itself. You use special management software to connect to the print server and manage print jobs. You can configure a computer (either a server or a workstation) to perform print server functions. The computer can fill other roles on the network in addition to being the print server. Most operating systems include print server software. You can purchase an external print server. This device is used only as a print server, although many print servers can manage multiple printers
Install the Printer Drivers | Each network host that wants to use the printer must have the corresponding printer driver installed. When you share a printer in Windows, the current printer driver is automatically delivered to clients that connect to the shared printer. If the client computers run a different version of Windows, you can add the necessary printer drivers to the printer object. To add drivers for network users: Edit the printer properties and use the Advanced tab Edit the print server properties and use the Sharing tab

## Slide 22
Managing Printing in Windows
Printer Properties | Edit the properties of the printer object in order to: Print a test page Share the printer Change the driver used by the printer object Add drivers for network users Change the port used by the printer Match the colors on the screen to the colors that are printed by loading color management profiles Assign permissions to control what users can do Configure a time range during which the printer will be available Configure custom settings for the specific print device Users with the Print permission can print using the printer; users with the Manage printers permission can edit the printer properties and pause the printer, but cannot manage any documents waiting to be printed.
Print Queue | A print queue is a location on the hard disk that holds print jobs that are waiting to be processed. Each printer object has its own print queue. Double-click the printer to open the print queue. By default, users can manage their own jobs in the print queue (pause/unpause or delete). Users who have the Manage documents permission can manage all documents in the queue (pause, resume, delete, or rearrange the order). Users can only pause individual documents (or all documents) in the queue; they cannot pause the printer.
Print Server | The print server is a software process that takes print jobs from the queue and sends them to the print device. A single print server services all print queues and print devices. To edit the print server properties do the following in Windows 10: Select Start. Select Settings. Select Devices. Select Devices and Printers. Select Print Server Properties. Edit the print server properties to: Add ports and modify the port for any printer Manage print drivers used on the system, including drivers required by network users Configure printing notifications Change the drive and directory used for all print queues (spooler location) on the system

## Slide 23
Managing Printing in Windows
Print Drivers | Print drivers allow you to utilize the following configuration settings: Duplex allows you to print on both sides of a sheet of paper. Collate organizes and orders a document into separate sets. Orientation allows you to change the orientation of the paper so you can print in both portrait and landscape. Quality lets you modify the print quality of the text and images on the paper.
Print Spooling Service | Windows printing is dependent upon the Print Spooling service. The Print Spooling service is a software process that captures print jobs from applications, places them in the print queue, and then sends each print job to the print device. Use the Services snap-in to manage the Print Spooling service. By default, the Print Spooling service is configured to start automatically each time the system starts.

## Slide 24
Preventative Maintenance
Element | Recommended Maintenance
Environment | Keeping printers in a clean, safe area helps prevent premature failure. An optimal printing environment includes: Keeping the printer in an area with minimal amounts of dust or other air debris will help the printer to run smoothly and will extend the life of its mechanical components. Using surge protectors will help protect a printer from the effects of power surges and spikes. Providing proper ventilation will help a printer to not overheat. Excessive heat causes electrical components to degrade rapidly. Avoid keeping printers in closets or rooms that aren't properly ventilated
Maintenance Kits | Following the manufacturer's recommendations for the installation of maintenance kits can greatly extend a printer's life. Most maintenance kits include replacements for the most commonly used components of a printer such as: Fuser wires Rollers Toner drum If these parts are replaced on a regular basis (usually after about 20,000 pages of printing), you can avoid a great deal of common printer problems. It is important to buy the maintenance kit for your exact make and model of printer
Toner | A printer's reported toner level isn't based on how much toner is left in the cartridge, but on how many pages have been printed since the toner cartridge was installed. For this reason, it is important to check the actual toner level periodically. If the cartridge still has enough toner, but you are receiving prompts that say that toner level is low, you can reset the toner page counter by following the instructions in your owner's manual

## Slide 25
Printer Troubleshooting
Printer Doesn't Print
If a printer does not print, try the following troubleshooting techniques:
Check to make sure that the printer is turned on and is online.
Make sure that the printer is not paused.
Verify that the cable is connected on both ends and that it is the correct cable for that printer.
For network printers, make sure that the printer is configured with correct TCP/IP settings for the network.
Ensure that there is paper in the feed tray and that the tray, feed, and rollers are all in their correct positions. Verify that the correct paper tray was selected when sending the print job.
Look for a paper jam. If a jam is found, clear it and then check any feed and roller mechanisms nearby and confirm that they are clean and operating correctly.
Check the ink and toner levels.
Perform a test print from the workstation.
Open an application and try to print directly from the application.
If this does not work, access the printer properties in Devices and Printers and then click Print Test Page. This option bypasses the application. If it works, troubleshoot the printing configuration in the application.
Perform a test print from the printer console.
If successful, the problem is with the workstation or the connection to the printer.
If unsuccessful, the problem is with the printer itself.
Check the printer console or workstation for any error messages or error codes. Use the printer documentation or the manufacturer website to look up specific codes displayed on the printer.
On the workstation, verify that the Print Spooler service is started.
Check the print queue. Sometimes a large document might be first in the queue and is stalling or otherwise preventing other documents from printing. Move the document down in the queue or delete the document from the queue if necessary.
If a problem cannot be found, try restarting the printer and the computer.
Driver Issues
It is important to make sure that the following driver issues are addressed when troubleshooting printers:
Verify that the latest version of the driver for the specific make and model of the printer has been installed. If the incorrect driver is installed, this can lead to post-script text, garbled text, and other irregular activity.
Incorrectly configured network printing often leads to users installing the wrong driver on their machine. Make sure to configure your network so that users don't have to install the driver on their machine, especially without supervision.
On occasion, driver files may become corrupted. If this is the case, you should reinstall the latest version of the driver from the manufacturer's website.
Printout Quality Issues
If the printer prints, but the printout quality is poor, check the following:
Check ribbon, ink, and toner levels.
For dot matrix printers, printer images become faint when the ribbon needs to be replaced. Also, ensure that there is not too much gap between the printer head and the paper.
For inkjet printers, if pages have missing lines, use the printer's automatic cleaning feature. If this doesn't work, replace the printer cartridge. For missing or incorrect colors, verify ink levels.
For laser printers with missing lines, try shaking the toner cartridge to distribute the toner evenly. If lines are still missing, or if extra characters appear, you might need to have the printer cleaned or some internal components replaced.
For laser printers:
If faint images from previous printouts appear on subsequent pages, the fluorescent lamp and rubber scraper might not be removing remaining toner from the drum prior to starting a new print job.
A dirty primary corona wire can cause a vertical stripe down the print job because that part of the OPC drum is not being charged by the charge corona.
A dirty secondary corona wire could cause the same problem because the charge is not being applied to part of the paper.
A dirty drum or roller can create lines or splotches at regular intervals on the print job.
If toner is not sticking to the paper, check the transfer (fuser) rollers.
A faulty static eliminator strip might cause paper jams because the paper will stick to the components inside the printer.
For newer laser and inkjet printers, calibrate the printer (perform a self-test). Often the printer uses the self-test to check the printed image and make minor adjustments automatically. Calibration fixes blurry text, misalignment (jagged lines), or incorrect colors.
If the text appears garbled, make sure the proper printer driver is used. If necessary, upgrade to the latest version or reinstall the driver.
If the page prints only part way through (and the rest of the page is blank), you might need to upgrade the memory on the printer or check the print server settings.
Check the pickup rollers if paper is not being fed through the printer properly.
Use the correct paper type for the printer. Most paper will be labeled as appropriate for a specific type of printer. For example:
Using glossy paper in inkjet printers could lead to smeared ink because the ink is not being absorbed into the paper.
Using glossy paper could cause the paper to not be pulled into the rollers correctly.
Be careful when using thick paper or cardstock in a laser printer; they can cause paper jams. The weight of laser printer paper should generally be between 70 and 130 grams per square meter (GSM). On some laser printers, you can change the paper path for thick paper, so it is fed through the printer in a straight line (rather than curling the paper up to the top of the printer). Such straight-line paper paths can help prevent paper jams with thick paper.

## Slide 26
Printer Troubleshooting
Laser Printer Considerations
When working with laser printers, be aware of the following:
A laser printer's fuser operates at a high temperature and can burn you.
Because an OPC drum is sensitive to light, it can lose its effectiveness if it is over-exposed.
Do not put any materials in a laser printer that melt below 180 degrees Fahrenheit. When they pass through the fuser, they can melt and permanently damage the laser printer.
Do not attempt to print on paper with photocopied or laser printed images already on it. The images can come off onto parts of the laser printer and smear your print jobs.
To clean up toner spills, scoop up large quantities of toner or use a damp cloth to wipe up lesser quantities. Use toner vacuums that are specially designed to clean up toner spills. Never use a household vacuum to clean up a toner spill. Because toner is very fine, it is likely to pass through a household vacuum's filter and be blown into the air. Also, it can be attracted to magnets in the motor and ruin the vacuum or cause a fire
End of Printers. Mobile is Next

## Slide 27
Portable Devices
A laptop (or notebook) is a portable version of a desktop system. It often has similar hardware and runs similar software.
A Tablet PC is a notebook that includes a touchscreen to allow input by tapping the screen, dragging objects, or through handwriting recognition. A stylus is a special pen designed to be used by these touchscreens for input. Tablet PCs might run special versions of the operating system to enable touchscreen input.
A PDA (Personal Digital Assistant) is a hand-held device, typically with a small touchscreen. A PDA uses special hardware and software that provides basic productivity applications (email, word processing, spreadsheets).
A smart phone is a phone that includes functions of a PDA. As functions are added to smart phones, the line between smart phones and PDAs is disappearing.
A netbook is a notebook computer with a smaller form factor (10-11 inch screen or smaller) and custom hardware designed to maximize battery life (from 6-11 hours on a single charge). Originally, netbooks used a special operating system that often did not support all of the features of a normal desktop operating system. Increasingly, netbooks can run a regular version of the operating system, although the reduced hardware might still limit their usefulness to email, word processing, and multimedia. Netbooks typically do not have integrated CD/DVD drive

## Slide 28
Component​ | Description​
Processor​ | Processors built especially for laptop computers have lower power consumption requirements and produce less heat than desktop processors. [X86 or ARM]​
Memory​ | Laptop memory uses SODIMM and UniDIMM packages with SDRAM and DDR/DDR2/DDR3/DDR4 memory. These modules are sometimes called MicroDIMM​
Keyboard​ | Notebook keyboards are smaller than standard keyboards. Keys are often a bit smaller and closer together. Keys such as the number pad and some function keys might be left off, but are accessible by pressing a special Fn key to provide alternate functions for regular keys​
Pointing Devices​ | Instead of a mouse, notebooks use one (or more) of the following devices: ​ Pointing sticks are small knobs in the center of the keyboard. Pushing on this knob moves the cursor.​ The touchpad is located below the keyboard. Moving your finger across the pad moves the mouse. You can also tap the touchpad to click the mouse.​ Buttons below the keyboard replace mouse buttons for clicks, double-clicks, and right-clicks.​ A digitizer pad is used in laptop and PDA systems to receive input. Input is written onto the pad with a stylus pen and then those motions are transferred into data that is processed by the system​
Video​ | Be aware of the following facts about screens and video cards: ​ XGA screens have the normal 4:3 aspect ratio. WXGA screens use a widescreen aspect ratio.​ Some screens promise brighter display for crisper viewing or better viewing outdoors.​ The video controller is either integrated onto the motherboard or it might be a separate board that can be replaced.​ Video memory typically shares a portion of the system memory, although some notebooks have dedicated video memory.​ Most notebooks have an external video port that you can use to display the screen on a projector or a monitor​
Networking​ | Most notebooks include built-in networking devices such as an Ethernet port, a modem port, wireless, Bluetooth, and/or infrared. Wireless networking capabilities are often provided by a small card that plugs into an internal mini-PCI slot (located under the keyboard or accessible through the back). The wireless antennae might be a wire that extends around the screen​
Internal hard Drives​ | Internal hard disks are typically 2.5" or 3.5" and very thin compared to desktop hard disks. SATA, solid state drives, and Flash drives are used in portable devices​
Laptop Components

## Slide 29
Common Fn Laptop Keys
Dual displays
Wireless (on/off)
Cellular (on/off)
Bluetooth (on/off)
GPS (on/off)
Airplane mode
Touchpad (on/off)
Screen orientation
Screen brightness (increase/decrease)
Keyboard backlight (increase/decrease)
Volume settings (up/down/mute)
Media controls
Repair and Upgrade Considerations
When upgrading or repairing laptop components, keep in mind the following considerations:
To identify the source of problems on a notebook, plug in a known good external component. For example:
If the keyboard doesn't work, plug a keyboard into the USB or PS/2 slot.
If the video display doesn't work, connect an external monitor.
If the external device works but the internal device doesn't, then replace the internal device if the component is removable.
Some notebook components are built into the motherboard and cannot be replaced without replacing the entire motherboard. In those cases, add a similar component using an external bus type (such as PC Card/PCMCIA, ExpressCard, or USB).
An alternative to replacing failed components (because of cost) is to add external components. For example, you can use your notebook as a desktop computer by connecting an external monitor.
Notebooks vary considerably in design and composition. Consult the documentation to find the location of screws and to identify installation sequences for accessing system components.
Notebook parts are not as standardized as other PC components. In many cases, you will need to order from the manufacturer to get the correct part.
Components with a high degree of standardization include the processor, memory, and internal hard drives.
Before servicing a portable device, unplug it and remove any batteries.
Plastic case components are sometimes screwed into place and sometimes snapped into place. For pieces of the case that snap into place, use a plastic tool to carefully pry the piece off

## Slide 30
Laptop Considerations
Device | Consideration
Hard Drive | Internal hard drives are usually 2.5" or 3.5" in size. Verify the interface type (SATA), speed, capacity, and RPM speed supported by the notebook before purchasing a replacement drive. Most hard drives are replaced by removing a cover on the bottom or side of the computer. Some disk drives are placed inside a caddy with a special connector. You will need this caddy when replacing the drive
Memory | Most notebooks use a small panel on the bottom to access the additional memory slots. (Can also be installed on MB)
Keyboard | When experiencing problems with the keyboard: Cleaning the keyboard might correct stuck keys or keys that will not display a character when typed. If numbers type instead of letters (such as 1 for J, 2 for K, etc.), make sure that the Num Lock is turned off
Touchpad | The touchpad takes the place of a mouse. The most common problem for the touchpad is that the mouse cursor is not controlled properly based on where you press. In this case, recalibrate the touchpad. Some notebooks recalibrate the touchpad at every system boot. Reboot the computer, making sure not to press the touchpad during startup. Most notebooks include a utility for calibrating the touchpad. Run the utility and follow the instructions to recalibrate.
Wireless Network Card | Wireless network cards might be integrated onto the motherboard, or added through add-on cards. Mini-PCI or mini-PCIe slots are used to add devices such as a wireless card Wireless cards require an antenna. Connectors on the card connect to the antenna, which is usually a wire routed into the lid and around the display.
Processor | Remove the keyboard to expose the processor. Some notebooks have processors soldered onto the motherboard. On these systems, you will not be able to upgrade or replace the processor
LCD Display | The bezel is the case in which the LCD is set. The backlight illuminates the LCD by evenly dispersing light over the entire screen. These backlights are usually cold cathode fluorescent lamps (CCFL) or LEDs.

## Slide 31
Laptop Power
Laptop systems are designed to use as little power as possible. Common ways laptops save power are:
Turning off any drives that aren't currently being used.
Stepping down the bus speed in the CPU.
Turning off the monitor after a period of inactivity.
Putting the computer to sleep or turning it off automatically.
When your laptop is plugged into the wall, it receives power through an adapter that converts the AC power from the outlet to DC power usable by the computer. Most adapters can be used on both 110 and 220 AC volt power sources. The energy received through the adapter is divided between running the laptop system and charging the battery.
Remember that most adapters are not interchangeable between laptops because laptops require varying amounts of voltage and amperage and also have different plugs. Before connecting a laptop to an adapter, look at the information listed on the adapter to make sure that it supplies the correct amount of voltage and amperage necessary for your specific laptop and has a plug that will fit properly. Failing to use the correct adapter can cause a laptop to:
Receive insufficient power to turn on.
Receive insufficient power to charge the battery.
Receive an excess of power that will fry the system
Laptop Batteries
Battery | Characteristics
Nickel Cadium (NiCAD) | Develops a memory and begins to store less power as it is repeatedly recharged. To avoid battery memory problems, completely drain the battery before recharging it. Takes up more physical space than lithium ion batteries. Very heat sensitive. No longer used on new laptops
Mickel Metal Hydride (NiMH) | Does not develop a memory. 40% longer lifetime than nickel cadmium. Greater charge capacity than nickel cadmium. Less toxic than nickel cadmium. Slightly more expensive than nickel cadmium
Lithium Ion / Polymer (Li – ion) | Does not develop a memory A rechargeable battery with twice the capacity of a nickel cadmium battery with significantly increased stability and safety. Takes up less physical space and weighs less than nickel cadmium or nickel metal hydride batteries for comparable power output. Has a shorter lifespan than nickel metal hydride. Not heat sensitive like nickel cadmium. Cannot be overcharged. More expensive than nickel cadmium or nickel metal hydride
Fuel Cells | A growing technology that is still developing and is being implemented into the small electronic device market. Not truly a battery. Offers instant power and uses replaceable cartridges.

## Slide 32
ACPI: Advanced Configuration and Power Interface
ACPI is also known as Instant Available and Always On. Is often mistakenly referred to as APM (an older standard).
The operating system, BIOS, and devices interact to manage power.
Users can configure settings that identify events and power consumption characteristics. For example, you can configure the display to turn off after 5 minutes of inactivity.
The system can monitor the battery and other device states and dynamically change power consumption on one or more devices.
ACPI supports Plug and Play
Power States
Power State | Characteristic
Working | The whole system is usable. Unused save power in a low power state
Sleep (Modern Standby) | Able to switch from a low-power state to a high-power state quickly
Sleep | The system appears to be off. Volatile memory is refreshed. Some components are powered so the computer can wake from keyboard, LAN, or USB input
Hibernate | The system appears to be off. Power consumption is at the lowest level. Volatile memory is saved to a hibernation file to preserve the system state. Some components are powered so the computer can wake from keyboard, LAN, or USB input
Soft Off | The system appears to be off. This state is comprised of a full shutdown and boot cycle
Mechanical Off | The system is completely off and consumes no power. The system returns to a working state only after a full reboot

## Slide 33
Power Schemes / Settings
Each power scheme controls power down settings for the monitor, hard drives, and the entire system, and has settings for when running on AC power or on battery power.
You can modify the existing schemes or create new ones to meet your needs through the Power Options utility in the Control Panel. In Windows 10, you can edit power schemes by right-clicking the desktop and selecting Display Settings > Power & Sleep.
The preconfigured power schemes available depend on the operating system version and the computer type (laptop or desktop). Some manufacturers also include preconfigured power schemes. Default power schemes are often included to maximize performance or power savings.
Power schemes work for both laptop and desktop systems.
Edit the power scheme to control what the device does when you press the power button, shut down the system, or close the laptop lid.
In Windows, sleep corresponds to the suspend ACPI state. With hybrid sleep, data in memory is retained as well as written to the hard disk. If the computer is turned off while in hybrid sleep, it can be resumed using the data stored on disk
Power management must be supported by the BIOS, devices, and the operating system.
In Windows, hibernation must be enabled before you can select Hibernate as an option for shutting down the system or in a power scheme.
The BIOS must have ACPI support enabled before you can enable hibernation in Windows. If the Hibernate tab is missing, check the BIOS. If the BIOS does not have a setting for ACPI, you might need to upgrade the BIOS.
By default, Windows is allowed to control power to all devices that support the feature. You can edit the device properties in Device Manager to prevent Windows from controlling the device.
The Wake on LAN (WoL) feature allows a device that receives a special network signal to wake the computer from a sleeping or hibernated state. WoL is often used by desktop administrators to remotely start up computers for management purposes.
By default, devices are not allowed to wake the computer, although they might support this feature.
Edit the device properties in Device Manager to allow a device to wake the computer.
WoL is not recommended for laptop computers, as the computer will periodically come out of standby to check its network state which runs down the battery
Most laptop manufacturers provide service manuals on their websites that you can use to learn specific disassembly/reassembly procedures for a particular laptop make and model.
The components used in laptop systems are much smaller than those used in desktop system. You should carefully organize and label each part as you remove it from the system to ensure that it doesn't get lost and that it gets reinstalled in the correct location.
Keep devices away from food and drink. Liquid spills are especially damaging to a portable device. Liquid can easily run beneath the keyboard and onto internal components.
For individual keys that stick, you might be able to remove the key and clean underneath it. If that does not work, you will need to replace the keyboard.
Clean the display with lint-free cloth and isopropyl alcohol. Spray the cleaner on the cloth, not directly on the screen, to avoid getting cleaner on other components.
Cooling is a major concern for portable devices. Follow these recommendations:
Keep all air vents clear and unobstructed. Vents are typically located on the back of the unit.
To help heat dissipation, do not place a laptop on a surface where air cannot circulate beneath it evenly The best way to keep a laptop properly ventilated is to purchase special laptop cooling bases that provide fans for the bottom of the unit. If a laptop cooling base is not available, set it on top of a hard, solid surface, such as a desk or countertop. Soft surfaces, such as a couch or your lap, should be avoided because it is likely they will obstruct even air flow.
Adjust processor throttling (if supported) and configure Power Options to reduce power consumption. Lower power consumption not only saves battery life, it lowers the heat output.
When moving from outside to inside, allow the computer to warm up before using it. One of the main reasons is to prevent water vapor condensation that can occur when the system is powered on and warms up quickly.
Do not leave portable devices in cars where the temperature can reach extremes or where direct sunlight can be magnified.
Although they are built to withstand portability, protect portable devices in properly-padded cases or include proper packaging materials when shipping them.
When installed, both PCMCIA and ExpressCard cards extend past the outer edge of the laptop. You should remove the cards from the slots before putting them in a case to prevent them from catching on objects and breaking

## Slide 34: Troubleshooting Laptops
Power
Video
Applications
Components
Laptops can run from either AC power through the transformer or from battery power..
If your laptop has no display at all..
If you cannot load an app from the Microsoft Store, use the Windows Store Apps Troubleshooter to search for and correct problems
The most common portable components used with laptop systems are keyboards, mice, digitizer pads, and antennae..
Due to the custom layout and form factor of most laptops, it is best to consult the manufacturer website/forum or consult the documentation that came with the laptop. Most problems cannot be "fixed" directly, just replaced with alternatives.

## Slide 35
Common Mobile Devices
Device | Description
Tablets | Tablet devices use a touchscreen interface instead of the touchpad and keyboard used by notebook PC
Smart Phones | Smart phones combine the functionality of a cellular phone with the features of a desktop computer
Wearable Devices | Wearable devices are a type of mobile device meant to be worn somewhere on the body
Webcam | Webcams are camera and microphone systems that allow users to communicate through the internet with audio and video
E-Readers | E-readers are similar in size to tablets, but they lack the functionality of a tablet

## Slide 36
Key Features Mobile Devices
An accelerometer is also called a g-sensor. It detects a tablet's physical movements by measuring its linear acceleration in one dimension. The user interface can be automatically rotated to portrait or landscape mode, depending on the unit's orientation
Applications must be written to run on mobile devices based on the operating system and system architecture. App distribution is provided online by platform
Two computer architectures are used by mobile devices:
x86: The x86 architecture is compatible with standard x86 PC hardware and software, which allows the device to run operating systems such as Windows. Some newer versions of Android can also run on the x86 architecture.
ARM: Some tablets, such as the iPad, use the ARM architecture. ARM is more power-efficient and less expensive to manufacture than x86. Android runs primarily on ARM
An emergency notification system is a method of facilitating one-way message broadcasts to one or many groups of people, alerting them to a pending or existing emergency
Geotracking is the ability to identify a person's current physical location by obtaining GPS data from their smart phones or other GPS-enabled devices
GPS is a space-based navigation system that provides location and time information in all weather conditions anywhere on or near the Earth where there is an unobstructed line of sight to four or more GPS satellites
A gyroscope measures the vertical and horizontal orientation of the device. This essentially creates a user input mechanism
IMEI stands for International Mobile Equipment Identity. It is a unique number given to every single mobile phone. It is typically located behind the battery. IMEI numbers of cellular phones connected to a GSM network are stored in the Equipment Identity Register database containing all valid mobile phone equipment. When a phone is reported stolen or is not type approved, the number is marked invalid.
IMSI stands for International Mobile Subscriber Identity. This is a unique identifier that defines a subscriber in the wireless world, including the country and mobile network to which the subscriber belongs. The IMSI is one of the pieces of information stored on a SIM card
Mobile payment services operated under financial regulation and are performed using a mobile device. Instead of paying with cash, check, or credit cards, a consumer can use a mobile phone to pay for a wide range of services and digital or hard goods
Mobile devices implement 802.11b/g/n networking to provide networking connectivity. Bluetooth is also commonly implemented for connecting peripherals in place of wired USB connections
Three operating systems are commonly used with mobile devices:
Android (open source)
iOS (closed source/vendor specific)
Windows (closed source/vendor specific)
A software development kit (SDK) is a set of software development tools that allow the creation of applications for a certain software package, software framework, hardware platform, computer system, video game console, operating system, or similar development platform. To create applications, you have to download a specific software development kit. For example, the development of an Android app requires an SDK with Java, for iOS apps an iOS SDK with Swift, and for MS Windows the .NET Framework SDK with .NET. Android application package (APK) is the package file format the Android OS uses to distribute and install mobile apps and middleware
A virtual assistant is a program that understands your conversation, replies to you, and carries out many daily tasks for you like sending mail, making a search, opening apps, reporting the news and weather, and more. You can initiate these tasks using your voice. Some examples of a virtual assistant include AIVIC, Skyvi, and iris
Wi-Fi calling allows your iPhone to place and receive phone calls and text messages over a Wi-Fi network. If you have a weak cellular signal but a solid Wi-Fi signal, your iPhone will automatically switch over and route calls and texts using Wi-Fi. You can only use this if your cellular carrier supports it.

## Slide 37
Connection Types - Mobile
Cellular networks used for voice and data include the following types:
2G (second generation) networks were the first to offer digital data services. 2G data speeds are slow (14.4 Kbps) and are used mainly for text messaging, not internet connectivity. 2.5G supports speeds up to 144 Kbps.
EDGE (also called 2.75G) networks are an intermediary, between 2G and 3G networks. EDGE is the first cellular technology to be truly internet-compatible, with speeds of 400–1,000 Kbps.
3G offers simultaneous voice and data. Minimum speeds for stationary users are quoted at 2 Mbps or higher. The following extensions enhance 3G networks:
HSPA+ (also known as smart antenna) uses multiple-input and multiple-output (MIMO). It significantly increases data throughput and link range without additional bandwidth or increased transmit power.
Long Term Evolution (LTE) and LTE-Advanced increase downlink/uplink speeds to 100/50 Mbps and 1Gbps/500Mbps, respectively.
4G is available with minimum speeds around 3–8 Mbps, with over 100 Mbps possible. 4G:
Uses MIMO.
Is not compatible with 3G; 4G requires a complete retrofit on the part of service providers and new equipment for the consumer.
Utilizes Worldwide Interoperability for Microwave Access (WiMAX). WiMAX delivers high-speed internet service (up to 1 Gbps for stationary users) to large geographical areas.
5G is able to achieve speeds twenty times faster that 4G; its peak speed is 20Gb per second.
Uses MIMO.
Includes lower frequencies than previous generations, down to 600 MHz.
Uses Long-Term Evolution (LTE) for wireless connections
A hotspot is a physical location where you can obtain wireless internet access using a wireless local area network (WLAN) with a router connected to an internet service provider.
Tethering is connecting one device to another. In the context of mobile phones and tablet computers, tethering allows sharing the internet connection of the phone or tablet with other devices like laptops. Connection of the phone or tablet with other devices can be done over wireless LAN (Wi-Fi), over Bluetooth, or by physical connection using a cable like USB
Airplane mode is a setting available on many smart phones, portable computers, and other electronic devices that suspends the device's radio-frequency signal transmitting functions, which disables telephone, Wi-Fi, and Bluetooth when activated
A mobile virtual private network (mobile VPN) provides mobile devices with access to network resources and software applications on their home network when they connect using other wireless or wired networks
Bluetooth is a wireless technology standard for exchanging data over short distances from fixed and mobile devices and for building personal area networks (PANs). It can connect several devices, overcoming problems of synchronization
An NFC connector is used to emulate cryptographic smart card functionalities for RFID tags or memory cards
A mini-USB connector is a small USB cable connector that is often used by handheld electronic devices like mobile phones, MP3 players, and digital cameras. On mobile phones it is often used for both USB data connectivity and charging. The new connector, called micro-USB, is smaller than the mini-USB connector and allows for even thinner device designs
Lightning is a proprietary computer bus and power connector created by Apple Inc. to replace its previous proprietary 30-pin dock connector. It is used to connect Apple mobile devices like iPhones, iPads and iPods to host computers, external monitors, cameras, USB battery chargers, and other peripherals
An infrared port is a port on a mobile device that enables devices to exchange data without using cables

## Slide 38: Troubleshooting Tools: Mobile
App Scanner
Wi-Fi Analyzer
Cell Tower Analyzer
An app scanner is a tool that can be used to identify problems with installed apps.
When installed, the app scans all installed apps on the mobile device and uses a definitions list to identify any issues.
App scanners can be configured to automatically scan the mobile device on a specified schedule
2. Wi-Fi analyzers are special apps that can be used to troubleshoot Wi-Fi connectivity issues. Most Wi-Fi analyzer apps provide the following functionality:
Identify the number of APs that are broadcasting
Display the signal strength and channel of each wireless network
Obtain wireless network information
3. A cell tower analyzer can be used to troubleshoot cellular network connectivity by displaying the following information:
Signal strength/interference
Number of cell towers in the area
The location of each cell tower
Mobile network information

## Slide 39: Common Mobile Problems
Display Issue - A mobile device's display can stop working for a several reasons:
Make sure the device is fully charged and powered on. It is possible that the device is powered off or the battery is drained.
Check the device's brightness level. If the brightness level is too low, it may appear as though the display is off. Look at the screen in a dark room to make sure this isn't the case
Mobile devices use capacitive touchscreens, which require a conductive material touching the screen to work:
Look for liquid on the screen. Because water is conductive, any type of moisture on the screen will result in erratic touchscreen behavior.
Check for cracks or physical damage. A cracked screen can disrupt the current flow across the screen and cause specific sections of the touchscreen to fail.
Make sure the screen is calibrated. If the touchscreen is inaccurate, try calibrating it using the device's built-in calibration app
Mobile devices are vulnerable to many of the same attacks that target desktop systems. One such attack is unauthorized access:
Unauthorized account access occurs when an attacker obtains the login credentials for a cloud backup service or the device itself
Unauthorized root access is typically the result of a virus or malicious program installed on the mobile device
Most connectivity issues are a result of a weak signal or some sort of interference.
If the device is having problems connecting to a wireless network:
  Make sure the wireless adapter is turned on.
  Verify that the wireless configuration settings are correct.
  Use a Wi-Fi analyzer to identify the network's signal strength as well as interference sources (e.g., other network signals).
  Verify that you are not over your data limit and being denied data access.
If the device is having problems with cellular service:
  Make sure the mobile device has a SIM card installed.
Use a cell tower analyzer to identify network coverage, signal strength, and network type (i.e., 1x, 3G, 4G)
If the device seems to be running slow, there are a couple things you can look at in order to identify the problem.
Identify system resources and usage. Many mobile devices have a system monitor that can be used to identify which apps are using system resources (i.e., memory, processor, etc.).
Make sure the app being used is compatible with the mobile device. Older mobile devices have slower processors and might not be able to run all the latest mobile apps available to it.
Check the amount of free storage on the mobile device. If a mobile device's storage is more than 80% full, performance can be reduced considerably.
If the cell phone overheats, turn it off and place it in a cool place out of direct sunlight. It is possible for overheating to damage hardware, but generally, cooling down will correct issues. Avoid overheating by keeping the phone out of direct sunlight and extremely hot places, such as a car parked in direct sunlight

## Slide 40: End of Week 3